## Slide 1: ADnED Handling V4 Neutron Event Data
Matt Pearson
SNS ORNL
18th-22nd May 2015

## Slide 2: Neutron Events
N
Neutrons
He3
Detector
Multiple
Drift
Tubes
Read
Out
Card
Read
Out
Card
Read
Out
Card
DSP
Timing System
Bunched
in pulses
at 60Hz
Optical Reciver
nED framework
DSP
Nexus
File
ADARA
V4
V4
Clients
nED is a driver for the various types of readout cards, and a framework for dealing with neutron events.
ADARA is a custom protocol for streaming events to disk.
nED produces a V4 channel for online visualization.
Events are composed of
(pixel ID, time of flight) pairs.
8 bytes for one event.

## Slide 3: Neutron Events (2) – using pvData
N
structure
time_t timeStamp
NTScalar proton_charge
double value
// Time-of-Flight values for N neutron events
NTScalarArray time_of_flight
uint[] value
// Pixel IDs for N neutron events
NTScalarArray pixel
uint[] value
[mkp@bl99-dassrv1 ~]$ pvget neutrons
neutrons
structure
time_t timeStamp 2015-04-28T09:34:51.844 35
epics:nt/NTScalar:1.0 proton_charge
double value 6e+08
epics:nt/NTScalarArray:1.0 time_of_flight
uint[] value [63755,94783,45297,83246,74134,86331,85143,60222,84875,73684]
epics:nt/NTScalarArray:1.0 pixel
uint[] value [946,2093,735,2358,938,2858,453,2843,869,2647]
Example ‘pvget’:

## Slide 4: ADnED Requirements
Integrate event data for X/Y plot (also means mapping pixels to 2-D X/Y plot)
Integrate TOF data for 1-D spectrum
Calculate multiple ROI for all plots
Filter events going into TOF spectrum based on a X/Y ROI
Filter events going into X/Y plot based on a TOF ROI
Monitor multiple V4 channels (each nED instance is one V4 channel)
Handle data from N detectors in one channel, or spread between channels.
Support put_callback on a start acquisition for high level software
Adjustable binning on TOF spectrum
Calculate d-space, energy transfer, etc, based on pixel ID and TOF.
Detect error conditions (missing packets, bad timestamps).
Pause acquisition without resetting data
Performance requirements:
Handle up to approx 10M events/s (80MB/s). Our highest data rate
beamline is 5-6M events/s. So 1 gigabit networking is enough.
Update plots at ~1Hz.
Update scalar values at ~10Hz (to support short acquisitions).
Prior to developing ADnED we tested V4 performance.
Works up to 100M events/s. See Kay Kasemir’s talk at last EPICS meeting.

## Slide 5: ADnED used areaDetector framework
A lot of the functionality is free (waveform, ROIs, Statistics, binning, etc).
What we developed:
ADnED driver:
  Monitors V4 channels
  Applies filters based on ROIs
  Performs pixel mapping
  Integrates events based on detector pixel ID ranges
  Start/Stop acquire
  Produces 1-D NDArray objects for N detectors
NDPluginROIStat:
  New areaDetector plugin to perform simple statistics on N ROIs
  (released in ADCore 2-2)
ADnEDPixelROI:
  Custom ROI plugin to convert 1-D NDArray to 2-D NDArray
ADnEDTransform:
  Library of calculations for d-space, etc.
OPIs, Python tests (PyEpics).

## Slide 6
nED
ADnED
ADnEDTransform
Event
Handler
V4
Frame
Handler
X/Y
ROI
1-D to 2-D
TOF
ROI
2-D
NDArray
X/Y
Stat
X/Y
ROIStat
X/Y
Array
1-D
NDArray
1-D
NDArray
TOF
ROIStat
TOF
Array
8 ROIs+Stats (min, max, total counts)
ROI 1 also used for filtering X/Y pixel data
1-D TOF Array
8 ROIs+Stats (min, max, total counts)
ROI 0 used for OPI autoscaling
ROI 1 also used for filtering TOF data
2-D XY Array
Profile Arrays
Event Handler:
Consume events from multiple nEDs
Filter events based on XY ROI or TOF ROI
Apply pixel mapping (logical ID to X/Y space)
Frame correction on TOF
Convert TOF to d-space, delta-E, etc.
Sort events into detectors.
Plugin chain is repeated for each detector.
Frame handler creates NDArray objects at a slow rate (eg. 10 Hz)
1-D
NDArray
Buffer
Det1
Det2
DetN
nED
ADnEDPixelROI

## Slide 7: ADnED Top Level Screen

## Slide 8: ADnED XY Plot
Intensity widget + some rules

## Slide 9: ADnED Time of Flight Spectrum (TOF)

## Slide 10: ADnED User Friendly Screen

## Slide 11: ADnEDTransform
Base class defines interface & some common code:
virtual epicsFloat64 calculate(epicsUInt32 type, epicsUInt32 pixelID, epicsUInt32 tof) const = 0;
Concrete class defines calculation based on pixel ID and TOF.
Change calculation and/or input arguments at runtime.
For example, on our VISION beamline we calculate energy transfer from
the inelastic detector:

## Slide 12: ΔE and TOF spectrum on VISION
Plots update at 1Hz
ΔE calculation has to keep up with event rate (in this case it’s only ~10K e/s)

## Slide 13: ADnED So Far
Deployed on two beamlines (3rd one at end of May).
Install on beamlines as we convert them to EPICS.
More custom OPI screens for new beamlines.
May require more detector diagnostics (or in a new application)
ADnED:
https://github.com/areaDetector/ADnED
Simulation event server:
https://github.com/kasemir/EPICSV4Sandbox
ADnED Dependencies are: base, asyn, ADCore, V4 (pvAccess, etc).
IOC application will also require: calc, busy, sscan, autosave