## Slide 1: Time Source Callback and Attribute Plugin for areaDetector
Garth Brown, Kukhee Kim for Camera Team

## Slide 2: Abstract
Timestamp tagging to data and aligning data to individual beam pulse are important part of data acquisition system for pulse machine. We have utilized Beam Synchronous Acquisition (BSA) for LCLS, FACET and other accelerator facilities in SLAC. BSA provides a common interface for the timestamp tagging and aligning data to beam pulse. Unfortunately, we could not get benefit from the BSA for camera image data due to the image is an array data and it should be stored as image file format. BSA only supports scalar type epics PV. Our timing system in SLAC has 360Hz granularity. Most of image processing and acquiring cycles are non-deterministic in time domain and spend longer time than the 360Hz timestamp update period. These bring difficulty of timestamp tagging for image data.
We have discussed with Mark Rivers, author for the areaDetector module, about time source callback to implement the driver level timestamp tagging with user defined function. The driver level timestamp tagging gives more deterministic and real-time behavior. The timestamp is stored as a part of meta-data of the image and can be utilized by downstream plugins such as file plugin which saves the timestamp into image file format. We also discussed to extend attribute plugin to post out the timestamp related data to epics PVs. He reflected our requirements for the time source callback in the latest areaDetector module and the attribute plugin also.
We are going to describe the details about the time source callback and attribute plugin.

## Slide 3: Contents
areaDetector
Time Stamping issues for camera image data
Improvement of recent areaDetector
  Time Source callback
  User Attributes
  Attributes Plugin
Conclusion

## Slide 4: areaDetector module
A software module to provide general interface for Image Data/Camera in EPICS
  Not only for Image data, but also for any kind of array
Witten in C++, work with Asyn
Camera Hardware
Vendor API
Driver
NDArray and other classes
File Plug-In’s
Asyn
Asyn Port
ADBase template
NDPluginBase
template
Other PVs
(1) EPICS Channel Access
MPEG plug-in
HTTP server
EPICS PV
Software Code
Hardware
areaDetector module
(2) Streaming
(3) File output TIFF, netCDF, JPEG, …

## Slide 5: Timestamp Tagging Issue for Image Data
Image data type (waveform) is not fit for Beam Synchronous Acquisition (BSA) system
Image acquiring and data processing is not deterministic to fit with 360Hz granularity timing system
Timestamp/pulse id information should be embedded into a part of image data (meta data in image file)

## Slide 6: Timeline for the Timestamp Issue
time
Active timeslots (120Hz)
Events for Camera
Events for Camera
Fail Scenario
Take Picture
areaDetector Driver Processing
Asyn
Record Processing
Uncertain Delay by Callback Processing
RT Violation for timestamp update
Take Picture
areaDetector Driver Processing
Asyn
Record Processing
Uncertain Delay by Callback Processing
Temporal Solution
Dummy Record Processing
Update timestamp and sustain it until next event comes out
Timestamp is valid in this period
Get timestamp from Dummy Record via TSEL field
Timeslots (360Hz)
8.3 msec
2.8 msec

## Slide 7: Improvement of areaDetector
Purpose/Goals:
Need to get the Timestamp which includes pulseID supported natively by the areaDetector Package. This needs to be done in such a way that the accelerator community can use this new feature in a generic way. Each facility may different ways in which they supporting timing.
Closely worked with Mark Rivers and Mark provided improvements for areaDetector
  Provide hooks to get EPICS timestamp
    areaDetector already had its own timestamp, double type
    SLAC pulseID embedded timestamp could not fit into the double type timestamp
  Provide a callback mechanism to update the epics timestamp which can deliver the SLAC pulseID embedded timestamp into the areaDetector
  Provide a callback mechanism for a user attribute in the Plug-In’s
    To avoid software change when new attribute is added and new data processing is required for the new attribute
    Add up epics timestamp (sec, nano-sec) into the virtual attributes in Attribute Plugin to post out to PVs (time series PVs)

## Slide 8: Improvement Details of PV time stamping
Changes on Asyn/areaDector
  Changes on asynManager and asynPortDriver to support passing timestamps from the driver to device support, and device support to the record.
  Changes on areaDetector
    Add up new timestamp field in NDArray data structure
      Originally, it supports “double” type timestamp NOT epicsTimestamp
      Now, it has new timestamp field which support the epicsTimestamp
    The drive sets the new epicsTimestamp field in the NDArray when the image arrives. Then sets all record timestamps for input record in the driver and plugins to be that timestamp from the NDArray.
  Asyn provides a method to register a user-defined timesstamp callback – TimestampSource, this function will be called by areadDetector right after the image arrives, and updates the epicsTimestamp field in the NDArray
  If user did not register the timestamp source, there is a default timestamp source which updates the epicsTimestamp field with the Current Time Provider (should be NTP which is chosen by the generaltime facility in EPICS BASE).
  Note: TSE=-2 is required for record processing to get areaDetector’s “epicsTimestamp field” into an EPICS record’s timestamp.

## Slide 9: Time Sources and Time Stamping in the improvements
Current Time Provider
Event Provider
NDArray data structure
DOUBLE type timestamp
epicsTimeStamp
always
Default TimeSource function
When no registration
for user-defined function
User-defined TimeSource function
Record
epicsTimeStamp
Asyn device pushes the epicsTimestamp field to record.
It will affect only the record has TSE=-2.
Otherwise, the record support override its timestamp.
File Plug-In (TIFF, netCDF) saves both epics timestamp, and double timestamp.
Timestamp logic in record support
File Plug-In
TIFF
netCDF

## Slide 10: Timeline for the time source callback
time
Active timeslots (120Hz)
Events for Camera
Events for Camera
Take Picture
areaDetector Driver Processing
Asyn
Record Processing
Uncertain Delay by Callback Processing
RT Violation for timestamp update, but it does not matter. the timestamp has been updated by device support.
Timeslots (360Hz)
8.3 msec
2.8 msec
User-defined Time Source function updates epicsTimestamp in the NDArray
Asyn device support pushes the epicsTimestamp to the record

## Slide 11: Simple Example for using Time Source Callback
Build Application with Mark Rivers’ latest areaDetector and Asyn modules
Set up TSE=-2 for the Image Waveform Record
Add the following into “st.cmd” to register the “user-defined timestamp source”
Prepare “C” code for the user-defined timestamp source
Add following into DBD file to so we can call this timestamp source function from iocsh()
asynRegisterTimeStampSource("PORT1", "myTimeStampSource")
#include <epicsTime.h>
#include <registryFunction.h>
#include <epicsExport.h>
#include "evrTime.h"
static void myTimeStampSource(void *userPvt, epicsTimeStamp *pTimeStamp)
{
evrTimeGet(pTimeStamp, 0)
}
epicsRegisterFunction(myTimeStampSource);
function("myTimeStampSource")
In real implementation, the event number is configurable by PV,
to bind the timestamp to a specific event

## Slide 12: Simple Test Example for TIFF file plugin
65002 (0xfdea) LONG (4) 1<749697253>
65003 (0xfdeb) LONG (4) 1<106987391>
SIOC:DMP1:PM01:PATTERN.L 2013-10-03 18:14:13.106987 32639
OTRS:DMP1:695:Image:ArrayData 2013-10-03 18:14:13.106987 16 16 15 14 16 1 . . .
OTRS:DMP1:695:Image:ArrayDataTime 2013-10-03 18:14:13.106987 32639
OTRS:DMP1:695:Image:ArrayDataTime.A 2013-10-03 18:14:13.106987 749697253
OTRS:DMP1:695:Image:ArrayDataTime.B 2013-10-03 18:14:13.106987 106987391
TIFF Header
Tag65002: epicsEpoch in Second Tag65003 : nano-second in epicsTimestamp
PuleID from Pattern Processing
Image Waveform
The timestamp parsed by a Sub-routine Record
PulseID
epicsEpoch in Second
Noano-second in epicsTimeStamp

## Slide 13: Attributes for Plugin
Plug-In’s in areaDetector provides user attributes: EPICS PV attribute and Param attributes
  To provide additional meta-data which are not supported by the driver and plug-in
  EPICS PV attribute: get PV value into an attribute
  Param attribute: turn an internal variable in the software into an attribute
  User attribute can be configured by use of an XML file
Implement new attribute called: “function” attribute
  Provide a callback mechanism to call the user function
  Allow programming additional logic to existing plug-in’s without code change

## Slide 14: Test Setup for netCDF file plugin
NDArrayData
User-defined
Time Source Function
Timestamp
& Timing Pattern Modifiers
@ time source callback time
AsynPort Driver
File plug-in for netCDF
Timestamp
& Timing Pattern Modifiers
@ plug-in callback time
XML file for User Attributes
Function Attribute Callback
for diagnostic purpose
epicsTSSec
epicsTSNSec
netCDF file
CA monitor callback
Pulse ID from PV
SIOC:DMP1:PM01:PATTERN.L
Built-in Attributes
Attr_Seconds
Attr_Nano-Seconds
Attr_PulseID
Attr_TimeSourceTS
Attr_Timeslot
Attr_TimeString
Attr_TimeSourceDelay
Attr_FuncDelay
User Attribute

## Slide 15: Test Results: dump of netCDF header

## Slide 16
Built-in Attributes
areaDetector native timestamp (double type)
EPICS timestamp from the time source function Second
Nano seconds
User Attributes
EPICS timestamp from the function attribute
Seconds
Nano seconds
Pulse ID
Pulse ID from PV
Timeslot at time source calling
Timeslot at attribute calling
Pulse ID matching!!!
Timestamp Matching!!!
Timeslot matching!!!

## Slide 17
String Type EPICS timestamp
Delay measurement for the time source callback from the fiducial
(in nano-second scale)
Delay measurement for the attribute callback from the fiducial
(in nano-second scale)
Only few tens micro-second delay between the user-defined time source callback and the attribute callback

## Slide 18: Conclusion
areaDetector improvements
  time source callback
  user attributes in plugin
Excellent co-operation from Mark River
  Accept to apply SLAC specific requirements to areaDetector
  Shift the specific requirements to generic new features for benefit to community

## Slide 19: Special Thanks to Mark Rivers !!!