## Slide 1: EPICS Integration of Raspberry Pi Monitoring System for simple applications and user trainings
Son, ChangWook
IBS, S.Korea
May 18. 2015 Michigan, USA
1/13
2
0
1
5

## Slide 2: Contents
  Brief introduction of raspberry pi
  How to use and integrate into EPICS
  Environment monitoring system
  EPICS Training kit
  5. Summary & Plan
2/13
2
0
1
5

## Slide 3: Raspberry Pi
 | Model B | Model B+ | Pi2
SoC | Broadcom BCM2835 | Broadcom BCM2835 | Broadcom BCM2836
CPU | 700 MHz ARM1176JZF-S Single Core |  | 900 Mhz ARM Cortex-A7 Quad Core
SDRAM | 512MB | 512MB | 1GB
External Memory | SD | Micro SD | Micro SD
Interface | GPIO, UART, I²C, SPI, I²S +3.3V, +5V |  | 
Power | 5V 700 mA (3.5 W) | 5V 600 mA (3.0 W) | 5V 800 mA (4.0 W)
OS | Raspbian, Google Chrome OS, Windows 10 (Pi2) |  | 
Library | wiringPi, BCM2835, pigpio, Python, Ruby, Perl, Java |  | 
Cost | $35 | $35 | $35
3/13
2
0
1
5

## Slide 4: How to use
Sensors
IOC
(Raspberry Pi)
Controller (PLC)
Ethernet
4/13
2
0
1
5
PLC Test System
RPi
OPI

## Slide 5: How to use
Motor
IOC
(Raspberry Pi)
Driver
Ethernet
5/13
2
0
1
5
Step Motor Test
OPI

## Slide 6: How to use
Sensors
IOC
(Raspberry Pi)
Ethernet
6/13
Camera
Dust
Sensor
Raspberry Pi
T&H
Sensor
2
0
1
5

## Slide 7: Environment Monitoring System
- In order to Monitoring of Temperature and Dust
- Three Raspberry pi is installed in SRF Test Facility
- Two routers have configured for network
Wireless
Bridge
7/13
ECRIS
RFQ
Pi1
Pi0
Pi2
2
0
1
5

## Slide 8: Environment Monitoring System
Data
Web Browser
Web Server
IOC
(Pi0)
Archiver
Appliance
IOC
(Pi1)
IOC
(Pi2)
Server(Debian wheezy 64bit)
8/13
2
0
1
5
Python script
- Channel data is archived -> archiver appliance
- Retrieve & Save to text data -> Python script
- Convert to graph -> jQuery
jQuery

## Slide 9: Web Interface
Pi0 Tem.
Pi1 Tem.
Pi2 Tem.
7 Days
Pi0 Camera
Pi1 Camera
5 min. interval snapshot
9/13
Pi1 Dust
2
0
1
5

## Slide 10: EPICS Training Kit
Propose
- For education and EPICS starter user
- For easy approach
High Cost & Complicated
Low Cost & Simple
10/13
2
0
1
5

## Slide 11: EPICS Training Kit
11/13
2
0
1
5
Support Library & Applications
https://github.com/RaonControl -> Private
Will be open to the public
Support Library
Applications

## Slide 12: EPICS Training Kit
Button
LED
Temperature
Sensor
Character LCD
12/13
2
0
1
5

## Slide 13: Summary & Plan
13/13
Summary
Various Raspberry pi application test is done
Environment Monitoring System is working
Plan
Reliability Test for Step Motor with test bed system
Temperature distribution test of Cooling Rack
Make a all-in-one case with 3D printer
2
0
1
5