## Slide 1: From VME/RTEMS to Industrial PC/LinuxRT: A Migration Story
Mitch D’Ewart
May 19 2015
EPICS Collaboration Meeting May 2015

## Slide 2: Outline
SLAC controls platform background
Why Linux for controls
Building an embedded real-time Linux system
System bring-up
LinuxRT considerations
Current status
Open issues
Future outlook

## Slide 3: SLAC Accelerator Control Platform
  VME/RTEMS based EPICS IOCs
    Strong presence at SLAC
    Most of LCLS control system
    Most of SPEAR3 control system
  New controls platforms
    Industrial PC, xTCA
      X86, x86_64, atom x86
    Embedded targets
      ARM
    New projects to upgrade to modern platform

## Slide 4: Why Linux?
New platform, opportunity to upgrade OS
Linux is the OS used for servers, OPI at SLAC
Linux is the development platform for EPICS at SLAC
Reuse existing components
  Already used for soft IOCs
Open source
Full control of the software

## Slide 5: Linux for Real-Time Applications
Many options to modify Linux to behave like RTOS
  RTAI
  Xenoami
  CONFIG_PREEMPT (config option in vanilla Linux)
  PREEMPT_RT Patch
  Many more
Goal is to make Linux like an RTOS
  Remove unbounded latency
  Minimize jitter

## Slide 6: PREEMPT_RT Patch
Set of patches to make vanilla Linux behave like an RTOS
Make Linux itself real-time
  Does not require microkernel/hypervisor
    Example RTAI, Xenamoi, etc.
Compatible with Linux programs
  If it runs on vanilla Linux it runs on PREEMPT_RT
POSIX interface for modifying priorities

## Slide 7: Buildroot for Linux RT System Generation
Embedded Linux build system
  Cross-compile toolchain
  Root file system with libraries cross-built
  Kernel and bootloader images
Easy to setup
  menuconfig, gconfig, xconfig, etc.
Hundreds of packages
Simple structure to understand and extend
Open source, vendor neutral

## Slide 8: Our Embedded Linux Target
Use buildroot and PREEMPT_RT patch
Minimal root file system
  Small but powerful
  System bring-up, debug any issues
  NFS mount additional directories
    Programs, libraries, kernel modules, etc.
  Target real time applications
Busybox – single binary for multiple unix utilities
Use GNU C library – glibc
  Started with uclibc but have moved to glibc
  Needed for vendor supplied static libraries

## Slide 9: uClibc vs glibc
uClibc
  C library targeting embedded systems
  Smaller than glibc
    complete .so set 560k
  Source compatible glibc
    Cross compile application is generally enough
  Not compatible across version (backward, forward compatible)
glibc
  GNU C Library
  Larger footprint that uClibc
    complete .so set 7.9M
  Generally binary compatible
  Generally backward compatible
libc_bench
  Benchmark comparing C library implementations

## Slide 10: LinuxRT Targets
Started with single LinuxRT target
  buildroot-uclibc-x86
Added targets
  buildroot-uclibc-x86
  buildroot-uclibc-x86_64
  buildroot-glibc-x86
  buildroot-glibc-x86_64
  buildroot-zynq
Now supporting
  buildroot-glibc-x86
  buildroot-glibc-x86_64
  buildroot-glibc-zynq

## Slide 11: Maintaining Buildroot Configuration
How to maintain consistent configuration across targets?
Maintain common and target specific configurations [Till Straumann]
Buildroot configuration
  br-<br-release>-common.config
  br-<br-release>-<target>.config
Linux configuration
  linux-<linux-release>-common.config
  linux-<linux-release>-<target>.config
Busybox configuration
  bb-<bb-release>.config

## Slide 12: Bootloader, System Bring-Up
PXE and iPXE bootloaders
Power on -> BIOS -> Network card PXE stack
DHCP request
  Obtain IP address
  Point to image for TFTP
TFTP Download
  Root file system (rootfs.ext2)
  Kernel image (bzImage)
Initial NFS mount
Generic startup scripts (Kristi Luchini, Garth Brown)
  Additional NFS mounts
  Load kernel modules
  Start EPICS processes

## Slide 13: LinuxRT Considerations
Lock real-time applications in memory
  Memory swap will kill real-time performance
  Call mlockall() as soon as possible
Run with real-time priorities
Run multiple real-time IOCs on single server
  Need CA Repeater running
Now need kernel modules for each target
How to organize this?
  Current approach
    linuxKernel_modules
      <kernel module>
        <target>
        <target>
      <pci_mrfevr>
        <buildroot-glibc-x86_64>
        <buildroot-glibc-x86>

## Slide 14: Multicore EPICS IOC
Resource sharing
  Many IOCs on single host – BPM, LLRF, MPS, etc.
  Sharing microResearch EVR
Application scaling, load balancing on SMP
  Let the scheduler decide where to run a process?
How to best share resources
  CPU affinity for separate IOCs?

## Slide 15: Current Status
Accelerator control systems
  Beam position monitors
  Machine protection system (MPS BSA processor)
  Low Level RF
  Magnet power supply controls
Photon control systems
  Industrial PCs
  Primarily RHEL6
  Beginning to role out LinuxRT
Ongoing migration to LinuxRT

## Slide 16: Open Issues – Non RT Behavior?
EPICS Base 3.14.12.4
EPICS missing deadlines on LinuxRT with SMP
  RT performance loss on SMP?
  MPS BSA Processor (Gasper Jansa)
Setting CPU affinity resolves the issue
  Not ideal solution

## Slide 17: Future work
Clean up resource sharing – MRF EVR
Investigate low latency network stack
  Linux network stack has higher latencies than RTEMS
  Have low latency network stacks on RTEMS
    Fast Feedback Network
    UDP communication
  Linux network stack has higher latencies than RTEMS
    Ping pong testing shows much higher latency
Investigate SMP scheduling issues

## Slide 18: Conclusion
New platforms to support at SLAC
  x86, x86_64, ARM
LinuxRT (PREEMPT_RT patch) is the future RTOS for SLAC
Many systems already gaining experience with LinuxRT
Many more systems to migrate in the future

## Slide 19: Thanks to
Till Straumann
Kukhee Kim
Ernest Williams
Gasper Jansa
Kristi Luchini
Garth Brown

## Slide 20: References
https://rt.wiki.kernel.org/index.php/Main_Page
http://buildroot.uclibc.org
http://www.etalabs.net/compare_libcs.html
https://www.osadl.org/fileadmin/dam/rtlws/12/Brown.pdf
http://www.freescale.com/files/soft_dev_tools/doc/white_paper/CWLNXRTOSWP.pdf