Muon Cooling for a Neutrino Factory and Muon Collider
MICE Status and Plans
C. T. Rogers, on behalf of the MICE collaboration
ASTeC Intense Beams Group
Rutherford Appleton Laboratory

---
Overview
- Reminder of purpose and design of MICE
- Status of diagnostics
- Status of magnets
- Plans for operations
- Analysis of data
- Route to full demonstration of ionisation cooling

---
Muon Accelerators
Pavel Snopok,
December 2014

---
4D Ionisation Cooling
4D Ionisation Cooling
RF
Absorber
4D (transverse) cooling achieved by ionisation energy loss
Absorber removes momentum in all directions
RF cavity replaces momentum only in longitudinal direction
End up with beam that is more straight
Stochastic effects ruin cooling
Multiple Coulomb Scattering increases transverse phase space volume
Energy straggling increases longitudinal phase space volume

---
MICE – Ionisation Cooling PoP

---
MICE Aims

---
Diagnostics

---
Trackers
- Muons pass through scintillating fibre planes across solenoid
  - Fit a helix to the particle trajectories to reconstuct momentum
  - Principle detector for phase space reconstruction
- Tracker hardware is installed in spectrometer solenoids
- Successfully read out tracker electronics in the hall in January
- Ongoing work in cabling, readout, unpacking and reconstruction
- Talk by Ed Overton on Thursday

---
EMR
Francois Drielsma et al.

---
Particle Characterisation
muon
electron
Penetration depth
bar
multiplicity
per plane
plane
density
Francois Drielsma et al.
- EMR commissioned and calibrated
  - Paper in preparation

---
Beam Polarisation
Sophie Middleton et al.
- Beam polarisation can affect positron impurities downstream
- May be possible to measure beam depolarisation due to material
- Calculate angular distribution of decay positrons in EMR
  - Deduce beam polarisation

---
Muon vs Pion Response
Cerenkov
Muons
Muons
Pions
Pions
Cremaldi/Winter

---
DAQ trigger system
- New trigger based on CAEN V1495 FPGA
  - Replaces maze of wiring
  - More functionality
  - Less fragile
- Now accepted as production trigger

---
Magnets

---
Spectrometer Solenoid
- Both spectrometer solenoids are on the beamline
- Solenoid refurb was completed following spectrometers transport to RAL
- Refurb on helium and vacuum system
- Compressor installation
- Ongoing work on cryocoolers
- Small leak on bellows

---
Absorber and Focus Coil
- FC2 is on the beamline
- FC1 has now been accepted by the collaboration
  - Achieved current is lower than design current
  - But required current is lower due to lattice revisions
- Focus coil power supply glitches
  - Detecting false quenches; investigation ongoing
- Readiness review for lH2 operation in January 2015
  - Relief-line for lH2 safety window not large enough diameter
  - Requested further testing of lH2 safety windows
  - Step IV will start with LiH while lH2 team review options
beam

---
Magnet Mapping
V. Blackmore, J. Cobb
Additional concern about flange alignment to bore

---
Effect on Beam (Preliminary)
10k muons
10k muons
Beam centroid (y)
Beam 4D emittance
- Now track sample of particles through the cooling channel
  - All magnets powered
  - Random seed = initial emittance
- BLACK: magnets with perfect alignment
- BLUE: magnets with measured alignment
- Plan to “bolt and be damned”

---
Operations

---
Operations Status
- Shifts
  - In normal running mode, data taking will be 24/7
  - To be included on publications, a shift quota must be fulfilled
    - 3 x 5 shift blocks, subject to confirmation
  - Shifters need to do some training and observe two shifts
- On-call/experts
  - Subsystems will provide on-call and system experts
- Few weekends data taking in March/April
  - Shake down readout and debugging controls systems
  - Beamline pre-commissioning; try a few newly optimised settings
  - Excercise the readout → data movement → reconstruction data flow
- Talk by Milorad Popovic on Thursday

---
Plan for User Run 2015/01
- Constraints
  - Magnet training has priority over data taking
    - May take the entire user run
  - 1 shift per night during first part of the user run (01a)
  - 3 shifts per day during second part of the user run (01b)
- Two outline run plans prepared
  - Baseline scenario
  - Pessimistic scenario
- Priorities:
  - Commission the tracker
  - Check integrated detector resolution/efficiency
  - Beam-based measurement of detector and magnet alignment
  - MICE muon beamline to MICE cooling channel matching
  - Demonstrate cooling channel optics
- Initially no absorber
- Talk by Paul Soler

---
Optimistic run plan
- Blue – external constraint
- Red – ran out of time
- 9 shifts required to complete commissioning after 01b

---
Pessimistic run plan
- Blue – external constraint
- Red – ran out of time
- 68 shifts still required to complete commissioning after 01b

---
Plan for subsequent user runs
- Lithium Hydride will be installed before liquid Hydrogen
  - Extra 6 days for LiH install in each run eats into our contingency
- Subject to progress in 2015-01

---
Analysis and Optics

---
Effect of Non-Linear Dynamics
- Non-linear emittance growth can ruin the ionisation cooling effect
  - Appears to arise due to high-order terms in solenoidal field expansion
- Mismatch makes problem worse
R. Ryne et al.

---
Beam weighting
- Beam selection samples the beam events to try to find a sample of beam events that match some desired distribution
  - Try to select events in under populated regions
- Beam weighting applies statistical weights to events
  - Events in under-populated regions we count more than once
  - Events in over-populated regions we count less than once
  - We are allowed to apply fractional weights to these events
- Beam weighting algorithm
  - Decide which regions are over-populated or under-populated
  - Apply an appropriate statistical weighting
- How do we decide which regions are over-populated?
  - In a high dimensional space like 4D or 6D

---
Beam weighting (ND)
Vector between
nearest neighbours
bisector
- Introduce “Voronoi tesselation”
  - For each point, find nearest neighbour vectors
  - Bisect nearest neighbour vectors to define a tile
  - Determines region nearest to a particular point
  - Content of the region is “phase space volume” of the point

---
Boundary effects
- Does it work?
  - Go from Var(x), Var(y) = 1, 1 to Var(x), Var(y) = 0.5, 1
  - Try applying weighting 100 times
  - Close enough?

---
Bayesian Methods
- Use Bayesian method to validate cooling channel model
  - No beam selection required!
  - e.g. magnet currents and measurement errors (toy MC)
R. Ryne

---
Demonstration of Ionisation Cooling

---
Demonstration of Ionisation Cooling
- Secondary absorber design decisions:
  - Baseline material is LiH – fallback is plastic
  - Baseline position is on radiation shutters – fallback is in SS bore
- Need to finalise FC->FC gap length – optics decision
- Talk by JB Lagrange on Thursday

---
Demonstration of Ionisation Cooling
- RF cavity operation in 0 B-field demonstrated
- More to hear about operation in > 0 T field later in the week
- RF power distribution system under design
  - Parts have been purchased, some retrofitting
- RF session on Thursday afternoon

---
To Conclude...

---
Conclusions
- Reminder of purpose and design of MICE
- Status of diagnostics
- Status of magnets
- Plans for operations
- Analysis of data
- Route to full demonstration of ionisation cooling

---
Conclusions
DATA
- Physics goals have been outlined
- Status of Step IV analysis preparation has been discussed
- Plan for June/July has been presented
- Planning for subsequent runs discussed
- Plan for analysis group support of Step IV operations was described