Muon Cooling for a Neutrino Factory and Muon Collider
Characterisation of the KURRI FFAG main ring
C. T. Rogers, on behalf of the KURRI-FFAG collaboration
ASTeC Intense Beams Group
Rutherford Appleton Laboratory

---
FFAG accelerators for muons
- Need to accelerate muons quickly – they decay!
- Rapid Cycling Synchrotron
- Recirculating Linear Accelerator
- Fixed-Field Alternating Gradient Accelerator (FFAGs)
  - Higher bending field at large radii
  - Scale the optics with radius – keeps constant tune

---
KURRI FFAG accelerators
- 11 MeV linac for injection
- Three FFAG accelerators at KURRI
  - Old injector ring 3 – 11 MeV
  - ERIT ring 11 MeV internal target machine
  - Main ring 11 - 150 MeV; test ring for test ADS Reactor

---
Design features
- Yoke-free combined function scaling magnets
- Tight bend at injection
- Variable frequency RF (not a cyclotron)
  - Magnetic material in RF cavity
- Diagnostics
  - Radial probe
  - Beam monitors
  - Horizontal and vertical perturbators

---
Experimental Programme
- Experimental programme aims to:
  - Validate simulation of the FFAG
    - Kinematics
    - Foil/stochastics
  - (Later) Examine space-charge dominated regime
    - Effect of foil
    - Effect of high radius/not symmetric beam-pipe
- Measure
  - Closed orbit distortion
  - Energy-dependent tune
  - Field index
  - Foil characteristics

---
Transverse Simulation
- Excellent agreement between many codes
- SCODE: FFAGs and synchrotron code with space charge
- OPAL: Cyclotron modelling code with space charge
- MAUS: Geant4 based code (yes the MICE code) with good material physics models
- Zgoubi: standard FFAG code
- EARLIETIMES: KURRI home-brew code

---
Closed orbit distortion
- Closed orbit distortion (COD)
  - Magnetic alloy in RF cavity
  - Yoke-free scaling magnets
- Measure using radial probe
  - Place probe (collimator) at a given radius
  - Inject beam at 11 MeV
  - Look at time-to-loss
  - Move probe
  - Repeat...
- Allows to study radial position of beam
- Make a coil to correct COD

---
Measure field index
- Measure closed orbit in the acceleration cycle
  - Move radial probe;
  - Accelerate beam and look at RF frequency when the beam scrapes on the probe
  - Apply:
Note influence of closed orbit distortion

---
Measured Tune
- Use vertical perturbator to excite vertical coherent oscillations
- For horizontal tune
  - Use horizontal perturbator
  - In low energy region use RF cavity
  - In high energy region use extraction kicker
- Look for coherent oscillations in bunch monitors

---
Foil Model
- Use GEANT4 to model foil
  - Energy loss and MCS is consistent with PDG numbers
  - Note slight over estimate of the tail of the stopping power distribution for C

---
Simulation of Foil in Ring
- Combined ring simulation
  - Try simulating foil and RF in the ring
  - How can we study the foil effect on beam?
- Vary RF cavity voltage
  - When does the RF bucket form?

---
Measurement of foil energy loss
dt
- Measure time of RF peak compared to bunch peak
- Validate longitudinal model
  - What voltage is required to get RF bucket formation?
- Get RF bucket formation between 0.46 V – 1.33 V
  - Consistent with MC
- Seek to quantify
No longitudinal capture
Longitudinal capture

---
Summary
- Characterisation of KURRI FFAG
  - Closed orbit
  - Tune
  - Field index
  - Foil model (energy loss)

---
Towards high intensity
- Looking to move to high intensity running
  - Correct COD
  - Correct tune shift
  - Improve transmission