## Slide 1: Energy deposition update
P. Snopok
Front End phone meeting
March 31, 2015

## Slide 2: MARS
Modified the old chicane deck to work with the new MARS version
  m1512.f => m1514.f
No ROOT or other special geometry required, baseline extended geometry will work
Main concern: channel length
  may need to simulate by sections (buncher/rotator/cooler)

## Slide 3: Input
ICOOL deck from David Neuffer
Start 10 m downstream of the target
  C target 6.75 GeV protons by Xiaoping Ding
  Is there a MARS file @ 10 m? I can use it directly
Not going to use the chicane in any form
  unless there is a desire to run the chicane final distribution through the rest of the front end
    this will still be a separate simulation
Buncher: 21 m (at 17 atm)
Phase rotator: 24 m (at 34 atm)
Matcher: 3 m (no gas, should I change that?)
Cooler: 112.5 m (150 cells, no gas)

## Slide 4: Magnetic field
Straightforward in drift/buncher/rotator: 2 T uniform field, easy to implement in MARS
Matcher/cooler: there is a list of coil sheets provided with the ICOOL deck
  I can use those to generate field maps
  Some minimal transformation is required for import into MARS
  are there field maps readily available?

## Slide 5: RF cavities
325 MHz, 25 cm
  except the first cavity that is 50 cm long
Modeled in MARS using simple pillbox geometry
  unless a different geometry is strongly desired
Energy change is via RF kick at the center of the cavity
  MARS invokes user-defined routine whenever the center plane is crossed
Documentation is limited, have some examples handy
Phasing information from the RF diagnostic file
  can be trusted?

## Slide 6: Geometry challenge
What are the layers (material, thickness, specific properties) comprising the cavity wall
  no such information in ICOOL/G4beamline
How thick the beampipe and shielding around (if any) should be
  energy deposition study, not shielding study
What else is in the channel, other than RF, coils, solid absorbers (15 mm LiH around RF)
  any windows, structures around coils