## Slide 1
Single-shot ultrafast imaging using spatiotemporal dispersion of ultrashort pulse
September 11-14, 2018
ULITIMA 2018
Argonne National Laboratory
Keiichi Nakagawa
Dept. Bioengineering, Precision Engineering,
The University of Tokyo

## Slide 2
Biomedical Precision Engineering Lab.
I. Sakuma
U. Tokyo
A. Tsukamoto
NDA, Japan
[Ca2+] increase evoked by acoustic waves
MDCK cells
Computer assisted surgery

## Slide 3
Motivation: acoustic interaction with cells
Stretch
Touch
Shear stress
I want to see it!
Acoustic wave
Cell

## Slide 4
I needed…
Sub-nanosecond temporal resolution
  Speed of sound: 1.5 µm/ns
Single-shot capability
  Structure of cell is changed
Good spatial resolution
  To analyze complex events
Low photo-damage of cells
  Intensity is focused both spatially and temporally
Capability for visualizing acoustic waves and cells
  Differential interference contrast (DIC) microscopy
~ 10 µm
~ 10 ns
AW

## Slide 5
Sequentially Timed All-optical Mapping Photography
(STAMP)
K. Nakagawa et al.
Nature Photonics 8, 695 (2014)
Japanese Patent 6120280,
I. Sakuma, K. Nakagawa, A. Iwasaki, F. Kannari, Y. Oishi, A. Tsukamoto
Filing date: Aug 20, 2013, Issue date: Apr 7, 2017
Notes: So, here I want to introduce a new type of ultrafast imaging method which we call STAMP that stands for sequentially timed all-optical mapping photography. With this method, we can perform motion-picture femtophotography of ultrafast dynamics.

## Slide 6
Principle

## Slide 7
Sequentially Timed All-optical Mapping Photography
Time domain
–
Spectral domain
Spectral domain
–
Spatial domain
s1
s2
s3
t1
t2
t3
t3
t2
t1

## Slide 8
Basic configuration of STAMP
Temporal
mapping device
Spatial
mapping device
Image sensor
Computer
Daughter
pulses
Target
Ultrashort
pulse source
Notes: This is a rough schematic of STAMP. It consists of an ultrashort pulse source, temporal mapping device, spatial mapping device, image sensor, and computer. The ultrashort pulse from the source is temporally stretched and segmented into several daughter pulses by the temporal mapping device. The daughter pulses are incident onto the target as successive flashes for stroboscopic image acquisition. Then, these pulses are separated by the spatial mapping device and incident onto different areas of the image sensor without image deformation.

## Slide 9
Operation of STAMP

## Slide 10
I needed…
Sub-nanosecond temporal resolution
  STAMP achieves sub-nanosecond resolution in videography
Single-shot capability
  Multiple frames can be obtained in a single shot
Good spatial resolution
  ~images quality of conventional microscopes
Low photo-damage of cells
  High-sensitivity imager can be used
Capability for visualizing acoustic waves and cells
Intensity image
STAMP
DIC
Amplitude
Wavelength
Phase
Polarization

## Slide 11
Features of STAMP
High temporal resolution
  STAMP achieves femtosecond resolution in videography
Single-shot capability
  Multiple frames can be obtained in a single shot
Good spatial resolution
  ~images quality of conventional microscopes
Detector
  Cooled CCD, EMCCD, ICCD, high-speed imager, X-ray/IR imager, etc.
Compatible with conventional imaging techniques and instruments
Intensity image
STAMP
DIC, Holography, Polarization imaging, etc.
Amplitude
Wavelength
Phase
Polarization

## Slide 12
Limitations of STAMP
Technical limitations
  Bandwidth of light source, configuration of spatial mapping device, etc.
Trade-off between the exposure time and number of frames
Requirements for the sample
  Basically, STAMP cannot capture luminous objects
  The object does not have any strong dependence on wavelength
Notes:   To achieve large number of frames, the daughter pulse bandwidth needs to be small, but the exposure time becomes large.

## Slide 13
Experimental realization

## Slide 14
Collaborators
A. Iwasaki
U. Tokyo
F. Kannari
Keio Univ.
Y. Oishi
Keio Univ.
(KEK, Japan)

## Slide 15
Proof-of-principle experiment
Cooled CCD camera
Resolution: 2048×2048
QE: 94% @810 nm
Ti:S laser with CPA
Pulse duration: 70 fs
Center wavelength: 810 nm
Rep. rate: 1 kHz
Single pulse was generated by an optical chopper and a mechanical shutter
Spectral imaging
with periscope array
Mirrors
Diffraction
grating
Periscope
array
Cylindrical
mirror
Pulse shaper
Pulse stretcher
~ fs
~ ps
Diffraction grating
/2
/2
PBS
Mirrors
PBS
Diffraction
grating
Lens
Lens
SLM
Grating pair
Glass rods
50 µm
799-802 nm
814-817 nm
811-814 nm
808-811 nm
805-808 nm
802-805 nm

## Slide 16
Femtosecond laser ablation
Sample
  Glass (t = 50 µm)
Excitation pulse
  Pulse duration: 70 fs
  Center wavelength: 810 nm
  Pulse energy: 100 µJ
    ～ 1015 W/cm2
Imaging
  Frame interval: 15.3 ps
    65.4 Gfps
  Exposure time: 13.8 ps
  Shadowgraph imaging

## Slide 17
Femtosecond laser ablation
0 ps
15.5 ps
31.0 ps
46.5 ps
61.5 ps
76.5 ps
20 µm
Glass
Air
Glass
Air
Reproduced from R. R. Gattass, E. Mazur, Nature Photon. (2008)

## Slide 18
Phonon polariton (THz radiation)
Sample
  LiNbO3 (t = 500 µm)
Excitation pulse
  Pulse duration: 70 fs
  Center wavelength: 810 nm
  Pulse energy: 40 µJ
Imaging
  Frame interval: 812, 229 fs
    1.23, 4.37 Tfps
  Exposure time: 1020, 733 fs
  Polarization-gating imaging
Notes: Next, we used STAMP to monitor the phonon-polariton dynamics on femtosecond timescales.
An excitation pulse was cylindrically focused into a lithium niobate wafer.
The dynamics was monitored in a transmission mode.
These are the parameters of an excitation pulse.
Pulse duration was 70 fs, center wavelength was 810 nm, and pulse energy was 40 micro joule.
These are conditions of imaging.
Frame interval were 812 fs and 229 fs, these are equivalent to 1.23 Tfps and 4.37 Tfps, respectively.
Exposure time were 1020 fs and 733 fs, respectively.
For visualizing phonon wave-packet, we used polarization-gating imaging technique..
birefringence

## Slide 19
Phonon polariton (THz radiation)
0 fs
780 fs
1590 fs
2400 fs
3255 fs
4035 fs
100 µm
2167 fs
2357 fs
2517 fs
2782 fs
3052 fs
3297 fs
100 µm
The speed of wave-packet is calculated from the movie to be 4.6×107 m/s
0 fs
190 fs
350 fs
615 fs
885 fs
1130 fs
100 µm
We could observe complex dynamics of phonon wave-packet formation by STAMP.
Notes:   Here are the image frames that captured the phonon pulse dynamics with a frame interval of 800 fs, corresponding to a frame rate of 1.2 Tfps. First, we can see a complex electronic response of the crystal and then the formation and upward propagation of a phonon pulse. With a finer frame interval of 230 fs or a frame rate of 4.4 Tfps, we can visualize the detailed dynamics of the electronic response at the phonon pulse generation as well as the phonon pulse propagation. Interestingly, the propagation speed of the phonon pulse is as high as one sixth of the speed of light, but our STAMP can temporally resolve this dynamics clearly. Furthermore, from the images, we can perform both time-domain and frequency-domain analysis to identify the THz spectrum of the phonon pulse.

## Slide 20
Visualizing acoustic interaction with cells?
Nature Photonics 8, 744 (2014).

## Slide 21
Visualizing acoustic interaction with cells?
2014 – 2015
Postdoc
Goda Lab at Tokyo Univ.
- 2016
Postdoc
Nelson Group at MIT
2016 - present
Assistant Prof -> Lecturer of Tokyo Univ.
I have obtained a femtosecond laser this year!
I graduated before doing bio-experiment
COMING SOON! (hopefully)

## Slide 22
25-frame burst-mode imaging
T. Suzuki et al., Appl. Phys. Exp. (2017)
STAMP utilizing spectral filtering
F. Kannari
T. Suzuki
Ph.D. candidate
at Kannari Lab
T. Suzuki et al., Int. Conf. Ultrafast Phenomena (2016)
fs laser-induced breakdown in glass
Phase transition of Ge2Sb2Te5
0 ps
5.5 ps

## Slide 23
Directions

## Slide 24
Two directions of STAMP
Finding and understanding dynamic behaviors in atomic world
STAMP
New strategy and method
based on the combination with AI and informatics
0 ps
15.5 ps
31.0 ps
46.5 ps
61.5 ps
76.5 ps
20 µm
0 fs
190 fs
350 fs
615 fs
885 fs
1130 fs
100 µm
For human
For machine

## Slide 25
Jump in SMALL WORLD
m (100)
s
(100)
Speed of Light: 0.3×109 m/s
Speed of Sound: ~1×103 m/s
1 m/s
ms
(10-3)
µs
(10-6)
ns
(10-9)
ps
(10-12)
fs
(10-15)
mm (10-3)
µm (10-6)
nm (10-9)
pm (10-12)
Space
Time
We need ultrafast imaging in observation of atomic-scale events

## Slide 26
Original concept: spatiotemporal mapping
K. Nakagawa, “Spatiotemporal mapping photography for sub-nanosecond single-shot imaging” Doctoral Dissertation (2014).
The information compressed in the time domain
is expanded and detected in the spatial domain
through the parameter

## Slide 27
Spatiotemporal Mapping Photography
K. Nakagawa, “Spatiotemporal mapping photography for sub-nanosecond single-shot imaging” Doctoral Dissertation (2014).
Ultrashort pulse of X-ray or electron
Target
Motion picture reconstructed from the relation of
Detector
Temporal mapping device
Spatial mapping device
Jitter-less
Keys to achieve:
  Find a good parameter of 𝝌: wavelength, phase, polarization, incident angle, spatial profile (structured, frequency), etc.
    cf. cranz-schardin camera, single-shot spectroscopy with echelon, FRAME
  Make good use of the properties of pulse sources: XFEL, plasma accelerated electrons, etc.
  Employ computational imaging techniques: compressed sensing, machine learning, etc.

## Slide 28
High-speed imaging for machines
>1 kfps
Fast data acquisition
Data-driven science
Advances in
imager sensor and optics technologies
Advances in
information
science and technology
<30 fps
Slow sensing
Limitation in understanding
compact, cost-effective, easy to use

## Slide 29
Ultrafast imaging in high-speed imaging
High-speed vision and information science and technology
Ultrafast imaging
Matryoshka doll

## Slide 30
Demonstration: Nesting high-speed videography
1 kHz
~100 Gfps
1 kfps
Real-time feedback
Pulse manipulation
Ultrafast monitoring
Cyber-physical system
Machine learning
Laser processing
Air
Glass

## Slide 31
Summary
We have developed STAMP (Sequentially Timed All-optical Mapping Photography) for single-shot sub-nanosecond imaging
We use STAMP to monitor laser ablation, phonon-polariton dynamics, phase transition, and so on.
  Timescale: 100 fs - 100 ps
  Number of frames: 25
We are currently developing an advanced STAMP system for observation of acoustic interaction with cells
Next challenge: videography of ultrafast events in atomic scale
Strategy of high-speed imaging is changing with advances in image sensor, optics, and information technologies

## Slide 32
Acknowledgements
ULITIMA 2018
Committees & Members
Thank you very much!
Massachusetts Institute of Technology, Nelson Group
Biomedical Precision Engineering Lab., Univ. Tokyo
K. Goda
Kannari Lab., Keio University
R. Horisaki
A. Iwasaki
A. Tsukamoto
T. Ushida

## Slide 33
First demonstration of STAMP
  K. Nakagawa, A. Iwasaki, Y. Oishi, R. Horisaki, A. Tsukamoto, A. Nakamura, K. Hirosawa, H. Liao, T. Ushida, K. Goda, F. Kannari and I. Sakuma, “Sequentially timed all-optical mapping photography (STAMP)” Nature Photonics 8, 695–700 (2014).
  Interview "Femtophotography" Nature Photonics 8, 744 (2014).
25-frame STAMP
  T. Suzuki, R. Hida, Y. Yamaguchi, K. Nakagawa, T. Saiki and F. Kannari, “Single-shot 25-frame burst imaging of ultrafast phase transition of Ge2Sb2Te5 with a sub-picosecond resolution” Applied Physics Express 10, 92502 (2017).
For details of STAMP
  K. Nakagawa, “Spatiotemporal mapping photography for sub-nanosecond single-shot imaging” Doctoral Dissertation (2014).
Thank you for listening
kei@bmpe.t.u-tokyo.ac.jp
https://sites.google.com/site/keinakagawa6

## Slide 35
History of therapeutic acoustic waves
Science (1955)
1950s
High intensity focused ultrasound for tumor ablation
Lancet (1980)
Early 1980s
Shock wave lithotripsy
Late 1980s
Drug and gene delivery by sonoporation
PNAS (1987)
Ablate / Break
Recent
Ultrasound neuromodulation
Nat. Rev. Neurol. (2010)
2000s
Angiogenesis by low-intensity shock wave
Circulation (2004)
Control / Regulate
Notes: Control or regulate the biological function
We want to know how the acoustic waves interact with our body.

## Slide 36
Mechanobiological effects
Stretch
Touch
Shear stress
Difference in wavefront
Shear stress is loaded to the membrane
Reflection by the nucleus
The nucleus is pushed
Effects for the cytoskeleton and membrane
Notes: Control or regulate the biological function
We want to know how the acoustic waves interact with our body.

## Slide 37
Limitations in resolution
1 ms
1 s
1 ns
1 ps
1 fs
1 s
1 mm
1 m
1 nm
1 m
Space
Time
~10 ms
~1 ns
~100 nm
~100 µm
Diffraction limit
(Physical)
Mechanical & Electrical Limits
(Technical)
Notes: Let’s compare the temporal resolution with the spatial resolution. In spatial domain, the resolution of human eyes is limited to about 100 um. With the help of the microscope, we can see sub-micrometer objects down to about 100 nm, which is fundamentally limited by the diffraction limit.
On the other hand, in temporal domain, the resolution of human eyes is limited to about 10 ms. With the help of the conventional high-speed camera, we can observe fast dynamics down to about 1 ns. This limit comes from technical limitations in mechanical and electrical components of the camera such as mechanical scanning, data readout, and shutters. Here I want to emphasize that these limitations are technical, not fundamental, and therefore, there is room for improvement.

## Slide 38
Imaging of laser ablation dynamics with STAMP
Processing with ns-laser pulse
（nano: 10-9）
Processing with fs-laser pulse
（femto: 10-15）
B. N. Chickov et. al., Appl. Phys. A (1996).
http://www.allaboutvision.com
Laser ablation in medicine
http://www.bbc.com/news/health-27595573
© Medtronic
Notes: Which do you prefer?

## Slide 39
Excitation pulse
  Pulse duration: 70 fs
  Wavelength: 810 nm
  Pulse energy: 100 µJ
Corresponding to a frame rate of 65.4 Gfps (exposure time = 13.8 ps)
0 ps
15.5 ps
31.0 ps
46.5 ps
61.5 ps
76.5 ps
20 µm
Glass
Air
Laser
Imaging of laser ablation dynamics with STAMP
Notes: In order to show the utility of STAMP, we used it to observe laser ablation dynamics. Here a powerful pulse excites the glass plate while STAMP monitors its ablation process. Here are the STAMP image frames that indicate the generation of free electrons in the glass followed by the generation of a plume that expands away from the ablation point. The exposure time is 13.8 ps and the frame interval is 15.3 ps, which corresponds to a frame rate of 65.4 Gfps.

## Slide 40
Sample
  LiNbO3 (thickness = 500 µm)
Excitation pulse
  Pulse duration: 70 fs
  Center wavelength: 810 nm
  Pulse energy: 40 µJ
Atoms
Phonon-polariton: collective lattice vibrational waves excited by electromagnetic waves
Imaging of phonon pulse dynamics with STAMP
Notes: The next target was observation of phonon pulse dynamics with STAMP. Phononics has been a hot area of research nowadays as it is important in semiconductor physics and therefore is a good choice as a testbed for testing STAMP’s high-speed imaging capability.
We excited this lithium niobate crystal with a cylindrically focused pulse to produce a phonon pulse via impulsive stimulated Raman scattering while we monitored the light-matter interaction with STAMP.
This vibration is classified as an optical phonon so the velocity of this phonon pulse is much fast.

## Slide 41
0 fs
780 fs
1590 fs
2400 fs
3255 fs
4035 fs
100 µm
Frame interval: 800 fs (Corresponding to a frame rate of 1.2 Tfps)
0 fs
190 fs
350 fs
615 fs
885 fs
1130 fs
100 µm
2167 fs
2357 fs
2517 fs
2782 fs
3052 fs
3297 fs
100 µm
Frame interval: 230 fs (Corresponding to a frame rate of 4.4 Tfps)
Imaging of phonon pulse dynamics with STAMP
Notes: Here are the image frames that captured the phonon pulse dynamics with a frame interval of 800 fs, corresponding to a frame rate of 1.2 Tfps. First, we can see a complex electronic response of the crystal and then the formation and upward propagation of a phonon pulse. With a finer frame interval of 230 fs or a frame rate of 4.4 Tfps, we can visualize the detailed dynamics of the electronic response at the phonon pulse generation as well as the phonon pulse propagation. Interestingly, the propagation speed of the phonon pulse is as high as one sixth of the speed of light, but our STAMP can temporally resolve this dynamics clearly. Furthermore, from the images, we can perform both time-domain and frequency-domain analysis to identify the THz spectrum of the phonon pulse.

## Slide 42
高速度イメージングの必要性
= 100 µm (髪の毛の太さ) / 10 µs
http://www.bbc.com/news/science-environment-23462815
= 100 pm (原子の大きさ) / 10 ps
= 100 mm / 10 ms ←人間の目（と脳）では分解不可
100 m / 10 s
9.63
9.75
9.79
9.80
Olympics 100m final at London 2012

## Slide 43
細胞レベルの音響作用？
音響波面を観察すれば物理作用が推測できる
細胞核での反射
細胞核への運動量付与
細胞骨格や膜への影響も
細胞内外での波面のずれ
細胞膜へのせん断力

## Slide 44
撮影技術と超短パルス
STAMP
超短パルス
「光」
中川桂一，レーザー研究 (2015)
撮影技術
機械・電気デバイス

## Slide 45
STAMPの撮影例
0 ps
15.5 ps
31.0 ps
46.5 ps
61.5 ps
76.5 ps
20 µm
Glass
Air
0 fs
780 fs
1590 fs
2400 fs
3255 fs
4035 fs
100 µm
0 fs
190 fs
350 fs
615 fs
885 fs
1130 fs
100 µm

## Slide 46
The periscope array spatially separates image-encoded daughter pulses while satisfying the condition for image formation
Periscope array
Notes: The periscope array is the key component of the STAMP system. The image-encoded daughter pulses are diffracted by the first diffraction grating and then focuses onto the periscope array in which each different spectral component reflects back, but comes out at a different height while traveling the same optical path length regardless of wavelength because of this unique structure. Then, the daughter pulses are recombined at the second diffraction grating, but exit at different heights, keeping the spatial profile in each spectral component intact.

## Slide 47
空間写像装置
M. Tamamitsu, Y. Kitagawa, K. Nakagawa et al., Opt. Eng. (2015)
スライスミラーは
理化学研究所先端光学素子開発チーム，
東大天文学専攻との共同開発
当研究グループによる新しいスペクトラルイメージングシステム
今回は６分割スライスミラーを利用

## Slide 48
4. Low photo-damage of cells
Tissue (mm)
Cell (µm)
Photon density
Spatially: 106
Temporally: 103
Time
Time
Space
Space

## Slide 49
5. Capability for visualizing AW and cells
Differential interference contrast is used to detect the wavefront of acoustic waves and the shape of cell with high contrast
Acoustic wave
Space
Pressure: refractive index
Wavefront
large
Cell
Polarization and Phase