## Slide 1: LARP Accelerator Systems
17 February 2014
LARP DOE Review
Fermilab
T. Markiewicz/SLAC
BNL - FNAL- LBNL - SLAC
US LHC Accelerator Research Program

## Slide 2: LARP Accelerator Systems in 2014
 | Total | $742+60k | $495+60k without Simos & Toohig
Electron Lens Scraper | FNAL (Valishev, Stancari) | $315k | Separate presentation
Beam-Beam Studies | LBL (Ji) BNL (White) | $105k $67k | 33% Toohig ended 1/31/14
Irradiation Studies of Collimator Materials | BNL (Simos) | $180k →$0k | 2nd of 2 year commitment xfered to CRAB; $ needs replacing
Low Level RF | SLAC (Rivetta) | $37k | 
Travel to Support Delivered LARP Hardware | LBL (Ratti) SLAC (TWM) SLAC (Fisher) | $15k $15k $8k | Luminosity Monitor Rotatable Collimator & UA9 Synchrotron Light Monitor
Contingency |  | $60k | 
E_dep studies (FNAL, Mokhov) & Lattice Studies (SLAC, Cai) moved to Magnet Project
Crab Cavity & WBFB spun off into separate projects

## Slide 3: Beam-Beam Studies
These are essential for reducing project risk. A number of key components of HL-LHC performance scenario have not been demonstrated in hadron colliders
  very high beam-beam tune shift
  operation with crab cavities
Development of novel concepts is required to mitigate the high event density and ensure quality data delivery, which contributes to the efficient use of LARP equipment
LARP expertise is well recognized by CERN.
  LBNL and FNAL possess unique codes.
  A.Valishev (LARP/FNAL) is the leader of HiLumi LHC Beam-Beam Task
2011 DOE Review:
“Continue work on beam physics, especially beam-beam interactions.”

## Slide 4: Beam-Beam Studies
 | LHC nominal | HL-LHC 25 ns baseline
p/bunch [1011] | 1.15 (0.58A) | 2.2 (1.11 A)
Energy in one beam [MJ] | 360 | 690
Beam-beam tune shift | 0.01 | 0.033
#Pile up @5E34 | 25 | 140
New scheme
Crab-Kiss Collisions (S.Fartoukh)
Net gain in data quality by 2 at each step at constant performance
½ beam-beam tune shift
Beam-beam compensation wires
are in HL-LHC Plan B
w/o crab-cavity
significantly higher beam current
makes losses critical
machine imperfections critical
high pileup and pileup density
affect data quality

## Slide 5: Luminosity Monitor
Recall:
  System operational since LHC commissioning
    Used at every store to bring beams in collision and through the beta squeeze
    Not a single operational failure
  Handoff completed in 2010
Maintenance underway during LS1
  All four systems removed from TANs due to bakeout of the vacuum structures
After radiation cool-down
  CERN will test, maintain and reinstall
  LARP will assist in advisory capacity
Contributions to early discussions of the conceptual design of the luminosity monitors for the HL-LHC
  x

## Slide 6: LLRF
SLAC team successfully modelled performance of the LLRF control of the 400 MHz LHC system: used for commissioning, to system limitations, ….
CERN needs the equivalent for the new SPS 200 MHz+800 MHz system, ideally soon enough to provide guidance on upgrade choices
  Base model of SPS RF Cavity and LLRF generated as FY13 deliverable.
  Original FY14 plan was to study hardware limitations & effect on beam loading and instabilities. Examples:
        New cavity controller with 1-turn delay feedback, feedforward and longitudinal damper
        Interplay between the 200MHz and the 800MHz system
        RF interaction with beam
Funding gutted in summer 2013 adjustment of FY14 budget
CERN (Philip Baudregian) and SLAC (Claudio Rivetta) looking for a cost effective way (SLAC supervising a fellow, etc.) to use 10% FTE FY14 budget
Ex-LARP Ph.D./Toohig Fellow/CERN staff Themis Mastorides now Asst. Prof. at Cal Poly & may possibly participate in these activities.

## Slide 7: RF System Model for SPS Interaction of LLRF and Beam Dynamics
    Example: Evaluating the impact of technology choices in transient beam loading and instability growth rates.

## Slide 8: Synchrotron Light Monitor
The LHC 4 TeV nominal emittance SLM system had a telescope viewing a 1mm spot at 30m and is diffraction limited. Main effort is to prepare for smaller 7 TeV beams with improved emittance. Thought is to used light source inspired interferometry to go below the diffractive limit despite significant blurring due to depth of field of elongated 6m LHC dipole source.
Alan Fisher has developed a layout & analysis & has collaborated with the CERN group in FY13 during 2 visits tacked onto trips made under other funding.
  CERN has invited Alan to apply for a 3-year associate position
Baseline LARP plan is to continue at this low level of travel funding and to develop a SLM based halo monitor after primary functionality of SLM at 7 TeV is achieved

## Slide 9: Horizontal Interference, Monte Carlo, εn = 1 µm

## Slide 10: Horizontal Interference, Monte Carlo, εn = 10 µm

## Slide 11: Irradiation of Collimator Materials
CERN will install a “Phase 2 Secondary” collimator made of an advanced material in one of the reserved LHC slots during Xmas shutdown 2015. They need to decide on material in ~June 2014.
Current front-runners:
In late 2012 (strongly) requested LARP to fund BNL BLIP+Hot Cell facility to measure physical properties before and after irradiation. $252k in FY13 and $180k in FY14 allotted, mostly for facility charges. FY14 $ transferred to Crab. Discussions with CERN ongoing as to how to replace funding.
Moly-Graphite/Carbon Fibers coated with Moly
Cu-Diamond Composite

## Slide 12: BLIP + Hot Cell + Analysis
Samples Studied:
Molybdenum
Glidcop
Cu-CD
Mo-GrCF
Features:
Irradiation w/ 200MEV p+
Indirect water cooling of vacuum encapsulated samples
Sample degradation vs. dpa
Thermo-physical & mechanical characterization of irradiated samples for fluence up to 1020 p/cm2
Irradiation w/neutrons to simulate showers on secondary collimators
200 MeV p+ from Linac
CERN provided materials & mechanics & FLUKA study
Nick Simos in charge at BNL: calculations, approvals, running, testing

## Slide 13: Status of Irradiation Study
Damaged capsules replaced by SS degrader with a new capsule support that allowed larger water channels
Irradiation continued in 2013 & is now 60% complete
Restart 3.5 week irradiation BLIP asap (~18 Feb at last check; safety review passed)
After cool down, post irradiation study of physical properties of the 5 of 7 remaining samples
Neutron irradiation of a collection of new samples in a new target holder (downstream of the isotope production target)
Capsule with Mo-Gr failed due to thermal stress & adjacent Cu-CD capsule damaged
2013 run halted to extract target box

## Slide 14: The LARP Rotatable Collimator Prototype Candidate for a Phase II Secondary Collimator
2012 DOE Review:
“Very quickly bring the effort on the rotatable collimator activity to an orderly conclusion. This should be done by the end of calendar 2012.”
1E-13
P=3.1E-8 Torr at RGA & 1E-6 Torr at CCG
It is with my great pleasure that I inform you that today we opened the box that you sent with the SLAC collimator prototype! The hardware seems in very good order at least from the outside visual inspection. See some pictures in attachment. Thank you very much for your continued effort that has allowed this important achievement! We will soon come to a detailed proposal of the tests that we will want to do here before setting up tests with beam - I have already organized a meeting tomorrow with the key teams involved to finalize the preliminary plan that we discussed at Daresbury. Best regards and many thanks again,

## Slide 15: Improvements to 2nd Prototype
Cooling coil wound into over-deep grooves & protected with shims
Glidcop machined with required features, especially those to mount the “RF bearing”, and “flashed” with copper for braze to mandrel

## Slide 16: New Ceramic Main Bearings with Restraint Clip 2011 version W-S2 impregnated SS; falls of shaft during bake
“Naked” Hub Screwed to Axle
Bearing on Hub
Spacer Ring & Bearing in Housing
Bearing Restraining Clip
Ring, Bearing in Housing & Clip
Oversize Outer Housing w/ Flats that prevent rotation in jaw supports

## Slide 17: New RF Bearing Assembly 2011 version used custom race with 1mm Rhodium coated balls
Ceramic bearing in race & the 2 rings that capture it
Assembled bearing package that will hold the RF Foil
Trapped bearing in ring that is fixed to the collimator jaw
Attaching outer ring to collimator
Close-up of ridge
where bearing rolls
Before outer ring screwed on

## Slide 18: Welding Flanges Attached to Tank Cover and Baseplate Make up saw kerf from proto I and permit multiple weld/grind/weld

## Slide 19: Design, Fab, Install, Adjust & Test Flexure to Precisely Set Actuator Height (can always be accessed through openings in tank and adjusted if needed)
Thermistor Port

## Slide 20: Leak Testing after Flange End Welded
Hardware | Pressure @ Pump (Torr) | Leak Rate (Torr-l/sec) | Leaks
He Leak Tester | 6E-6 | 6E-6 | 2 CuSil Pinholes 1 Flange Pinhole
RGA Turbo Cart w/20 l/sec Ion Pump | 6E-8 | 1E-11 | 1 CuSil Pinhole
 | 2.1E-8 | 1E-13 | No leaks

## Slide 21: Plasma Cleaning then Pump w/RGA Turbo (only) Over Weekend
1 hour O2 then 2 hours H2
Plasma at antenna
1E-13
After ~70 hours
1E-13
24
48
72
P=3.1E-8 Torr at RGA & P=1E-6 Torr at CCG

## Slide 22: Water Fittings: Flow & Pressure Test
Pressure(in) =50psi
Pressure(out) =8psi
Pressure drop =2.8 bar
Flow =2.1 gal/m
=8 liter/m
Pressure(static) =360psi
=24 bar
CuSil Metric Swagelok

## Slide 23: Final Tube Vacuum & Facet Rotation Tests
8 rotations of 48 tooth wheel (384 total) rotates 1 facet = 360°/20=18°
1 click = 818µrad → 16µm over 20mm facet width; 160nm over beam size
Each Jaw Rotated “2+0/8+0/48” Facets
“Pawls” at scribed “∆” when facets plumb; visible if RF foils end unscrewed
Scribed centerline on each facet visible in windows at either end
Each jaw moved 29.6mm from OLS

## Slide 24: Current CERN Test Plan
CERN has identified scientific & technical personnel & purchased a dedicated controls test stand for use by RC
Vacuum test by vacuum group (prep began 2014-02-12)
  Replace transport flanges & plastic immobilization parts; clean plastic debris
  Install two SLAC-made BPM fixtures w/ 8 LHC BPMs and standard blank vacuum flanges covers
  Leak-check, vacuum bakeout and RGA measurement: Determine if eventual vacuum meets LHC standards; if not, determine if it is good enough for a SPS test; if so, plan for an SPS test
Rotation & metrology tests
  cable to motor stepper controllers, LVDT and switch readout and confirm normal translation is possible
  verify state of health of the motors
  "standard" set up of switches, hard stops, etc.
  metrology tests without rotation
  rotation tests
  more metrology tests
Wire impedance tests
SPS tests
Eventually destructive HiRadMat beam tests followed by radiation cool-down followed by metrological exam

## Slide 25: Charges to Reviewers Relevant to Accelerator Systems
Evaluate
The quality and significance of the LARP scientific and technical accomplishments, and the merit, feasibility and impact of its planned development program
  The brief presentation attempted to convince the reviewers of the quality of the accelerator system program
The effectiveness and appropriateness of the laboratory interactions to maximize the leveraging of existing infrastructure and expertise available at those laboratories.
  While most accelerator system efforts are centered at one US lab, in all cases there is close communication and collaboration with CERN

## Slide 26: Accelerator System Out-Year Budgets
A “flat budget” would fund current ~1.4 FTEs and 50k travel.
  Cutting this would not add much to a big budget task
  Cutting this would remove the US from much of the intellectual involvement at the energy frontier of accelerator science
Accelerator Systems provides the fertile ground from which new ideas and projects come.
  Crab & WBFB “projects” originated here
  Strong involvement in collimation remains
  Beam studies and lattice work above & beyond application to LARP deliverables valuable and appreciated
  LARP instrumentation hardware in use daily
Cross fertilization goes both ways
  Ex: crystal channeled 6 GeV e- beam at SLAC
    Application to ILC collimation & Gamma ray source

## Slide 27: In case you hadn’t seen this ….
Thank you for your attention!