## Slide 1: Superconducting Solenoid-Based Focusing Lenses for HINS Linac
I. Terechkine
AAC Meeting
November 16-17, 2009

## Slide 2: Outline
Basics of solenoid focusing, requirements, and R&D structure
RT section lens
S/C sections lenses
Cryomodule design approach
Summary
2

## Slide 3: Why Solenoid Lens?
One focusing element provides axially symmetric focusing – important for high intensity beams.
The beam loss is governed by emittance growth and halo formation due to non-linear effects in the low energy sections (  << 1 ), where Coulomb forces are strong. Solenoids provide smooth axially symmetric focusing that helps to limit emittance growth.
3

## Slide 4: How it works
1. Radial component of a fringe field combined with asymmetric particle rotation provides radial component of the particle velocity;
2. Rotation in the longitudinal field results in different azimuthal position of the particles after the lens.
Focusing length:

## Slide 5: Requirements

## Slide 6: Project Structure

## Slide 7: RT Section Lens
RT CH Section
MEBT
Cryogenic Line
Chopper
RT CH Cavities (16)
Solenoids (19)
2.5 MeV
10 MeV
Buncher Cavities (2)

## Slide 8: Lens Design
HTS leads.
Helium line.
Vacuum relief.
Instrumentation
/ access port.
Support post.
Thermal shield (80K).
Power lead 80K anchor.
LN2 line for shield and HTS leads.
Solenoid magnet with helium vessel.
Conduction cooled copper lead.
Removable lead cover.
18 inch (457 mm) diameter vessel.

## Slide 9: Lens Fabrication
Corrector Assembly

## Slide 10: Lens Performance
CH SOLENOID PRODUCTION STATUS:
13 Type-1 (without Steering Dipoles): 11 tested
10 Type-2 (with Steering Dipoles): 9 tested
Quality Assurance Re-testing at Fermilab
First 4, then 1 of every 4: 4 T2, 3 T1 done; two tests pending
Type-1
Type-2

## Slide 11: Lens Testing
MTF: Stand-3
MTF: Stand-6

## Slide 12: Superconducting Section Lenses
Cold bore design
Corrector field quality
10-5 T fringe field
Alignment issues
I = 190 A

## Slide 13: Dipole Corrector

## Slide 14: Fringe Field Test
Focusing field at solenoid center: 5 T @ 160 A
Requirement for field at cavity surface: <10 µT @ 225 mm
Testing new shielding material from Amuneal

## Slide 15: Fringe Field Test

## Slide 16: Alignment Requirements
Alignment requirement: +/-150 µm (with dipole correctors (B*L ~ 0.5 T-cm) and sensitive BPM)
Cryogenic environment: vacuum + low temperature
Must allow reproducible assembly on an insertion bench (clean room) and in the cryomodule
Must allow reliable measurements on the beam line
Promising approach – optical alignment scheme

## Slide 17: Optical Alignment
CCD Camera: 1 µm resolution
Corner Reflector

## Slide 18: Alignment R&D
Proof-of-principle test has been made – OK
Alignment scheme bench test in preparation
Test cryostat for SS-1 lens certification and for the alignment concept verification by comparison with other alignment methods
Prototype cryomodule with RF cavities to finalize assembly and alignment procedure. Testing with beam.

## Slide 19: Test Cryostat Concept
Existing cavity test cryostat design
Warm bore to allow stretched wire technique
Laser-based alignment system
Modified position of the current lead assembly
Prototypes cryomodule design

## Slide 20: Conclusion
Designs of all focusing lenses for the HINS linac have been completed (including ones with embedded dipole correctors); test methods have been developed; lens performance is well understood.
Room temperature section lenses are in the final production stage; embedded BPM feature is being implemented.
Lenses for superconducting cavity section are in the final prototyping stage (test of a pre-production lens is ongoing).
Developed fringe field measurement method can be used to verify shielding efficiency in any RF cryomodule.
Suggested alignment method is beneficial for any linear superconducting accelerator.
Testing solenoid-base transport channel is of general importance for accelerator physics.

## Slide 21: Acknowledgments
Participant List:
G. Davis, C. Hess, F. Lewis, S. Sanchez, T. Wokas, Y. Huang, D. Orris, T. Page, R. Rabehl, W. Schappert, D. Sergatskov, M. Tartaglia, I. Terechkine, J. Tompkins.
Support from departments: D&D, Q&M, T&I, MS, and SRF.
Publication list – 52 inputs