## Slide 1
CLIQ tests on SQXF at FNAL
Emmanuele Ravaioli
LARP Collaboration Meeting
13 May 2015

## Slide 2
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
Main objective
Assessing the performance of a CLIQ-based protection system in conditions closest possible to the full-size case.
Goals
Test CLIQ performance -Different at low and high current
Verify correct choice of the optimum configuration
Compare performance 1-CLIQ vs 2-CLIQ
Further validate existing model of a CLIQ discharge
CLIQ tests on SQXF at FNAL

## Slide 3
Optimum CLIQ discharge configuration
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
Optimized
Not Optimized
Significant increase of CLIQ effectiveness (2.5-3 times)
Significant reduction of Leq (2.5-3 times)
→ Increase of deposited loss (6-9 times!)
→ Increase of oscillation frequency (1.5-2 times)
+
+
–
–
+
–
–
+

## Slide 4
1-CLIQ or 2-CLIQ
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
2-CLIQ
1-CLIQ
Parameter | 1 CLIQ | 1 CLIQ 2xU0 | 1-CLIQ, 2xU0, C/2 | 2 CLIQ
Equivalent inductance, Leq | Leq | = | = | ÷4
Total capacitance, Ceq | C | = | = | x2
Charging voltage, U0 | U0 | x2 | x2 | =
Peak current change, dI/dt | U0/Leq/NE | x2 | x2 | x2
Peak deposited loss | ∞(U0/Leq/NE)^2 | x4 | x4 | x4
Peak AC current, I | ∞U0*sqrt(Ceq/Leq)/NE | x2 | x20.5 | x20.5
Frequency, f | 1/2/π/sqrt(Leq*Ceq) | = | x20.5 | x20.5
Same performance

## Slide 5
Scaling of CLIQ performance
E. Ravaioli - TE-MPE-TM 15 April 2015
  CLIQ effectiveness
  → Coil geometry
  → Position of CLIQ connections
  → Electrical order of the poles
  → Conductor parameters
  → etc…
At high current
Low energy needed to start the quench
High energy density, needs to be quick!
 POWER is the key parameter
At low current
High energy needed to start the quench
Low energy density, velocity not critical
 ENERGY is the key parameter
(Number of CLIQ units)^2
(Charging voltage)^2
(magnetic length)^-2 (fixed by design)
Number of CLIQ units
(Charging voltage)^2
Capacitance of each unit
(magnetic length)^-1
Magnetic length
# of CLIQ units
Capacitance

## Slide 6
How to choose the settings of the CLIQ system?
Name | Magnet length [m] | Configuration | NC | C [mF] | U0 [V] | E [kJ] | E/length wrt baseline | Pif/vol wrt baseline | ∞f wrt baseline
Baseline 1-CLIQ | 7.15 | Pole-Pole | 1 | 30 | 1000 | 15.0 | 2.1 | 19561 | 0.3
Baseline 2-CLIQ | 7.15 | Pole-Pole | 2 | 60 | 500 | 15.0 | 2.1 | 19561 | 0.2
SQXF-PP-1C-01 | 1.5 | Pole-Pole | 1 | 80 | 500 | 10.0 | 3.2 | 5.7 | 1.3
SQXF-PP-1C-02 | 1.5 | Pole-Pole | 1 | 80 | 210 | 1.8 | 0.6 | 1.0 | 1.3
SQXF-PP-1C-03 | 1.5 | Pole-Pole | 1 | 80 | 280 | 3.1 | 1.0 | 1.8 | 1.3
SQXF-PP-1C-04 | 1.5 | Pole-Pole | 1 | 40 | 500 | 5.0 | 1.6 | 5.7 | 1.9
SQXF-PP-1C-05 | 1.5 | Pole-Pole | 1 | 40 | 210 | 0.9 | 0.3 | 1.0 | 1.9
SQXF-PP-1C-06 | 1.5 | Pole-Pole | 1 | 40 | 397 | 3.1 | 1.0 | 3.6 | 1.9
SQXF-PP-2C-01 | 1.5 | Pole-Pole | 2 | 80 | 500 | 20.0 | 6.4 | 22.7 | 1.9
SQXF-PP-2C-02 | 1.5 | Pole-Pole | 2 | 80 | 105 | 0.9 | 0.3 | 1.0 | 1.9
SQXF-PP-2C-03 | 1.5 | Pole-Pole | 2 | 80 | 198 | 3.1 | 1.0 | 3.6 | 1.9
SQXF-PP-2C-04 | 1.5 | Pole-Pole | 2 | 40 | 500 | 10.0 | 3.2 | 22.7 | 2.7
SQXF-PP-2C-05 | 1.5 | Pole-Pole | 2 | 40 | 105 | 0.4 | 0.1 | 1.0 | 2.7
SQXF-PP-2C-06 | 1.5 | Pole-Pole | 2 | 40 | 280 | 3.1 | 1.0 | 7.2 | 2.7
SQXF-ULP-1C-01 | 1.5 | Up-Low-Pole | 1 | 80 | 500 | 10.0 | 3.2 | not optimized | not optimized
SQXF-ULP-1C-02 | 1.5 | Up-Low-Pole | 1 | 40 | 500 | 5.0 | 1.6 | not optimized | not optimized
SQXF-ULP-1C-01 | 1.5 | Up-Low-Pole | 2 | 80 | 500 | 20.0 | 6.4 | not optimized | not optimized
SQXF-ULP-1C-02 | 1.5 | Up-Low-Pole | 2 | 40 | 500 | 10.0 | 3.2 | not optimized | not optimized
New CLIQ units: C=40 or 80 mF, U0=50-500 V
CLIQ units for 7 m MQXF: C=30 mF, U0=1000 V

## Slide 7
Wish list (7 full sweeps, 5 low-current sweeps, ~50 tests)
Config | #units | U0 [V] | C [mF] | I0 [A] | Motivation
Opt | 1 | 200 | 80 | Full sweep* | Same peak power of MQXF-7m
Opt | 1 | 200 | 40 | Full sweep* | Useful for model validation
Opt | 1 | 100 | 80 | Full sweep* | Same peak power of MQXF-4m
Opt | 1 | 100 | 40 | Full sweep* | Useful for model validation
Opt | 1 | 300 | 80 | Low sweep** | Same energy density of MQXF-7m
Opt | 1 | 400 | 40 | Low sweep** | Same energy density of MQXF-7m
Opt | 1 | 200 | 80 | Low sweep** | Same energy density of MQXF-4m
Opt | 1 | 300 | 40 | Low sweep** | Same energy density of MQXF-4m
Opt | 1 | 500 | 80 | Full sweep* | Ultimate performance
Not-Opt | 1 | 500 | 80 | Full sweep* | Study of not optimized config, model validation
Opt | 2 | 100 | 80 | Full sweep* | Same peak power of MQXF-7m, 2-CLIQ option
Opt | 2 | 200 | 80 | Low sweep** | Same energy density of MQXF-7m, 2-CLIQ option
*Full sweep: from about 2 kA to ultimate, in 5 steps; **Low swep: two low current levels (2 and 5 kA?) |  |  |  |  | 

## Slide 8
Simulations – CLIQ on 1.5 meter long QXF magnet – 500 V
2-CLIQ, 2x80 mF, 500 V
1-CLIQ, 1x80 mF, 500 V

## Slide 9
Goals: Obtaining meaningful data while still assuring redundancy of the protection during the tests in the case of CLIQ misfiring (fully redundant CLIQ possible, but not during these tests; modifications to the unit design is under study)
Option 1: EE delayed
Pros: The resistance growth in the coil is only due to CLIQ (but quench-back is still present)
Cons: (especially at low current) the discharge is dominated by the EE; interaction between CLIQ and EE to be carefully considered
Option 2: IL QH delayed
Pros: Cleaner currents to analyze; in the outer layer, relatively easy to assess CLIQ performance
Cons: Maybe not very clear if the inner layers are quenched by CLIQ or QH
Option 3: IL+OL QH of only two poles (ideally OL QH of two poles, safe?)
Pros: Cleaner currents to analyze; direct comparison between performance of CLIQ and CLIQ+QH (partly biased since the current discharge is faster than with CLIQ only)
Cons: Careful study of the voltages to ground needed (asymmetric quench).
What is the best option for effective CLIQ tests?
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015

## Slide 10
2 CLIQ units are being manufactured at CERN specifically for these tests; they will be ready at the end of May/beginning of June (tests at CERN needed before shipping to the US)
A few issues to discuss (off-line)
Reverse diode string across the power supply
Reverse diode string across the energy-extraction system
Connections
Triggering signals
Integration of new CLIQ units at FNAL test facility
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015

## Slide 11
Annex
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015

## Slide 12
Circuit diagram of FNAL test station
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015

## Slide 13
CLIQ units for FermiLab – Main functional requirements
Main Funcional requirements | MQXF l=1.2 m | MQXF l=4.0 m | MQXF l=6.8 m
Maximum charging voltage [V] | 500 | 500 | 500
Capacitance [mF] | 80 | 80 | 80
Maximum stored energy [kJ] | 10 | 10 | 10
Internal resistance [mOhm] | <5 | <5 | <5
Max triggering delay [ms] | 1 | 1 | 1
Triggering delay (preferred) [ms] | 0.2 | 0.2 | 0.2
Expected peak current [kA] | 6.6 | 3 | 2.5
Expected frequency [Hz] | 30-50 | 15-25 | 10-20
Time before fully discharge unit [ms] | 50 | 100 | 200

## Slide 14
1-CLIQ or 2-CLIQ
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
2-CLIQ
1-CLIQ
Very similar performance expected, but 1-CLIQ:
More reliable (less components)
Avoid synchronization problems
Reduce the impact of various fault scenarios
Gives the same peak voltage to ground

## Slide 15
CLIQ – Coupling-Loss Induced Quench protection system
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
Current Change
Magnetic Field Change
Coupling Losses (Heat)
QUENCH
Temperature Rise
Patent EP13174323.9

## Slide 16: Summary of CLIQ and QH performance on the model magnet
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
At nominal current quench load reduced by ~30% using CLIQ
However, CLIQ performance strongly depends on the magnet length

## Slide 17
CLIQ – Typical discharge
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
Excellent agreement between simulations and measurements

## Slide 18
Testing CLIQ – Nb3Sn model magnet for HL-LHC (HQ02b)
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
First CLIQ tests on a Nb3Sn magnet

## Slide 19
Optimizing CLIQ – Examples of possible configurations
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
Different configurations can be obtained by varying the electrical order of the poles and the positioning of the CLIQ terminals

## Slide 20
Optimizing CLIQ – CLIQ effectiveness, Ѱ
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
CLIQ effectiveness, Ѱ
Introduced magnetic-field change, per unit of charging voltage and magnet length

## Slide 21
Designing CLIQ – Simulated CLIQ on a 7 m long MQXF
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
Temperature
Voltage to ground

## Slide 22
Protecting full-scale magnets with CLIQ – The strategy
Power per unit volume deposited by CLIQ depends on inter-filament loss (IFCL)
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
Charging voltage
(limited for safety reasons)
Equivalent inductance
of the discharge circuit
  → Coil geometry
  → Position of CLIQ connections
  → Electrical order of the poles
  (always an advantage, typically possible with minor changes)
Magnet length
(defined by design)
Number of CLIQ units
(for quadrupoles up to 2 units)
Capacitance of CLIQ unit
(no effect on power, but
to discharged energy)
For a given quadrupole magnet
Choose optimum CLIQ configuration
Increase voltage U0
2-CLIQ
Increase capacitance of CLIQ unit(s)

## Slide 23
1
2
3
4
1
2
3
4
Optimum CLIQ discharge configuration -2
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
[a.u.]
[a.u.]
Golden rule for optimizing any CLIQ discharge circuit
Introduce opposite current change in coils which are physically adjacent
Efficient distribution of magnetic-field change
Optimized
Not Optimized

## Slide 24
Multi-CLIQ
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
Further decreasing the impedance of the circuit can be reduced by subdividing the electrical circuit into 2xNC elements, effectively in parallel when CLIQ is triggered.
1-CLIQ
2-CLIQ

## Slide 25
Simulation results – I0 = 17.3 kA (Inom)
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
Assumptions: no QH; no EE; RRR=140;
10 ms detection time
For each studied configuration a minimum capacitance is needed to protect the magnet
As expected performance of
2-CLIQ-500 V
similar to 1-CLIQ-1 kV
MQXF
Magnetic Length 6.8 m
Self-inductance 70 mH
Nominal current 17.3 kA
Quadrupole magnet for the LHC high luminosity upgrade
(US-LARP collaboration)

## Slide 26
Simulation results – I0 = 9 kA (~50% Inom)
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015
1-CLIQ-500 V
is not sufficient to protect the full-length magnet
Both 2-CLIQ-500 V
and 1-CLIQ-1 kV are valid protection solutions for C>50 mF
Assumptions: no QH; no EE; RRR=140;
10 ms detection time

## Slide 27
CLIQ – Coupling-Loss Induced Quench
Current
Change
Magnetic Field
Change
Coupling-Losses
(Heat)
QUENCH
Temperature
Rise
Principle: When subjected to a magnetic field change, coupling losses occur in superconducting wires and cables. These losses are heat generated directly in the superconductor to quench!
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015

## Slide 28
Why do we need to delay the triggering of the extraction-system?
Avoid interference between CLIQ and EE system
  Avoid superposition of voltage across CLIQ and across EE resulting in voltage too high
  Avoid reducing CLIQ performance
Emmanuele Ravaioli - CLIQ tests on SQXF at FNAL LARP Collaboration Meeting - 13 May 2015