## Slide 1: Instrumentation Frontier Summary Ronald Lipton, Fermilab for Marcel Demarteau, Howard Nicholson, Ian Shipsey, speakers, conveners and liasions
Marcel defined our aspirations last week
Our vision is for the US to have an instrumentation program for particle physics that:
  Enables the US to maintain a scientific leadership position in a broad, global, experimental program
  Develops new detection capabilities that provides for cutting edge contributions to a world program
Our goal for Snowmass was to develop that vision by establishing the physics needs for future instrumentation in each frontier, technological opportunities, and possible paths forward

## Slide 2
Over the last week we have interacted with the 3 physics frontiers, discussed cross cutting technologies, and argued about how to best achieve our goals
Remarkable vitality demonstrated in presentations and whitepapers
Outstanding ideas
Great opportunities
Critical needs
Worry about opportunities slipping away
Instrumentation Frontier Whitepapers
Energy Frontier
Level 1 Track Triggers at HL-LHC
Tracker and Vertex Detector for a Muon Collider
Operation of Collider Experiments at High Luminosity
Noble Liquid Calorimeters
Triggers for hadron colliders at the energy frontier
A Differential Time-of-Flight Technique for Collider Detectors
Hadronic dual-readout calorimetry for high energy colliders
Atlas Upgrade Instrumentation
Trigger and Data Acquisition for hadron colliders at the Energy Frontier
Cosmic Frontier
Instrumentation Needs for Detection of Ultra-high Energy Neutrinos
nEXO Detector R&D
Large Arrays of Air Cherenkov Detectors
Low Background Materials for Direct Detection of Dark Matter
Dark Energy
Future Atmospheric and Water Cherenkov gamma-ray Detectors
Physics Motivation for WIMP Dark Matter Directional Detection
Direct Detection of WIMPs
Solid Xenon R&D at Fermilab
Applications of Laser Interferometry in Fundamental Physics Experiments
Instrumentation for New Measurements of the Cosmic Microwave Background polarization
A readout architecture for 100,000 pixel Microwave Kinetic Inductance Detector array.
Intensity Frontier
Advanced Water Cherenkov R&D for WATCHMAN
Liquid Argon TPC
LHCb Upgrade
Neutrino Detectors Working Group Summary
Electromagnetic Calorimetry in Project X Experiments
Liquid Scintillator Instrumentation for Physics Frontiers
Intensity Frontier Instrumentation Summary Report
Technologies
Combination of Active Edge and 3D Electronics Technologies
Plasma Panel Detectors for Ionizing Particles
3D Sensor Architecture
Development of Resistive Plate Chambers
Powering Future Particle Physics Detectors
Imaging Calorimetry
Future Crystal Electromagnetic Calorimetry
Development of Cost-effective Crystals For Homogenous Hadron Calorimetry
Application Specific Integrated Circuits (ASICs) for HEP applications
The Next Generation of Crystal Detectors
Use of Flat Panel Microchannel Plates in Sampling Calorimeters with Timing
Micro-Pattern Gas Detectors for Charged-Particle Tracking & Muon Detection
Low Mass Support and cooling (1 page)
Low Mass Support and Cooling for Future Collider Tracking Detectors (long)
Monolithic Pixel Sensors
High speed, massively parallel, ATCA based Data Acquisition Systems using modular components
The Next Generation of Photo-Detectors for Science in the Cosmic, Intensity and Energy Frontiers
Future Developments in Gigasample-per-second Waveform Sampling Application Specific Integrated Circuits
Micro-Pattern Gas Detectors for Calorimetry
Emerging Optical Link Technologies for HEP
Opportunities for HEP Technology Evaluation in Smaller-Scale NP Experiments
Synergies Between Detector Development in Nuclear and Particle Physics
Diamond Sensors
3D Technologies for Large Area Trackers
Secondary Emission Calorimetry: Fast and Radiation-Hard
Quartz Capillary Cladding Anthracene and Polycyclic Aromatic Hydrocarbon(PAH)-Core Scintillating/WLS Fibers for High Rates and Radiation Damage Resistance
Novel Compact Accelerator-Based Neutron and Gamma Sources for Detector Calibration
Ultra-Low Index and Rad-Hard Total Internal Reflection Claddings for High Numerical Aperture Scintillating, Waveshifting, Cerenkov, or Clear Optical Fibers, Capillaries, and Plates
Facilities
Irradiation Facilities at Fermilab
Irradiation Facilities in New Mexico
Beam Test Facilities

## Slide 3: Leadership
My favorite definition in this context
“having both a vision and the ability to execute that vision”
Visions:
Scientific vision from the frontiers
Technology vision from the scientists
Engineering vision from the equipment designers
Enabled by:
Scientific instrumentation
  Technical capabilities
  University and laboratory infrastructure
  Engagement with industry
$$

## Slide 4: Progress in Experimental Science
Incremental: Utilize improvements in in the commercial world to improve science reach. Modify current detectors.
Opportunistic: Add developments in other fields like material science and nanotechnology to utilize new materials, optimize designs.
Developmental: Develop technologies and infrastructure to enable specific experiments
Transformative: Programs that allow strategic investments in novel technologies that make future experiments affordable, effective, and improve physics reach
Intel won’t help you with this

## Slide 5
Review of Particle Properties
(1978)
Review of Particle Properties
(2011)
New

## Slide 6
Project Driven
SiPMs for LHC HCAL
Cold Electronics for LBNE
CCDs for LSST
ATCA systems for LHC
Generic
Large area photodetectors
3D electronics
SLAC test beam
Crystal calorimetry
Here in Frontierland our R&D is divided into project-driven and generic.
Projects develop technologies necessary for a specific experiment. They do not maintain infrastructure and cannot afford to take substantial risks. Generic R&D has fewer constraints. Both are needed.

## Slide 7
Project driven Detector R&D and typically project funded.
This is NOT generally funded by the generic Detector
R&D program at DOE.
Generic Detector R&D which is motivated by common
needs in instrumentation among several experiments
or which may increase reach or reduce costs of
future HEP experiments. Examples: Lab KA25 funding,
University ADR program, SLAC test beam, water based
liquid scintillator, compensated calorimetry, ILC detector
R&D including particle flow.
Transformational Generic Detector R&D and grand
Challenges at the multimillion dollar level. Examples:
LAPPD, large area, low radioactivity, photodetectors
with high efficiency at LAr and LXe scintillation
wavelengths, wavelength sensitive pixels for astrophysics.

## Slide 8
Generic R&D Program | Status | Characteristics
Water Based Scintillator | Ready for test deployment | 7x cheaper than oil base
Large Area Photodetectors | 1st prototype under test | Utilize microchannel plates and ALD for fast, large area
SLAC Test Beam | Available | Pulsed electron beam
High Speed optical modulation | Considered for ATLAS | 106 lower error rate than vxcels, rad hard, low power
High Pressure Xenon Gas | Data evaluation | Possible nuclear recoil direction detector
3 Dimensional Electronics | Demonstration MP run complete | Stack heterogeneous layers of electronics and sensors
Liquid Argon Purity | Complete | Test materials for LA systems
Compensated Calorimetry | In progress | Hadron calorimetry resolution improvement
Digital Hadron Calorimeter | Complete, data analysis | Imaging calorimetry
QUPID Phototube development | Prototype | Procured by Hamamatsu

## Slide 9: Liasons and Conveners
Thank you for the
great job

## Slide 10: Diagonalization
  We will see how these themes emerge from physics needs at the Frontiers
Technology | Implementation
Pixelization | Silicon pixels, MKIT, CCD, LAPPD, MSGC->large area
ASIC and electronics | Everywhere…
Trigger and DAQ | Stream everything if possible, intelligent front ends
Mechanics and power | Low mass materials, foams, power conversion
Photosensors | SiPM, MCP, Cathodes-> large area, fast
Speed | Fast silicon, crystals, photosensors, electronics
Resolution | Crystals, dual readout or PFA calorimeters,
  Some of the following discussion may seem diffuse, but there are strong themes that pervade the technologies and frontiers

## Slide 11: Technologies across boundaries
Time Projection Chambers
Cryogenic detectors
Semiconductor detectors
New materials and process technologies
Engineered Crystals
Detection of dark matter
Measuring the Higgs
Searching for new physics
At the energy frontier
Establishing the properties of Neutrinos and dark matter with large volume detectors
Testing physical laws in rare decays

## Slide 12: Energy Frontier – LHC
Focused Challenges:
Maintain detector performance in the presence of 140 int/xing
  Low mass tracking
  Fast timing
  DAQ
Extend forward calorimetry and tracking to h=4 for WW scattering and HH studies
Radiation hardness
Technology | Need | Implementation
Pixelization | Lower occupancy Track primitives | Tracker segmentation Track stubs, ROI
ASIC and electronics | Inner pixel IC | 65 nm rad hard designs Low power design
Trigger and DAQ | Track triggers High BW optical | Assoc. memory Mach Zender modulators
Mechanics and power | Cable mass Cooling to -25 deg | DC-DC/serial power Co2, carbon foams
Photosensors | Rad hard compact sensors | SiPMs
Speed | isolate primary vertex | 10 ps resolution tof
Sensors | Rad hard, pixelated | Thin silicon 3D silicon diamond

## Slide 13: Energy Frontier LHC (Heintz)
Dealing with pileup
Higher bandwidth and latency
Add track information to L1
  Pixelization
  Intelligent trackers (ROI or standalone)
Isolate primary vertices
  By timing
  By tracking
Extend forward coverage
Pixelated calorimeters
Forward disks
Fast timing
y
z
“stub”
x
CMS
Track
Trigger

## Slide 14: Energy Frontier Challenges in e+e- – ILC/CLIC (Stanitzki)
LHC

## Slide 15: LC Initiated Technologies
Digital HCAL
Bump bond pad
6 micron thick top silicon
4 micron pitch
Interconnect
array
3D Vertex
Detector
electronics
Dual
Readout
Calorimeter
Particle
flow

## Slide 16: Energy Frontier -Muon Collider (Mazzacane)
The muon collider is a possible path to a multi-TeV lepton collider
Can we do physics in the huge backgrounds from beam decay?
Full simulation of beam backgrounds combined with physics simulation and reconstruction
Hundreds of TeV/crossing
But backgrounds are soft and out of time
1 ns time cut reduces tracker background by 103!
Pixelate to reduce occupancy
1-10 ns cuts reduce background x 100 in calorimeter
108
Fast Timing
100 ns

## Slide 17: 1.5 TeV H/A
The first physics study to address muon collider backgrounds with full simulation
s-channel H/A->bbbar production in a 1.5 TeV muon collider.
Full GEANT/MARS backgrounds
4.6% dijet mass resolution with background
(Eichten)

## Slide 18: Cosmic Frontier Challenges
Broad, program with significant opportunities for progress
UHE cosmic rays and neutrinos
  Low rates at high energy require large exposures/aperture to make progress
Gamma rays
  R&D: Cherenkov and water tank arrays, Low-cost photosensors/low-power digitizers
  Distributed timing across large arrays
Dark Energy – next generation
  Order of magnitude improvement in sensitivity, ~km2 effective area, and extended energy
Dark Matter
  Almost every experiment is a new detector idea. There is a large program looking for larger mass, lower thresholds and directionality
CMB
  Large area spectrally sensitive arrays low power readout and high bandwidth DAQ

## Slide 19: Indirect Detection (Buckley)

## Slide 20: WIMP Direct Detection Instrumentation Needs (Cushman)
Radiopurity
  Photodetectors
  SiPMs, APDs, low radioactivity vacuum tubes improvements in solder/base, transparent windows, tube housing
  Applied to materials
  e.g. Cu, acrylic, poly, lead, components
  Neutron detection & shielding
Technologies
Cryogenic solid state – large masses, low energy deposition
77 K Germanium – lower noise, better resolution
Noble liquid – photosensors, HV delivery, single electron
Superheated liquid – new target liquids, radiopure acoustic sensors
Inorganic crystals = purification,
Directional detection – In gas, use columnar recombination?

## Slide 21: Cosmic Photosensors (Chang)
Can’t change flux of energy from the cosmos!
Increasing spatial instrumentation (larger volumes/areas, increased granularity)
Increasing energy bandwidth
Increasing readout throughput
Transition edge sensors for DM and CMB
Kinetic Inductance Detectors for spectrophotometry
Thick
CCDS

## Slide 22: Cosmic Frontier Common Technologies
Cryogenic detectors :
For CMB, Dark Matter and Dark Energy the new directions involve superconductor detectors.
We want transition edge sensors and MKIDs in large arrays
US leadership is clear in this area
SiPM Arrays:
DM, gamma rays, UHECR want large arrays of SiPMs. Maybe even for very fast astronomical imaging.
Low power readout and high bandwidth DAQ.
Good opportunity for organizing a coherent effort.
ASICs:
In many cases the future experiments involve large channel count, with power and density requirements. ASICs are the way to address this.
Need to keep this valuable resource in the labs and available to the university community.

## Slide 23: Intensity Frontier Instrumentation Needs
Calorimeters
  Fast (Mu2eLYSO, g-2PbF2, MEG LXe, ORKAPb-scint.)
  0 >99.9999% (K) with 4 fully hermetic photon detection
  KOPIO+ needs energy, time, position and direction
Trackers:
  Low mass (drift chambers, straws, Si)
  Good space/timing resolution
  Operation in vacuum (e.g. g-2, Mu2e, NA62/CKM straws in vacuum)
Massive Detectors:
  Need cost effective detection of scintillation or Cherenkov light
  Need cost effective detection of ionization electrons
DAQ
  sensitivity gains afforded by the high-level processing of all events
Simulations and Computing
  reasonably and economically steward 1-10 Peta-Bytes
  Include neutrino-nucleus interactions within GEANT4

## Slide 24: Intensity Frontier Precision
Needs for Photosensors (SiPM, MCP…)
g-2 - Dt/t for 2 showers
m->e – detection e, moderate rad hardness
ORCA – DE/E, Dt/t, low dark rate, high e
Need: large areas, lower cost, small form factor, lower dark count, active quench, rad hard, dynamic range.
Technologies: LAPPD, incremental development,
Digital 3D SiPM technlogy
Golden Modes
Muons: -Ne-N, g-2, +e+, EDM
Kaons: K
B: B , BKll, Bs, B

## Slide 25: Intensity Frontier- Neutrinos (Rebel)
Near term
High voltage - >50 kV
Light collection - provides t0, may be useful for reconstruction and calorimetry as well
Test beams
Fundamental Properties of Noble Liquids
How do ionization electrons behave during drift – diffusion, attachment, recombination?
How does the dielectric property of the liquid change with contamination?
How is light production and collection affected by contaminants?
How do the positive ions affect the electric field?
Long Term Priority - Magnetized LArTPC

## Slide 26: Intensity Frontier Recommendations
Development of large mass, cost effective detectors for neutrino detection and proton decay.
R&D on cost effective calorimeters with good photon pointing and time of flight (goal is <20mrad, 10ps).
R&D towards cost effective, high efficiency photon detection for kaon experiments (10-4)
Very fast, very high resolution photon/electron calorimetry for muon experiments (goal is 100ps, sub-percent energy resolution)
Very low mass, high resolution, high-speed tracking for muon,kaon, and light weakly coupled particle experiments (0.001 X0 per space point, 100ps per track)
High fidelity simulation of low energy particle interactions; strategies to effectively simulate >1012 particle decays & interactions.
High throughput, fault tolerant streaming data acquisition systems (goal of TB/second throughput to PB/year data storage)

## Slide 27: Use of ASICs (Haller)
ASICs are in most of the HEP experiments.
Essential to get science (size, performance, power, etc):
  ~ 50 ATLAS ASICs (currently < 15 with US participation)
  ~ 30 CMS ASICs (currently ~5 with US participation)
  ~ 6 LHCb ASICs (Europe based)
  ~ 40 ASICs for other experiments (~30 US based)
Intensity Frontier – LBNE
Cold electronics
“FEI5” 2X2 REGION (100X200)
FEI4 2X2 REGION (100X500)
If area to be kept the same as FEI4, about 4X more logic can be added
Energy Frontier – ATLAS Pixel
Large ASICS, collaboration
CTA high input bandwidth and sampling rate, calibration, low power.

## Slide 28: ASIC R&D
ASIC-related R&D is required in a number of areas in order to improve science output or simply make possible future experiments in the intensity, cosmic, and energy frontiers. Examples are:
  High-speed waveform sampling.
  Pico-second timing.
  Low-noise high-dynamic-range amplification and pulse shaping.
  Digitization and digital data processing.
  High-rate radiation tolerant data transmission.
  Low temperature operation.
  Extreme radiation tolerance.
  Low radioactivity processes for ASICs.
  Low power.
  2.5D and 3D assemblies.
  Power conversion/delivery.

## Slide 29: High Speed Systems (Varner)
Fast Timing traditionally
Particle Identification
Difficult, expensive, low-density, …
Next generation experiments
Rare processes -> background suppression
High statistics -> high event rates
High event rates -> pile-up, loss of signal purity
Some examples:
Next generation Particle ID
Reinvigorating older techniques
VH-LHC event pile-up
Even at trigger level
LHC IP time spread
Improvements in spatial and timing
information could enhance
background rejection and vertex
resolution in large water Cherenkov
detectors.

## Slide 30: Pixelization
MAPS
CCD
SOI
3D
Low mass, pixelated radiation hard detectors will be needed for ATLAS, CMS, an ILC, CLIC or muon collider in the energy frontier, and LHCb and next generation B or tau factories in the intensity frontier.
Often requires sophisticated in-pixel processing such as time stamping, cluster finding or inter-cell hit correlation.
Technologies:
Detector/electronics integration
Commercial wafer-scale processes
Microstrip gas detectors
70μm
140μm

## Slide 31: Photodetectors
Discussion of high speed, large area photodetectors and emitters pervaded our meetings.
New rad hard crystals with high light yield
Compact solid state photosensors (SiPM). Want them:
  cheaper, faster, quieter
  Can we build large arrays?
Replacements for PMTs
  LAPPD – large area microchannel plate based development - first article is being tested.
Spectral sensitivity
LAPPD
SiPM
Double beta
decay

## Slide 32: Crystals (Zhu)
Crystal challenges at future HEP Experiments:
Radiation damage at the energy frontier (HL-LHC);
Ultra-fast rate and γ-pointing at the intensity frontier;
Good jet mass resolution for future ILC/CLIC mC.
Compact, rad hard
Photodetectors
BAF2 – fast (@220nm), rad hard
segmented crystal calorimeters with more than ten times faster rate/timing capability using the sub-ns decay time of BaF2.
Homogeneous HCAL by reading both Cherenkov and scintillation light for PbF2, PbFCl and BSO.
Novel materials, such as crystals, ceramics and glasses, may play an important role in future HEP experiments.

## Slide 33: Trigger and DAQ
ALICE (post-LS2):Triggerless
Readout 50 kHz Pb-Pb (i.e. L = 6x1027 cm-1s-1), with minimum bias (pipeline) readout (max readout at present ~500 Hz)
ATLAS (post-LS3):Triggered
Divide L1 Trigger into L0, L1 of latency 5, 20 μsec, rate < 500, 200 kHz, HLT output rate of 5 - 10 kHz
L0 uses Calo & Muon Triggers, generates track trigger seeds
L1 uses Track Trigger & more muon detectors & more fine grained calorimeter trigger information.
CMS (post LS3):Triggered
Considering L1 Trigger latency, rate: 10 – 20 μsec, 0.5 – 1 MHz
L1 uses Track Trigger, finer granularity μ & calo. Triggers
HLT output rate of 10 kHz
LHCb (post LS2):Triggerless
Execute whole trigger
(Smith)

## Slide 34
CTA Camera
LSST
4000 x 3.2
Gb/sec
Mu2e
30 GB/sec
30 Tflop
LBNE
SuperKeKB

## Slide 35: Emerging Technologies (Alexander)
Micromachining – active edge sensors
Spectrally sensitive CCD
Quantum dot doping
3D Printed sensors
Micromachining
Cooling

## Slide 36
Large area photodetector Project
(LAPPD)
Atomic Layer deposition
Flex on
Polymer IC

## Slide 37: To the Third Dimension (RL)
Handle wafer
sensor
trenches
Buried
oxide
readout
IC and pads
200 micron
3D sensors, fast radiation hard,
Active edges
CMS – Use stack of 3D tiers to emulate tracker layers for CAM –based track recognition
Use 3D to connect each SiPM subpixel to quenching,
timing, and control electronics
Combine active edge and 3D
electronics to produce tiled sensors combined with ROICs for large area arrays
Use avalanche multiplication for fast, low power trackers

## Slide 38: Innovation
We have talked a lot about selling the field.
Spin-offs are a part of that story.
Investment in instrumentation has benefited x-ray science (accelerators, detectors), medicine (imaging systems), large scale computing, electronics, and supplied unique training… This requires investment and sometimes risk.
If we don’t continue to nurture that investment we will not only lose opportunities in our science but also opportunities to engage with our colleagues in other fields, broaden our appeal, and use our skills to benefit society
Rossi coincidence
circuit

## Slide 39: Challenges
One of our goals in this process is to define a path to transformative research which:
Has strong scientific impact
Is broadly applicable across areas within HEP
Can reduce costs of our experimental program
In addition the R&D would benefit if it:
Had impact beyond particle physics (spinoffs)
Exploits the strong capabilities within HEP/Labs/universities
We propose these as criteria for future judgments

## Slide 40: What if … with 1% Tax
We could build large area arrays of low mass rad-hard pixelated detectors at 20% of current costs with ns resolution?
We could build arrays of UV sensitive photo detectors with low noise and high quantum efficiency?
  Radio-pure too
We could measure hadron showers to 3% accuracy?
We could build focal planes of spectrally sensitive detectors?
We could build very large volume or very high field magnets?

## Slide 41: Statement
Innovation in instrumentation is central to discovery science. The field of high-energy physics has a long history of invention that has led to fundamental discoveries in particle physics and breakthroughs in many fields of science. In the 21st century multi-disciplinary research is where progress is being made. During the Snowmass process key strategic areas were identified for investment in cost-effective technologies that would enable the US high-energy physics community to maintain leadership and benefit the national interests. The community has established a Coordinating Panel for Advanced Detectors to foster these strategic advances in instrumentation by coupling the unique resources of the National Labs, our world-leading research universities and industry.

## Slide 42: Strategic Goals (Demarteau)
Develop more cost-effective technologies with increased reach
Develop balanced Instrumentation, based on our strengths, aligned with research priorities
Balanced funding level between projects and R&D and a program with appropriate “portfolio of risk”
Develop process for integrating universities, national laboratories, other branches of science and industry
Create opportunities for careers in HEP instrumentation
Identify opportunities for technology transfer and collaboration with other sciences
Fit more programs into this slice
Make slice bigger
Office of Science 2013 Budget

## Slide 43
CPAD Membership:
From Universities
  Jim Alexander, Cornell
  Marina Artuso, Syracuse
  Ed Blucher, Chicago
  Ulrich Heintz, Brown
  Howard Nicholson, Mt. Holyoke
  Abe Seiden, UCSC
  Ian Shipsey*, Purdue
  (*) co-Chair
From laboratories
  Marcel Demarteau*, Argonne
  David Lissauer, Brookhaven
  David MacFarlane, SLAC
  Ron Lipton, Fermilab
  Gil Gilchriese, LBNL
  Bob Wagner, Argonne
International
  Ariella Cattai, CERN
  Junji Haba, KEK
http://www.hep.anl.gov/cpad/

## Slide 44: CPAD (Shipsey)
Coordinating Panel for Advanced Detectors
Formed as a recommendation of the DPF Taskforce on Instrumentation
A standing body to “promote and assist in generic detector R&D”
CPAD was asked to oversee the Snowmass Instrumentation Frontier
CPAD has given priority to and is integrated into the Snowmass process.
CPAD work on:
Coordinating the national instrumentation program,
Coordination of instrumentation resources at National Labs for the HEP community
Development of interdisciplinary links, and links to industry
National Instrumentation Fellowships,
National Prizes
Is expected to begin as Snowmass concludes
We expect CPAD to help execute the vision initiated here

## Slide 45: Summary
This has been an exciting and exhausting week
We have explored physics needs and development opportunities
We have identified common thrusts
We have discussed ways to maintain a vigorous program with a mix of project and generic R&D, university, laboratory, and industrial involvement.
  This will not be easy
  The hardest part of having vision may be to sustain it. We are all busy, and have other pressing needs.
Execution of this vision will be up to CPAD, funding agencies, and us.
Investing in R&D is investing in the future of the field: in young people, in training, In university and laboratory infrastructure, in new technologies, in cost effectiveness and in technologies that will benefit other sciences, and produce spinoffs

## Slide 46: Backups

## Slide 47: Some other Examples from our meetings
Off detector data delivery of multi TB/sec tracker data
Large area low cost Pixelated detector systems
Spectrally sensitive focal plane detectors
Ground based IR astronomy from ground
Directional dark matter detectors at large scale with n floor sensitivity
UV photosensors
Scaling superconducting arrays for CMB
Hadron calorimetry with 3% DE/E
New manufacturing technologies for detectors
ps timing systems