## Slide 1: Introduction of MICE 201 MHz RF Cavity
Derun Li
Lawrence Berkeley National Laboratory
MICE RF Workshop
Fermilab, June 2, 2014

## Slide 2: MICE
Our responsibilities in MICE cooling channel:
  2 RFCC modules (eight 201-MHz cavities) (Step-6)
  2 spectrometer solenoids (delivered)
Demonstration of muon ionization cooling
International MICE experiment at RAL
RFCC
RFCC
SS
SS

## Slide 3: The RFCC Module
Sectional view
of RFCC module
tuner
Cavity fabrication
Beryllium window
Coupler
Design and fabrication progress

## Slide 4: RF Design of the Cavity
The cavity design parameters
  Frequency: 201.25 MHz
  β = 0.87
  Shunt impedance (VT2/P): ~ 22 MΩ/m
  Quality factor (Q0): ~ 53,500
  Be window diameter and thickness: 42-cm and 0.38-mm
Nominal parameters for MICE and cooling channels in a neutrino factory
  8 MV/m (~16 MV/m) peak accelerating field
  Peak input RF power: 1 MW (~4.6 MW) per cavity
  Average power dissipation per cavity: 1 kW (~8.4 kW)
  Average power dissipation per Be window: 12 watts (~100 watts)

## Slide 5: MICE RF Cavity
Cavity has been tested successfully at MTA

## Slide 6: Fabrication Development of Cavity
42-cm
Cavity fabrication technique development, in collaboration with JLab; First prototype cavity has been high power tested at MTA, Fermilab

## Slide 7: Single Cavity Vessel
The vessel is made by Keller Technology, and is currently at Fermilab.
MuCool CC coil
Tuners &Tuning mechanism
Same features RFCC module would have

## Slide 8: Single Cavity Vessel (cont’d)

## Slide 9: First RFCC Module - Status