## Slide 1
Booster at high intensity proposals/solutions?
S.Y. Lee, Indiana University
11/24/2015 at AGS
Booster Modeling (ORM+ICA)
Transverse beam dynamics at injection energy: Emittance evolution measurement at Fermilab Booster was systematically measured and analyzed in 2006. [see X. Huang, et al, PRSTAB 8, 014202 (2006)]
Longitudinal beam dynamics near transition
1. What I know about the Booster:
Proposal/Solution?
Conclusion!
PIP-II involves a 250-m superconducting linac to energy of 800MeV; and accelerated in the existing Booster accelerator to 8 GeV up to 20Hz rep rate.

## Slide 2: An Overview of Booster’s lattice
FU
DU
FD
FD
DD
L(6m)
FU
S(1.2m)
beam
S
0.5m
T
19.76m
Xiaobiao Huang, S.Y. Lee, Eric Prebys, and Ray Tomlin; 8, 064001 (2005)
Superperiod=24; In each period, four Combined-function magnets. Length 2.889 m. Gradients are K1(F)=0.0542 m-2 and K1(D)=−0.0577 m-2. Horizontal tune 6.7, vertical tune 6.8
X. Huang’s Ph.D. thesis (2005): Orbit response matrix method for booster modeling. See also the presentation of C.Y. Tan & K. Seiya in this workshop
X. Huang: Independent component analysis at Fermilab Booster:

## Slide 3: The Fermilab Booster
Circumference(m) | 474.2
Inj/ext energy (GeV) | 0.4/8.0
Cycling rate (Hz) | 15
Hori/vert betatron tunes | 6.7/6.8
Superperiod | 24
Transition gamma | 5.446
Harmonic number | 84
Protons per pulse | 5.0E12
Longitudinal 95% emittance (eV-s) | 0.10 at injection
Transverse 95% emittance (mm-mr) | 12 (normalized) at injection

## Slide 4
Ionization beam profile monitors (IPM's) measure the beam profile by collecting electrons from background gas ionization. Measurement accuracy will depend on the number of electrons collected. The number of electrons collected depends on pressure, bunch intensity, and data collection mode. The center-to-center distance between microchannels is of the order of ∆x=1.5mm. Thus one can measure the beam width to within 1.5-2.0 mm. For the IPM at Fermilab Booster, the space charge correction has been shown to be important [J. Amundsen et al PRSTAB 6 102801 (2003)]
1994: W.S. Graves, Ph.D. thesis (1994)
2005, Jan.: X. Huang carried out systematic measurement of beam size during the Booster ramping cycle using IPM at Fermilab Booster. We need to understand the data!

## Slide 5
6t-inj
500-rev
4000-rev
8000-rev
12000-rev
16000-rev

## Slide 6
We measure the beam profile evolution vs beam intensity in the entire ramping cycle! From 2 turn-injection to 18-turn injection.
Machine modeling measured from ICA: βx=6.3m, βz=21.4m, Dx=2.54m, at the IPM location with Qx=6.7, Qz=6.8
Measure all other machine parameters during the ramping cycle
Modeling the emittance evolution!

## Slide 7
Vrfsinφs
Vrf
KE
RF voltage and phase vs time
Bunch length σt vs turn number for all intensity
Betatron tune vs time
Beam intensity vs time
Beam loss vs time vs intensity

## Slide 8
Typical Injection scheme at the Fermilab Booster: H- at 400 MeV from Linac is about 30 mA. Strip injection into the Booster gives about 4.2×1011 protons per injection turn. At 400 MeV, the revolution frequency is 4.51×105 Hz. The Normal operation has 12 injection turns, and the total intensity is about 5×1012 ppp at 15 Hz rep-rate.

## Slide 9
Space charge effects: Linac delivers about 30 mA beam current to the Fermilab Booster, i.e. about 4.2×1011 particles in each injection-turn.
Result: The vertical (normalized) emittance grows quickly at the first 4000-turns! The emittance growth depends sensitively on beam intensity!

## Slide 10
Horizontal IPM measurements

## Slide 13
δ1
δ2

## Slide 14
Summary:
Vertical emittance critically depends on beam intensity in 4000 turns from εz,Nrms=2 – 6 πμm!
The horizontal emittance is less affected by the space charge force εx,Nrms=2 πμm! Why?
The post-transition horizontal bunch-width oscillation is induced essentially by the longitudinal mis-match of the bunch shape with space charge effect in the rf potential well. Using the bunch shape mis-match, one can deduce the phase space area.

## Slide 15
T
Space charge force is a local kick on every half cell:

## Slide 16
Quantum fluctuation due to RF cavities are localized.
Sextupole nonlinearity on each half cell for nonlinearity in dipoles
Skew quadrupoles → Linear coupling and linear sum resonance
Random quadrupoles with zero tune shifts
Random closed orbit error → injection mismatch
Dynamical aperture of 80 by 50 pi-mm-mrad
Random number generators are used to generate b0, a0, b1, and a1. The quadrupole error is subject to a constraint with zero tune shift. The integrated sextupole strengths are -0.0173m-2 and -0.263m-2 for focusing and defocusing dipoles respectively (measured systematic values).
(For n>nt=9600) Gδ=2, Aδ=0.5, f=1/150, αδ=1/(15*150)

## Slide 17
x
z
x
z
σx
σz

## Slide 18
No sextupole

## Slide 19
Normalized εz for 6 turn injection
12 turn injection
Normalized εz for 15 turn injection

## Slide 21
Summaries from The emittance evolution measurements:
The vertical emittance growth has resulted mainly from the skew quadrupoles, that induce a sum resonance at Qx+Qz=integer. The reason is that the Montague resonance suppresses the growth of the horizontal emittance, and enhance the vertical emittance by about 25%.
The random dipole field error also generates about 25% vertical emittance growth.
We use the rms space charge force model to carry out numerical simulations. We are able to fit the observed data of emittance growth.

## Slide 22
1. Transverse Dynamics:
For PIP-II, the space charge is reduced by a factor of 2 at 800 MeV injection! A beam with 12-turn injection encounters similar space charge force similar to that of 6-turn injection at 400 MeV! It appears that the space charge is not as important as that of the 400 MeV injection. However, longitudinal beam dynamics becomes the most relevant problem for beam slip-stacking!
PIP-II project problems:

## Slide 23
γT
2. Transition energy crossing & Longitudinal dynamics:
I heard that you have feed-forward to eliminate this oscillation (see talk by W. Pellico)!

## Slide 24
3. half-integer stopband correction
We have carried out unsuccessful efforts to correct half-integer stopband at PSR and Fermilab Booster! However, recent work shows that it is possible to make correction to reduce emittance growth and beam loss [Hung-Chun Chao and S.Y. Lee Phys. Rev. ST Accel. Beams 18, 024202 (2015)].
It would be nice to carry out beam dynamic experiments for stopband correction.

## Slide 25
5. 2nd harmonic cavity
2nd harmonic cavity to will reduce momentum spread at transition energy similar to isochronous synchrotorn, but, the required voltage, ½ of the main cavity voltage, is high. The cavity needs to ramp and change frequency. It is a difficult task.
4. Bucket-to-bucket injection
From Eric Probys’s talk, I find that you plan to use bucket to bucket injection scheme. This may eliminate the initial loss of about 5-8%! Good idea!
Move extraction notch to 750 keV line would be a nice idea too.

## Slide 26
6. How about ferrite insert?
Contains 30 ferrite cores (Ni-Zn Toshiba M4C21A) with Resistive Paste. Each core is 8 in. outer diameter, 5 in. inner diameter, 1 in. thick
C. Beltran et al., Microwave instability induced by the Ferrite inserts at PSR.

## Slide 27
Conclusion: A Proposal for PIP
800 MeV injection will help emittance preservation!
Longitudinal dynamics in crossing transition energy need careful study. Use Fermilab Booster as RCS to accelerate beam up to 4 GeV at 30 Hz repetition rate.
Build another accelerator to accelerate beams from 4 GeV to 20 GeV can avoid transition crossing at Booster and Main Injector! The slip-injection will be much easier because the longitudinal emittance is less problematic at this series of accelerators.
How about an inductive insert at Booster?

## Slide 28
 | PIP | PIP-II
Inj/ext energy (GeV) | 0.4 | 0.8
Protons per pulse | 4.30E+12 | 6.50E+12
frep (Hz) | 30 | 30
Power at injection (kW) | 8 | 25
Power at 4 GeV (kW) | 83 | 125
Power at 8 GeV (KW) | 165 | 250
Power at 120 GeV (kW) | 2477 | 3744
frep (Hz) | 40 | 40
Power at injection (kW) | 11 | 33
Power at 4 GeV (kW) | 110 | 166
Power at 8 GeV (KW) | 220 | 333
Power at 120 GeV (kW) | 3307 | 4992
J. Strait, N.V. Mokhov, and S.I. Striganov, PRSTAB, 13, 111001 (2010): “for constant beam power, the (pion) yield is maximum for a beam energy of about 7 GeV, but it is within 10% of this maximum for 4 <Tbeam < 11 GeV, and within 20% of the maximum for Tbeam as low as 2 GeV. “

## Slide 29
Many thanks for your attention

## Slide 30
ICA: Measurements of turn-by-turn data have traditionally being used to measure and model accelerators. Employing the independent component analysis (ICA), we were able to measure the betatron and synchrotron tunes, betatron amplitude functions, dispersion functions for the entire ramping cycle (submitted for publication).
The amplitude of oscillation is about 0.4 mm; Notice the bursts due to the pinger, which is fired about every 225 turns.
An impression of raw data; 2500 turns from turn 1; at location L01

## Slide 32
Problems:
17 cavities are located in dispersive region, with energy increase 400keV per revolution

## Slide 33
Proton Improvement Plan-II (PIP-II) is Fermilab's plan for providing powerful, high-intensity proton beams to the laboratory's experiments. The increased beam power will position Fermilab as the leading laboratory in the world for accelerator-based neutrino experiments. PIP-II will also provide a flexible platform for further enhancement of the Fermilab accelerator complex to extend this leadership to the full range of particle physics research based on intense beams in the decades to come.
The heart of PIP-II is a 800-MeV superconducting linear accelerator, which capitalizes on the lab's expertise in superconducting radio-frequency technologies. Along with modest improvements to Fermilab's existing Main Injector and Recycler accelerators, the superconducting linac, called SCL, will provide the megawatt proton beam that is needed for the Long-Baseline Neutrino Facility.
PIP-II is planned to deliver beam in the early part of the next decade.

## Slide 34
Fermilab's Proton Improvement Plan II, or PIP-II, will enable the world's most intense neutrino beam and help scientists search for rare particle physics processes. These investigations will require intense beams of protons, which will produce gushers of other neutrinos that scientists can then study in greater detail.
Protons are first emitted from a source and formed into a beam; accelerated in a 250-m superconducting linac to an energy of 800 MeV. The PIP-II linac is situated on the infield of the (decommissioned) Tevatron accelerator on the Fermilab site. This siting takes advantage of existing cryogenic, electrical and water infrastructure. The proton beam is accelerated in the existing Booster accelerator to 8 GeV.
Some of the protons exiting the Booster will head directly toward a variety of targets for the production of particles, of which some fraction eventually decay into muons. The muons will be captured within the MC-1 Building. There they will enter a detector, where scientists can make measurements of this short-lived particle.

## Slide 35
The other protons exiting the Booster will take a different path, continuing down the accelerator chain. They will be transferred and accelerated within the existing Main Injector-Recycler complex — a set of 3.3-kilometer-circumference rings that will produce a beam of protons at an energy of 120 GeV. These protons then strike a target, eventually producing neutrinos. The neutrinos will then fly through the Earth at nearly light speed. Under the PIP-II scheme, they will be directed to the Long-Baseline Neutrino Facility experimental area, planned to be built at Homestake, South Dakota, 1,300 kilometers away. The LBNF detectors will help researchers better understand the behavior of neutrinos, which are notoriously difficult to observe because of their flighty nature.