## Slide 1
CERN’s Vision on Future Colliders
Daniel Schulte
FNAL August 2014

## Slide 2
European Strategy
Approved by CERN council, ESFRI roadmap
Identified four highest priorities:
Highest priority is exploitation of the LHC including luminosity upgrades
Europe should be able to propose an ambitious project after the LHC
  Either high energy proton collider (FCC-hh)
  Or high energy linear collider (CLIC)
Europe welcomes Japan to make a proposal to host ILC
Long baseline neutrino facility (not a collider)

## Slide 3
c) ... Europe’s top priority should be the exploitation of the full potential of the LHC, including the high-luminosity upgrade of the machine and detectors with a view to collecting ten times more data than in the initial design, by around 2030. …
LHC and HL-LHC
today

## Slide 4: Expectations after Long Shutdown 1 (2015)
Cms energy 13 TeV
Bunch spacing 25 ns
Expected maximum luminosity: 1.6 x 1034 cm-2 s-1 ± 20%
  Limited by inner triplet heat load limit, due to collisions debris
 | Number of bunches | Intensity per bunch | Transverse emittance | Peak luminosity | Pile up | Int. yearly luminosity
25 ns BCMS | 2508 | 1.15 × 1011 | 1.9 µm | 1.6×1034 cm-2s-1 | ~43 | ~40-45 fb-1
Other conditions:
  Similar turn around time
  Similar machine availability
  β* ≤ 0.5m (was 0.6 m in 2012)
    Using new injector beam production scheme (BCMS), resulting in brighter beams.
F. Bordry

## Slide 5: The HL-LHC Project
Many improvements on the LHC ring
New IR-quads Nb3Sn (inner triplets)
  New 11 T Nb3Sn (short) dipoles
  Collimation upgrade
  Cryogenics upgrade
  Crab Cavities
  Cold powering
  Machine protection
  …
Goal is to obtain about 3 - 4 fb-1/day (250 to 300 fb-1/year)
Many improvements on the injector chain
Linac 4 - PS booster
PS
SPS

## Slide 6
Baseline layout of HL-LHC IR region
Example of International Collaboration
with national laboratories but also involving industrial firms
Q4
D2
F. Bordry

## Slide 7
Run 2
Run 3
Run 4
LS 2
LS 3
LS 4
LS 5
Run 5
LHC schedule approved by CERN management and LHC experiments spokespersons and technical coordinators (December 2013)
LS2 starting in 2018 (July) => 18 months + 3 months BC
LS3 LHC: starting in 2023 => 30 months + 3 months BC
Injectors: in 2024 => 13 months + 3 months BC
LHC schedule beyond LS1
Beam commissioning
Technical stop
Shutdown
Physics
Run 2
Run 3
Run 4
LS 2
LS 3
LS 4
LS 5
Run 5
(Extended) Year End Technical Stop: (E)YETS
EYETS
YETS
YETS
YETS
YETS
YETS
300 fb-1
3’000 fb-1
30 fb-1
F. Bordry

## Slide 8: Future Project at CERN
d) …to propose an ambitious post-LHC accelerator project at CERN by the time of the next Strategy update…
… CERN should undertake design studies for accelerator projects in a global context, with emphasis on proton-proton and electron-positron high-energy frontier machines. These design studies should be coupled to a vigorous accelerator R&D programme, including high-field magnets and high-gradient accelerating structures, in collaboration with national institutes, laboratories and universities worldwide.
HFM – FCC-hh
HGA - CLIC

## Slide 9
Provide a staged approach to reach 3TeV cms with L=6 (2) x 1034cm-2s-1
First stage 350GeV (top and higgs)
Second stage around 1.5TeV (depending on physics input)
Third stage around 3TeV (depends on physics as well)
CLIC Overview

## Slide 10
29 Countries – over 70 Institutes
Accelerator collaboration
Detector collaboration
Accelerator + Detector collaboration
Current CLIC Collaboration
Notes: The CLIC accelerator and detector&physics studies are already set up at international collaboraitons with wide participation from member and non-member states

## Slide 11: The CLIC CDR documents
Vol 1: The CLIC accelerator and site facilities
- CLIC concept with exploration over multi-TeV energy range up to 3 TeV
- Feasibility study of CLIC parameters optimized at 3 TeV (most demanding)
- Consider also 500 GeV, and intermediate energy range
- https://edms.cern.ch/document/1234244/
Vol 2: Physics and detectors at CLIC
- Physics at a multi-TeV CLIC machine can be measured with high precision, despite challenging background conditions
- External review procedure in October 2011
- http://arxiv.org/pdf/1202.5940v1
Vol 3: “CLIC study summary”
- Summary and available for the European Strategy process, including possible implementation stages for a CLIC machine as well as costing and cost-drives
- Proposing objectives and work plan of post CDR phase (2012-16)
- http://arxiv.org/pdf/1209.2543v1
In addition a shorter overview document was submitted as input to the European Strategy update, available at:
http://arxiv.org/pdf/1208.1402v1
An input document to Snowmass 2013 has also been submitted:
http://arxiv.org/abs/1305.5766

## Slide 12: Timeline
2013-18 Development Phase
Develop a Project Plan for a staged implementation in agreement with LHC findings; further technical developments with industry, performance studies for accelerator parts and systems, as well as for detectors.
2018-19 Decisions
On the basis of LHC data and Project Plans (for CLIC and other potential projects), take decisions about next project(s) at the Energy Frontier.
4-5 year Preparation Phase
Finalise implementation parameters, Drive Beam Facility and other system verifications, site authorisation and preparation for industrial procurement.
Prepare detailed Technical Proposals for the detector-systems.
2024-25 Construction Start Ready for full construction and main tunnel excavation.
Construction Phase
Stage 1 construction of CLIC, in parallel with detector construction.
Preparation for implementation of further stages.
Commissioning
Becoming ready for data-taking as the LHC programme reaches completion.
S. Stapnes

## Slide 13: CLIC Accelerator Activities 2014-18
Re-baselining studies ongoing (375 GeV, ~1.5 TeV, 3 TeV) – including more work on a klystron based initial phase
Overall design and system optimisation, technical parameters for all systems
Overall performance, reliability and risk studies
Cost, power/energy optimisation, scheduling, site, etc
Develop the technical design basis. i.e. move toward a technical design for crucial items of the machine; X-band as well as all other parts.
Priorities are module/structure development including significantly more testing facilities, complete modules for lab and CTF3, modulators/klystrons, alignment/stability/magnet studies and instrumentation
Purpose: Technical developments, industrial developments, cost and power optimisation, and components as needed for system tests
System tests and programs to address the key performance and operation goals
CTF3+ and drive beam front end
ATF, FACET and various other smaller programmes for specific studies
Purpose: Studies of drive-beam stability and RF units, beam-loading experiments, deceleration, RF power generation and two beam acceleration with complete modules, as well as beam based alignment/beam delivery system/final focus studies
Various RF elements of a complete module, X-band test stand
Prototyping of magnets, support/alignment systems and module instrumentation
Courtesy of Steinar Stapnes
Notes: ATF(Accelerator Test Facility) is a test accelerator focused on generating the super low-emittance beam (KEK)
FACET, the Facility for Advanced Accelerator Experimental Tests (SLAC
Key words for 2013:
rebaseling
power reduction studies
systemtests
structure testing capacity
drive beam power unit
common work with light source community

## Slide 14: CLIC and FELs
X-band technology appears interesting for compact, relatively low cost FELs
Logical step after S-band and C-band
Use of X-band in other projects will support industrialisation
They will be klystron-based, additional synergy with klystron-based first energy stage
Hence started to collaborate on use of X-band in FELs
Australian Light Source, Turkish Accelerator Centre, Elettra, SINAP, Cockcroft Institute, Athens, Oslo and Uppsala University, CERN
EU Design Study proposal to be submitted in September
High synergy
High repetition rate klystrons (500Hz soon to be ordered for CLIC)
RF component design
Cost model and optimisation
Other accelerator components, e.g. alignment, …

## Slide 15
Forming an international collaboration to study:
pp-collider (FCC-hh)  defining infrastructure requirements
e+e- collider (FCC-ee) as potential intermediate step
p-e (FCC-he) option
80-100 km infrastructure in Geneva area
~16 T  100 TeV pp in 100 km
~20 T  100 TeV pp in 80 km
FCC Overview
M. Benedikt

## Slide 16
Two main experiments sharing the beam-beam tuneshift
  Two reserve experimental areas not contributing to tuneshift
80% of circumference filled with bunches
 | LHC | HL-LHC | FCC-hh
Cms energy [TeV] | 14 | 14 | 100
Luminosity [1034cm-2s-1] | 1 | 5 | 5
Bunch distance [ns] | 25 | 25 | 25
Background events/bx | 27 | 135 | 170
Bunch length [cm] | 7.5 | 7.5 | 8
FCC-hh
A baseline parameter list exists: http://indico.cern.ch/event/282344/material/3/
A somewhat conservative first approach, will now make a conceptual design and optimise the parameters and look at alternative parameters

## Slide 17
FCC-hh Challenges: Magnets
Arc dipoles are the main cost and parameter driver
Baseline is Nb3Sn at 16T
HTS at 20T also to be studied as alternative
Field level is a challenge but many additional questions:
Aperture
Field quality
Different design choices (e.g. slanted solenoids) should be explored
Goal is to develop prototypes in all regions, US has world-leading expertise
Coil sketch of a 15 T magnet with grading, E. Todesco

## Slide 18
FCC-hh Challenges II
Optics and beam dynamics
IR design, dynamic aperture studies, SC magnet field quality, beam-beam, e-cloud, resistive wall, feedback systems design, luminosity levelling, emittance control, …
High synchrotron radiation load on beam pipe
Up to 30 W/m/aperture in arcs, total of ~5 MW
Machine protection, collimation etc.
>8GJ stored in each beam (24x LHC at 14TeV, 747-100 at 800km/h)
Collimation against background and arc magnet quench
100kW of hadrons produced in each IP
Stored energy in magnets will be huge (O(180GJ))
Injection system
…

## Slide 19
Preliminary baseline parameters exist
Up to four experiments
Luminosity/beam current limited by synchrotron radiation (50MW/beam)
FCC-ee
Parameter | Z | W | H | t | LEP2
E (GeV) | 45 | 80 | 120 | 175 | 104
I (mA) | 1400 | 152 | 30 | 7 | 4
No. bunches | 16’700 | 4’490 | 1’330 | 98 | 4
b*x/y (mm) | 500 / 1 | 500 / 1 | 500 / 1 | 1000 / 1 | 1500 / 50
ex (nm)/ey (pm) | 29/60 | 3.3/7 | 1/2 | 2/2 | 30-50/~250
sx(mm)/sy(nm) | 120/250 | 40/84 | 22/45 | 45/45 | 250/3500
xy | 0.03 | 0.06 | 0.09 | 0.09 | 0.07
L (1034 cm-2s-1) | 28 | 12 | 6.0 | 1.8 | 0.012

## Slide 20
FCC-ee Challenges
Significant issues have to be addressed for FCC-ee, including:
100MW of synchrotron radiation power ( e.g. efficient RF system)
High beam current at low energy (Z, …)
Wide bandwidth focusing optics for small beam size
Top-up injection to deal with short beam lifetime
Integration with FCC-hh requirements
Polarisation for low energy

## Slide 21
Tentative design choice: beam parameters as available from hh and ee
  Max. e± beam current at each energy determined by 50 MW SR limit.
  1 physics interaction point, optimization at each energy
Could consider linac-ring design
collider parameters | e± scenarios |  |  | protons
species | e± (polarized) | e± | e± | p
beam energy [GeV] | 80 | 120 | 175 | 50000
luminosity [1034cm-2s-1] | 2.3 | 1.2 | 0.15 | 
bunch intensity [1011] | 0.7 | 0.46 | 1.4 | 1.0
#bunches per beam | 4490 | 1360 | 98 | 10600
beam current [mA] | 152 | 30 | 6.6 | 500
sx,y* [micron] | 4.5, 2.3 |  |  | 
FCC-he

## Slide 22
2014 |  |  |  | 2015 |  |  |  | 2016 |  |  |  | 2017 |  |  |  | 2018 |  |  | 
Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4
Kick-off, collaboration forming,
study plan and organisation
Release CDR & Workshop on next steps
Workshop & Review
 contents of CDR
Workshop & Review identification of baseline
Ph 2: Conceptual study of baseline “strong interact.”
Workshop & Review, cost model, LHC results  study re-scoping?
Ph 3: Study
consolidation
Report
Prepare
4 large FCC Workshops distributed over participating regions
Ph 1: Explore options
“weak interaction”
Proposed FCC Timeline

## Slide 23
The FCC studies should be performed in a global collaboration
  Most of the issues are generic, many have outreach impact
    Physics
    Technology
    Beam physics
    Only a limited amount is site specific
The FCC collaboration is being formed right now
  Like collaborators to take over full responsibilities for workpackages
  Some MoUs signed
  A number of MoUs is in preparation
Collaboration with CEPC-SppC
A first FCC collaboration management meeting will be held at CERN September 9-10
  Also institutes that have not yet signed a MoU are welcome
FCC Collaboration Meeting March 23-27 2015
FCC Collaboration

## Slide 24: ILC
Obviously the central point is a proposal of Japan to host the ILC
CERN is contributing to ILC preparation
  Contribution of some limited CERN personnel to ILC activities
  Collaboration between ILC and CLIC
  Accelerator physics studies, e.g. ATF2 (final focus test facility)
  Technology developments, e.g. cavity coupler design, copper coating
  Site studies
  Exchange of experts, EJADE (covers also hadron accelerators)
Europe looks forward to a proposal from Japan to discuss a possible participation.

## Slide 25: Neutrino Physics
f) … CERN should develop a neutrino programme to pave the way for a substantial European role in future long-baseline experiments. Europe should explore the possibility of major participation in leading long-baseline neutrino projects in the US and Japan.
Implementation:
CERN is setting up a Neutrino Platform to support European contributions
for neutrino facilities in the US and Asia:
  Extension of the experimental area of the SPS complex
  (CERN North area), charged beam for detector development
  Detector R&D for neutrino experiments: liquid Argon technology
  Lot of expertise for this technology in Europe
  Prepare detectors at CERN for transport and installment in the US
  First detector to be refurbished at CERN is ICARUS
M. Kramer

## Slide 26
Highest priority is the LHC exploitation and HL-LHC preparation
  Focus of the work and the resources
Two main options for new flag ship project considered and studied
  CLIC
    CDR exists
    Goal for 2018: Technology development and also use for other projects
  FCC-hh (potential FCC-ee intermediate stage and maybe FCC-he)
    Very new project, but can profit from LHC and world-wide (in particular US) proton expertise, welcome collaboration
    Goal for 2018: Development of CDR
ILC
  Japan has to lead, CERN supports
Long-baseline neutrino programme
Conclusion

## Slide 27
For your patience
To the people from whom I stole slides and input
  R. Heuer, F. Bordry, F. Gianotti, M. Kramer, S. Stapnes, M. Benedikt
To the people who were and are doing the work
Thanks

## Slide 28
Reserve

## Slide 29
US expertise is very important for FCC-hh
  Magnet technology
  Collimation
  Beam-beam and mitigation
  Many other technologies
  Beam dynamics, shower tracking, …
  Operational experience, …
  Physics
Warmly welcome a close collaboration
Collaboration on FCC

## Slide 30: FCC-ee vs. Linear Colliders
Linear
CepC (2 IPs)
Circular,
adding four experiments
Modified from original version:
http://arxiv.org/pdf/1308.6176v3.pdf
F. Gianotti