## Slide 1: Experiment in a bottle (magnetic): MICE PRY

## Slide 2: Overview
Introduction and Concept
CAM concept (Forces on PRY)
Status of Manufacturing
Effect of PRY on MICE Beam
MICE PRY V’

## Slide 3: Partial Return Yoke
MICE hall: solenoids cause large stray field
Aim of PRY: Reduce stray field in hall to tolerable level
Shielding plates
  wall thickness 10 cm
  weight: 55t
Performance
  Reduces stray field outside of shield to 5-10 Gauss
(Note: not to scale)
H Witte. Step IV & VI: Local Flux Return. MICE CM 34, October 2012.

## Slide 4: Principle

## Slide 5: PRY Step IV
Courtesy of J. Tarrant / S. Plate
7.6m
2.8m

## Slide 6: Force Scenarios
Nominal cases
  200/240 MeV flip/solenoid mode
  Deflection 0.18 mm
Worst case analysis
  Increased forces by factor 5
  Still very safe
Monitoring: draw-wire sensor
WDS-3000-P115-CA-P

## Slide 7: CAM Concept
Mitigates overstressing of L-Seal bolts
Stress analysis now ok up to 5 times calculated load on end plate of PRY
L-Seal

## Slide 8
Status of Manufacturing

## Slide 9: Schedule
April 1st: PRY South Side complete
April 30th: PRY North Side arrived at Liverpool port
May 12th: PRY North Side at RAL
May 15th: PRY North legs installed and aligned
May 20th: Installation of north side plates

## Slide 10: PRY South Side
April 1st 2015

## Slide 11: PRY South Side
April 1st 2015

## Slide 12: PRY South Side
April 2nd 2015

## Slide 13: PRY North Side
May 15th 2015
Support structure
aligned to within 1 mm
PRY South Side

## Slide 14
Effect of PRY on MICE Beam

## Slide 15: Correction MICE Coil Currents
Solenoids run more efficiently with iron yoke
  i.e. at nominal current longitudinal field is too large
  Small effect (≈ %)
  Can be corrected by tweaking coil currents, but this is a lengthy process if done manually
New approach: perturbation theory
  Magnetization in PRY does not change
  Treat error field as perturbation
  Find set of coil currents which corrects these errors

## Slide 16: 240 MeV Flip

## Slide 17: 240 MeV Flip – Field Error

## Slide 18: Methodology
E2
SS
E1
M2
M1
FC
Bz1
Bz2
Bz3
Bz4
Bz5
Bz6
A · x = b
Linear equation system
Solve for x (=I)

## Slide 19: 240 MeV Flip - Corrected

## Slide 20: 240 MeV Flip – Error Field

## Slide 21: 240 MeV Sol – Error Field

## Slide 22: Uncorrectable Error
Partial iron return yoke: causes asymmetry of field
Evaluate by looking at field harmonics

## Slide 23: Central Mesh
Quad mesh
(3D: hexahedral mesh)
Surface mesh extruded
Tetrahedral mesh
Small effect, good accuracy required – need very fine mesh

## Slide 24: Azimuthal Field – No Iron
Mesh good enough? Test with case we know the answer for!

## Slide 25: Step IV, 240 MeV Flip
R=0.15m

## Slide 26: Step IV, 240 MeV Solenoid
R=0.15m

## Slide 27: Harmonics 240 MeV Flip
 | A | B
1 | -5.00E-20 | -1.30E-19
2 | 1.77E-06 | 4.00E-03
3 | 5.11E-20 | 5.98E-19
4 | 6.23E-19 | -1.78E-18
5 | -3.85E-20 | 4.32E-19
6 | -1.29E-06 | -2.85E-07
7 | 1.01E-19 | 3.96E-19
8 | -5.34E-19 | 6.30E-19
9 | -5.11E-20 | 5.26E-19
10 | -4.77E-07 | 2.44E-09
11 | -1.26E-20 | -1.66E-19
 | A | B
1 | 1.00E-19 | -2.19E-19
2 | 4.25E-06 | 2.70E-03
3 | -1.19E-19 | 4.43E-19
4 | 5.86E-19 | -8.93E-19
5 | 2.92E-19 | 4.02E-19
6 | -3.10E-06 | -1.80E-07
7 | -3.64E-19 | 7.93E-20
8 | -3.18E-19 | 2.02E-19
9 | 2.64E-19 | 2.98E-19
10 | -1.14E-06 | 5.95E-09
11 | -1.73E-19 | -4.09E-20
Z=-3.25m
Z=-3.75m
 | A | B
1 | 7.48E-20 | -1.01E-19
2 | 2.51E-06 | 1.55E-03
3 | -9.58E-20 | 2.40E-19
4 | 3.07E-19 | -6.09E-19
5 | 2.02E-19 | 2.10E-19
6 | -1.84E-06 | -4.50E-08
7 | -1.71E-19 | 3.06E-20
8 | -3.08E-19 | 1.74E-19
9 | 9.58E-20 | 1.31E-19
10 | -6.76E-07 | 9.77E-09
11 | -1.06E-19 | -2.95E-20
Z=-4.25m
 | A | B
1 | 6.65E-20 | -9.05E-20
2 | 1.25E-06 | 7.07E-04
3 | -5.38E-20 | 1.17E-19
4 | 1.45E-19 | -3.08E-19
5 | 6.43E-20 | 1.40E-19
6 | -9.15E-07 | -8.40E-09
7 | -1.02E-19 | -2.82E-20
8 | -8.09E-20 | 9.49E-20
9 | 3.57E-20 | 6.23E-20
10 | -3.32E-07 | 7.27E-09
11 | -1.05E-20 | 2.32E-20
Z=-4.75m
A: real harmonics
B: skew harmonics
R=0.15m

## Slide 28: Harmonics 240 MeV Flip
R=0.15m

## Slide 29: Harmonics 240 MeV Solenoid
R=0.15m
Communicated to Analysis Group

## Slide 30
MICE Step V’

## Slide 31: MICE Step V’
Two versions
  Reference design (J. Pasternak, V. Blackmore, …)
  Alternative design (Chris Rogers)
Described in MICE Note 450

## Slide 32: PRY MICE Final Step
2.25m
Existing PRY
New PRY Section
Doghouse may be required to shield vacuum pumps

## Slide 33: Engineering
New center section
Aim: drawings complete by beginning of June
120 kN
1.2 kN
3 kN

## Slide 34: Summary
Manufacturing PRY Step IV
  South side complete and installed
  North side: at RAL
  Installation ongoing
Effect of PRY on beam
  Procedure for correction of solenoid currents
  Effect of non-correctable error on beam quantified
PRY MCE Step V’
  Engineering ongoing, expected to be finished June 1st

## Slide 35: Additional Slides

## Slide 36: Engineering

## Slide 37: Ref Lattice - 5/10 Gauss No Doghouse

## Slide 38: Reference Lattice