## Slide 1: Multipass Beam Breakup Study at Jefferson Lab for the 12 GeV CEBAF Upgrade
ILKYOUNG SHIN
University of Connecticut
April 9, 2013

## Slide 2: Outline
Introduction
  Jefferson Lab and the 12 GeV Upgrade
  Multipass beam breakup (BBU) theory
Multipass Beam Breakup Study
  BBU simulations
  Experimental setup and measurement
  Data analysis
Results and Conclusions
My interest in LARP

## Slide 3: Jefferson Lab and 12 GeV Upgrade
Aerial view of Jefferson Lab
12 GeV Upgrade project
Beam energy upgrade from 6 GeV to 12 GeV
N
Linear accelerator
Arc
Recirculating linear accelerator
Hall A
B
C
Hall A
B
C
e-

## Slide 4: Motivation of BBU Study
Multipass BBU can limit the current in recirculating linear accelerators such as CEBAF
In 2007, multipass BBU was observed at 54 μA
  Prototype cavities for the 12 GeV Upgrade caused multipass BBU
    Anticipated BBU threshold current: ~ 20 mA
    Operational max beam current for 6 GeV: 200 μA
    Design max beam current for 12 GeV: 80 μA
Lessons from the BBU observation
  We should very carefully survey HOMs for all cavities
  We should experimentally investigate BBU

## Slide 5: Elliptical RF Cavity
Time-Varying Field: radio frequency
e-
1.5 GHz CEBAF cavity
Electric field
Electromagnetic field accelerates particles
EM field particle
energy
Particles excite electromagnetic fields
Particle EM field
energy
Beam-induced EM field causes multipass BBU

## Slide 6: TM110 mode
Dipole modes deflect particles
The magnetic field deflects particles in the transverse direction
The deflection is responsible for multipass BBU
y
z
E
e- beam
Force
B
x
y
z
y
B
x
Force

## Slide 7: Multipass Beam Breakup
RF Cavity
B
E
TM110 mode
e- beam
Force
B
Beam breakup (BBU)
  The beam deposits energy to the HOM while ohmic resistance of the cavity dissipates the HOM energy
  If power deposited > power dissipated
  Exponential increase of the HOM energy
  Beam loss: mutipass beam breakup
Beam

## Slide 8: Analytical Formula and Simulation
BBU threshold current: two-pass beam, one HOM in one cavity
p: recirculating particle momentum
e: electron charge
R/Q: shunt impedance of dipole mode
QL: quality factor of dipole mode
k: wave number of dipole mode
ω: dipole mode frequency
Tr: recirculation time
M12: One revolution transfer matrix element
Threshold current behavior
  Blue line: analytical formula
  Red dots: computer simulations

## Slide 9
Beam Breakup Study
at Jefferson Lab
Simulation and Experiment

## Slide 10: Simulations of BBU
Simulation codes developed at Jefferson Lab
  Two Dimensional Beam Breakup (TDBBU)
  MATrix Beam Breakup (MATBBU)
  My contribution
    Implementing RF focusing effect to TDBBU
My BBU simulation studies
  HOM damping requirement studies
  6 GeV beam in the 12 GeV accelerator

## Slide 11: Damping Requirement of (R/Q)QL
How much (R/Q)QL should be damped to avoid BBU
  Threshold current > Design beam current
Simulations performed using two arc optics
  4 GeV arc optics
  DBA arc optics
Simulation result
  HOMs should be damped to (R/Q)QL < 6.2x108 Ω
(R/Q)QL < 6.2x108 Ω was provided to the SRF group
  The SRF group designed cavities to meet the requirement

## Slide 12: BBU study for 6 GeV in 12 GeV Accelerator
Need 6 GeV beam in the 12 GeV accelerator
Simulation results
  3 pass for 6.6 GeV: Ith = 716 μA
  5 pass for 6.6 GeV: Ith = 174 μA
Beam dump power limits the maximum current
  Imax for 6.6 GeV: 1 MW = 151 μA x 6.6 GV
Comparison of Imax with the two Ith
  3 pass for 6.6 GeV: 716 μA > 151 μA
  5 pass for 6.6 GeV: 174 μA > 151 μA
Conclusion
  3 pass for 6.6 GeV is better choice

## Slide 13: HOM Survey at CMTF

## Slide 14: HOM Survey at CMTF (1)
Cavity configuration in a cryomodule
HOM ports
A cryomodule contains 8 cavities
A network analyzer is connected to HOM ports
Measured scattering parameter S21
Notes: RF cavities were made to meet the HOM damping requirement I provided.
And then, RF cavities were mounted in cryomodules.
A cryomodule is a liquid helium vessel, which contains 8 cavities in series as shown here.
I did HOM survey to confirm the conformity of HOM damping requirement.
This picture shows the CMTF and HOM survey setup.
A network analyzer was connected to HOM ports.
The HOM ports are connected to HOM couplers of the cavity.
We measured the scattering parameters S21.
More details on the next slide.
-------------------------------------------
Before installing the cryomodules to the CEBAF accelerator, we performed HOM survey at the CMTF.

## Slide 15: HOM Survey at CMTF (2)
HOM coupler
Laptop
Port 1
Port 2
Network analyzer
Measured transmission coefficient
,
Obtained QL from S21 measurement
Notes: During HOM survey procedure, We measured the scattering parameters S21 and saved the data to a laptop.
NWA excites HOMs by sending signal Vin through an HOM coupler and detects HOMs in the cavity by measuring Vout through another HOM coupler.
The rectangular pipes are fundamental power couplers which feed the accelerating mode power into the cavity.
I extracted QL from the measurement.

## Slide 16: Full HOM Spectrum
Total number of modes to be analyzed:
  3 passbands x 7 modes x 2 polarizations x 8 cavities x 2 cryomodules = 672 modes
TM011
TE111
TM110
TM111
Frequency[Hz]
2050-2250 MHz
2850-3050 MHz
1850-2050 MHz
Notes: This is a full HOM spectrum.
TE111, TM110, and TM111 are dipole modes of our concern. We are not interested in this monopole mode.
There are three passbands. Because this is for a 7-cell cavity, there are 7 modes in each passband. Two polarizations are possible in each mode. One cryomodule contains 8 cavities.
We have 672 modes to analyze.
It take a long time to analyze each peak one by one, but we saved a lot of time using Mathematica program, polfit.

## Slide 17: QL estimation
a
Measurement of QL:
Developed by C. Potratz, et al.
Loaded quality factor
Polfit: Mathematica program
f
Δf-3dB
-3dB
Frequency[Hz]
Black dot: measured data
Red line: fitted value
7 modes (TM110): 7-cell cavity
Double peaks: polarization of dipole mode

## Slide 18: Results of HOM Survey at CMTF
(R/Q)QLk
(R/Q)QLk
Cryomodule C100-1
Cryomodule C100-2
TE111 modes
TM110 modes
TM111 modes

## Slide 19: BBU Experiment at CEBAF

## Slide 20: Multipass Beam Breakup Experiment
12 GeV Upgrade at JLab
New cavity for 12 GeV
Purpose: experimentally investigate the vulnerability of the 12 GeV Upgrade accelerator to multipass BBU
Two cryomodules (16 cavities) installed at the end of the South Linac
Two-pass, 1.16 GeV beam: 40, 80, 180 μA
3 optical setups: FODO cells set to 90°, 105°, 120° phase advance

## Slide 21: Beam Transfer Function Measurement
Network analyzer excites HOMs: VNWA
HOMs perturbs the beam
Beam excites HOMs: Vbeam
Network analyzer measures total HOM voltages:
  Vtotal = VNWA + Vbeam
Vbeam contains BBU threshold information

## Slide 22: Data Analysis Methodology
BBU experiment for the 12 GeV CEBAF Upgrade
Previous BBU experiment at JLab FEL (C. Tennant’s dissertation, 2006)
Could not obtain the difference of QL in terms of beam currents: Ith >> 180 μA
There exists a consistency in the maximum values of the peak as a function of the average beam current
Magenta: 0 μA
Black: 180 μA
Measured QL as a function of beam current
Calculated the BBU threshold current using the differences of QL
Threshold current: ~2.4 mA
-20
-30
[dB]

## Slide 23: Comparison with previous experiment
Previous BBU study using peak values (N. Sereno’s dissertation, 1994)
BBU experiment for the 12 GeV CEBAF Upgrade
An stripline kicker perturbs the beam
HOMs are excited directly through HOM coupler

## Slide 24: Experimental and Simulation Results
BBU experiment results
  Threshold lower bound obtained from experiment: >2 mA
  BBU did not occur at 180 μA for 2-pass 1.16 GeV beam
Simulation results: used measured HOM quantities
  The BBU experiment (2-pass 1.16 GeV): Ith=9 mA
  The 12 GeV Upgrade (5.5-pass 12 GeV): Ith=4.5 mA
  Design maximum current for the 12 GeV Upgrade: 80 μA
Conclusion
  Multipass BBU is not a concern in the 12 GeV accelerator within the current HOM damping requirement
  (R/Q)QLk=1x1010 Ω/m

## Slide 25: Summary and Conclusion
Performed simulation studies for HOM damping requirement
  provided the SRF institute with the results for cavity design
Performed HOM survey at CMTF
  Confirmed that cavities met the damping requirement
  Developed a fast and reliable method for RF measurement analysis
Performed BBU experiment and simulated the 12 GeV Upgrade accelerator
  Multipass BBU is not a concern in the 12 GeV accelerator within the current HOM damping requirement

## Slide 26: My Interest in LARP
Researches to reduce beam instabilities
Microwave engineering and Beam instrumentation
Research experience at JLab
  Multipass beam breakup study
USPAS classes
  Intermediate Accelerator Physics and Beam Measurements (2010)
  Synchrotron Radiation Instrumentation and Applications (2010)
  Computational Methods in Beam Dynamics (2009)
  Microwave Measurements and Beam Instrumentation Laboratory (2009)
  Accelerator Physics (2008)
  Fundamentals of Accelerator Physics and Technology with Simulations and Measurements Lab (2007)
My interest
My background

## Slide 27: Acknowledgements
Thank you for inviting me to this collaboration meeting and interviewing me.
Particular thanks to Kyungseon Joo, Byung Yunn, Todd Satogata, Geoffrey Krafft
Special thanks to all CASA group members, SRF group members, and friends
Thank all of you.
Alex Bogacz
Michael Tiefenback Yves Roblin
Mike Spata
Balsa Terzic
Yaroslav Derbenev
Hipeng Wang
Jiquan Guo
Frank Marhauser
Mircea Stirbet
Ryan Bodenstein
Subashini de Silva
Alicia Hofler
Vasiliy Morozov
Edward Nissen
Rui Li
Fanglei Lin
Yuhong Zhang

## Slide 29: Backups for Questions

## Slide 30: HOM damping
HOM couplers: antennae
  extract HOMs energy
  have to be broadband to cover the most HOMs
  should not damp the accelerating mode
HOM coupler
HOM coupler

## Slide 31: FODO Cell and Phase Advance
FODO cell: a pair of focusing and defocusing quadrupoles
  If f1=-f2, the net effect is focusing
Phase advance: Ψ(s)
F
D
O
O
s
N
S
N
S

## Slide 32: Transcendental Equation
Threshold condition: denominator =0
ωλ
ωth

## Slide 33: Trapped Modes in Cavity
TE111, TM110 and TM111 lower than ~3GHz are trapped within the cavity
Above ~3GHz, any dipole HOM would propagate through the beam pipe
The cavity’s TM110 and TM111 modes are converted into the beam pipe's TE11 mode
  The field map of TM111 mode shows the mode pattern is more similar to TE111 than TM111 type
  At the beam pipe area, the mode has strong transverse electric fields
  TM111 modes propagate through the beam pipe
The mode conversion is not perfect
  A few modes (TM111 pi/7 and TM111 2pi/7) modes are trapped near 2.9 GHz
Cut-off frequencies
  TE11 mode: 2.51 GHz
  TM01 mode: 3.28 GHz
  TM11 mode: 5.2 GHz

## Slide 34: 7 modes in 7-cell cavity
Analogous model for multi-cell cavity
Amplitude distribution in a seven-cell cavity
Chain of weakly coupled pillbox cavities
Chain of coupled pendula as a mechanical analogue

## Slide 35: DBA lattice
Double Bend Achromat (DBA) lattice
  A lattice unit to minimize particle beam emittance
Schematic of DBA lattice
F
F
F
D
D
B
B

## Slide 36: Simulations and Theory
Threshold current behavior in terms of HOM frequency
  The blue and green lines are first and second order solutions.
  The block points are threshold currents from computer simulations.
  Threshold behavior is sensitive to an HOM frequency.

## Slide 38: RF Focusing

## Slide 39: Focusing effect in RF cavity
Where does the focusing effect come from?
  Accelerating field
  Ez induces Er and Bφ (Maxwell’s equations)
  Radial force on an electron (Lorentz force)

## Slide 40: Rosenzweig-Serafini Model
Transfer Matrix

## Slide 41: Rosenzweig-Serafini Model(1)
Assume
Average radial force
Equation of motion

## Slide 42: Other Researches

## Slide 43
Cumulative BBU (one-pass BBU) study for the 12 GeV injector prototype
Cumulative BBU behaviors
  Transient behavior: Transverse amplitude increases.
  Steady state behavior: Beam becomes stable.
Other Research (1)
Schematic of the 12 GeV injector prototype
Transverse amplitude vs. bunch number

## Slide 44: BBU Study for 12 GeV Injector Prototype
Simulation results (IPAC 2011, WEP085)
  Even in an extreme case, the transverse amplitude is not significant (<1mm).
  Cumulative BBU is not a concern for the prototype.
QL=5×1010
QL=5×1011
QL=1×1012

## Slide 45: Other Research (2)
BBU simulation study for the LHeC
  LHeC: a proposed collider at CERN
  New electron accelerator + existing LHC

## Slide 46: Other Research (3)
BBU simulation study for JLAMP
  JLAMP: Jefferson Lab AMPlifier
  4th generation light source proposal by Jefferson Lab

## Slide 47: Damping Requirement of (R/Q)QL
How much (R/Q)QL should be damped to avoid BBU
  Threshold current > Design beam current
Simulations for the 12 GeV Upgrade
  4 GeV standard arc optics
    BBU study was performed by B. Yunn in 2004.
  Double Bend Achromat(DBA) arc optics by Alex Bogacz
    I performed a BBU simulation study (JLAB-TN-08-069)
Simulation results
  HOMs should be damped to (R/Q)QL < 6.2x108 Ω
(R/Q)QL < 6.2x108 Ω value was reported to the SRF group
  The SRF group designed cavities to meet the requirement

## Slide 48: Threshold Current in the Frequency Domain
Threshold current in frequency domain
HOM voltage:
Threshold condition: denominator =0
Threshold current in terms of measured quantity S21
Determine ωth from the transcendental equation
= 0
Previous research in time domain
(C. Lyneis et al., 1983)

## Slide 49: Threshold Lower Bound
ω/ωλ
Aλ
Wake function is very sharply peaked at the resonance frequency ωλ
Threshold frequency ωth is different from resonant frequency ωλ
Using ωλ, lower bounds for the threshold current can be estimated
ωλ
ωth