## Slide 1: Simulation study of helical cooling channel
K. Yonehara
APC

## Slide 2: Review HCC design effort
< 2000: Y. Derbenev proposed a novel cooling channel based on helical dipole magnet
V. Balbekov et al. worked on a helical cooling channel
  Use very low helix pitch (κ = pφ/pz ~ 0.2)
  Use a wedge absorber
  Use a periodic magnet structure (Rotation dipole+solenoid)
Yellow+Green: Wedge absorber
Blue: RF cavity
P.Lebrun et al., NFMCC-DOC-193-v1

## Slide 3: Review HCC design effort (cont’d)
2003: Y. Derbenev and R.P. Johnson developed a continuous helical cooling channel
  Combine a continuous helical dipole+quad components with a solenoid magnet with a continuous high pressure gas filled RF cavity
  Gas can work on a cooling absorber as well as the dark current buffer
2005: First cooling demo simulation
  Tested HCC theory
2009: First end-to-end cooling demo simulation
K. Yonehara et al., Proceedings of PAC’05, TPPP052 & IPAC’10, MOPD076

## Slide 4: Review HCC design effort (cont’d)
2006: V. Kashikhin invented a helical solenoid magnet
2008: M. Popovic and M. Neubauer invented a dielectric loaded RF cavity
V. Kashikhin et al., Proceedings of EPAC’08, WEPD015
Siberian snake type helical magnet
Helical solenoid magnet

## Slide 5: Beam dynamics in Helical Cooling Channel (HCC)
No periodic structure ⇒ Large beam phase space

## Slide 6: Stability condition
Stability condition is
with
and
It represented by g (field index) and
q (= kc/k-1)
Beam dynamics is pretty simple in a local helical coordinate system

## Slide 7: Tune dispersion
Taylor expansion of dispersion function
D’ is tuned from dp/ds
Dispersion = 0.28 m
(proper dE/ds dx)
Short path
at lo p
Long path
at hi p
Dispersion = 0.13 m
(Close to isochronous condition)
Dispersion = 0.35 m
(path length is overestimated)
Energy loss term
Tune dispersion to obtain the best cooling performance
Add higher magnet component (e.g. sextupole)
Take higher momentum particle (costly)
μ beam in GH2

## Slide 8: V. Balbekov revisited HCC
HCC has been simulated with totally independent simulation code by V. Balbekov
The simulation results are reproduced in two different simulation codes
He also pointed out that there is strong frequency dependence on the longitudinal
acceptance
The admittance of HCC is given in PRSTAB paper
K. Yonehara, V. Balbekov, Proceedings of EPAC’08, THPC110

## Slide 9: Invariant phase space in helical channel
Please find definition of variables
in Y. Derbenev and R.P. Johnson, PRSTAB 8, 041002, 2005
Action variable in transverse phase space
Action variable in longitudinal phase space
Following emittance plot is estimated by using above invariance
However, difference between ECALC9F and this evaluation is within 5 %

## Slide 10: Define geometry in HS magnet
Offset from HCC center:
Rrf pos: Offset of RF cavity
Rcoil pos: Offset of HS coil center
Reference orbit
HCC center
RF cavity
HS coil
Other constant geometry:
HS coil I.R.= 650 mm (due to 200 MHz RF)
HS coil O.R. = 700 mm
Rref: Radius of reference orbit = 160 mm
Helical pitch = 1.0 (45 degrees)
Helical period = 1 m

## Slide 11: Cooling simulation in HS channel
 | Rrf pos | Rcoil pos | Transmission
Blue | 160 mm | 495 mm | 80
Orange | 160 mm | 565 mm | 75
Red | 160 mm | 475 mm | 82
Need to optimize parameters
Need to shrink RF cavity to be half radius

## Slide 12: Technological challenging of HCC
CAD drawing of helical cooling channel
HPRF cavity
Helical solenoid coil
K. Yonehara et al., Proceedings of IPAC’10, MOPD076
Helical solenoid technology
Study dielectric loaded RF cavity
Real pillbox 805 MHz HP cavity
High cooling power
LN2 regulator

## Slide 13: Dielectric loaded HPRF cavity test
Empty cavity:
f = 1003.87 MHz
Q = 22772.3
Experimental results:
SMALL CYLINDER
BIG CYLINDER
f = 897.96 (±0.97) MHz
Q = 11823.1 (±1037.1)
f = 814.30 (±0.81) MHz
Q = 9415.89 (±828.6)
ε = 8.925 (±0.125)
tgδ = 7.28E-5 (±4.92E-5)
ε = 9.595 (±0.134)
tgδ = 8.17E-5 (±5.52E-5)
Al2O3 ring
E field direction
Goal: Measure dielectric constant and loss tangent in room & cryogenic temperature
Study breakdown with dielectric material in HPRF cavity
Make a compact HPRF cavity to incorporate into a compact magnetic structure
Rin=3.5cm
Rin=5.325cm
L
=
5.2
cm
L
=
7.75
cm
Al2O3 99.5%
Dielectric rings
J. Cenni, MAP Friday meeting, https://indico.fnal.gov/conferenceDisplay.py?confId=4661
SF simulation

## Slide 14: HS magnet in final cooling section
A large ripple is induced in configuration (c)
We need a cooling simulation with them for further investigations
M. Lopes et al., Proceedings of PAC’11, TUP172

## Slide 15: Development of HS magnet technology
Joint of HTS for double pancake coil
Critical current at joint part
Wind helical solenoid coil
M. Yu et al., FNAL TD-11-001

## Slide 16: Force flow LN2 cooling system
LN2 chiller
& circulator
Cryo RF
system
LN2 inlet (66 K)
LN2 outlet (70 K)
m: LiN2 flow rate m3/s
c: Specific heat 2019 J/K/kg
ΔT: Temperature difference
(TLN2 from 66.4 to 77 K)
ρ: Density 853 kg/m3
m ~ 3 Litters/s @ΔT = 4K
Cooling efficiency of chiller: ~10 %
Cooling power = 4 kW

## Slide 17: Study matching section
Baseline design of matching section (transport beam from coaxial straight to helical structure) has been made
Change HS coil center position adiabatically
Tune longitudinal beta oscillation by changing the length of section and the current density of HS coil
Almost 100 % transmission
Longitudinal phase space grows
This can be fixed by putting RF cavity in the section
Or tune phase slip factor
Include pressure window effect in future study

## Slide 18: Working group
Original inventors & analytic investigation
Yaroslav Derbenev, Rolland Johnson
For homogeneous absorber filled HCC
Simulation tool developer
Tom Roberts, Rick Fernow
HCC simulation developer
Alex Bogacz, Kevin Beard, Katsuya Yonehara
Kevin Paul, Cary Yoshikawa, Valeri Balbekov, Dave Neuffer
Design/Test HCC beam elements
RF: Mike Neubauer, Gennady Romanov, Milorad Popovic, Alvin Tollestrup,
Al Moretti, Moses Chung, Ben Freemire, Mukti Jana, Leo Jenner,
Maria Leonova, Tom Schwarz
Magnet: Gene Flanagan, Steve Kahn, Vladimir Kashikhin, Mauricio Lopes,
Miao Yu, John Tompkins, Sasha Zlobin, Vadim Kashikhin

## Slide 19: Summary
HCC theory was verified in numerical simulation
Present efforts for designing/making real HCC
  HS magnet: Has been demonstrated
  Promising technology
  Need additional effort to design final cooling section
  e.g. Bsolenoid = 14.1 T, Bdipole = 4.3 T at final segment in latest
  simulation
  HPRF cavity: Has been demonstrated with intense beam
  Looks promising technology
  RF power can be an issue (cryogenic operation?)
  Cryogenic & infrastructure: have not been discussed
  Integration: Has been discussed
  Need further efforts

## Slide 20: Next task in HCC simulation effort
Take into account RF power dissipation in HPRF cavity
Demonstrate cooling simulation with last two HCC configurations
  Space charge in dense hydrogen gas?
 | Z | ±Δr | ±Δp/p | b | b’ | bz | ν | κ | λ | εt | εT | εL | ε6D
unit | m | cm | % | T | T/m | T | GHz |  | m |  | mm rad | mm | mm3
 | Channel length | Full Width | Full width | @ ref | @ ref | @ ref | RF |  |  | transmision |  |  | 
1 | 0 | 15 | 22 | 1.3 | -0.5 | -4.2 | 0.325 | 1.0 | 1.0 |  | 20.4 | 42.8 | 12900
2 | 40 | 8 | 10 | 1.3 | -0.5 | -4.2 | 0.325 | 1.0 | 1.0 | 0.92 | 5.97 | 19.7 | 415.9
3 | 49 | 7 | 10 | 1.4 | -0.6 | -4.8 | 0.325 | 1.0 | 0.9 | 0.86 | 4.01 | 15.0 | 10.8
4 | 129 | 3 | 2.5 | 1.7 | -0.8 | -5.2 | 0.325 | 1.0 | 0.8 | 0.73 | 1.02 | 4.8 | 2.0
5 | 219 | 1.7 | 1.8 | 2.6 | -2.0 | -8.5 | 0.65 | 1.0 | 0.5 | 0.66 | 0.58 | 2.1 | 3.2
6 | 243 | 1.6 | 1.3 | 3.2 | -3.1 | -9.8 | 0.65 | 1.0 | 0.4 | 0.64 | 0.42 | 1.3 | 0.14
7 | 273 | 1.3 | 1.3 | 4.3 | -5.6 | -14.1 | 0.65 | 1.0 | 0.3 | 0.62 | 0.32 | 1.0 | 0.08
8 | 303 | 1.2 | 1.1 | 4.3 | -5.6 | -14.1 | 1.3 | 1.0 | 0.3 | 0.60 | 0.34 | 1.1 | 0.07