## Slide 1: Recent progress of HCC D&S
K. Yonehara
APC, Fermilab

## Slide 2: Contents
R&D of HCC beam element
  How to mitigate the geometry constraint?
Re-optimizing HCC lattice
Summary
Compact beam element
Re-optimize HCC lattice
Original beam element

## Slide 3: HCC RF system
Re-entrant HPRF
Dielectric loaded HPRF

## Slide 4: Re-entrant HPRF cavity
• Since huge RF power (see magnetic field above plot) can be stored in
a dome the required peak power is almost factor 10 smaller than the
dielectric loaded RF (4.4 MW/m @ 300 K, 325 MHz)
• However, the peak RF gradient should be higher than the DLRF
► Accelerating gap in the re-entrant RF is 1/2 of the DLRF
► Thus, the plasma loading in the re-entrant RF cavity becomes significant
• Real EM fields of the re-entrant RF was tested in g4bl and observed cooling
• Longitudinal matching is the current issue
► Too strong longitudinal kick to hold particles in the RF bucket
Require more lattice tuning & test cooling simulation

## Slide 5: Dielectric Loaded HPRF cavity
MTA proton beam
Proposed dielectric loaded HPRF test cell
Tests will be made in FY15 & 16 to observe
the loss tangent and the dielectric strength
at high RF power with intense beam
Dielectric insert
Ref of Dielectric strength of Al2O3 (99.8%)
Breakdown
limit of N2 gas at low pressure
Color code is the same purity
sample from various companies
IPAC 2013
LLRF sample test in 2014
Best data point
Test, Test, Test!
Dielectric strength of test sample

## Slide 6: Strategy of DL HPRF test for HCC
• Original design was made to reduce the
risk of permanent damage of ceramics
→ We assumed to use a 99.8 % ring
→ Big tolerance for operating gradients
From recent tests,
• Obtained loss tangent of 99.5 % is
twice lower than our original design
• Company spec shows that the 99.5 %
is twice higher dielectric strength than
99.8 %
→ We consider a 99.5 % ring is better
than the 99.8 % one
If the high power test shows that the dielectric strength of the 99.5 %
sample is very high (> 20 MV/m) we can re-evaluate the insert with smaller beam hole and longer than the test sample
Allow to design a very compact cavity
Beam hole
Length

## Slide 7: Considerable advantages in DL HPRF
Similar as a
re-entrant cavity
Ez
Hq
Ceramic ring
Ez
Hq
Pillbox
Pillbox
+ partially fill with
a Dielectric Material
IR = 0.177 m
Q = 7,518
U = 2.34 J
P = 1.27 MW
IR = 0.073 m
Q = 5,073
U = 4.17 J
P = 3.36 MW
r [m]
• Cavity radius of the DL HPRF
is significantly small
• DL HPRF has almost twice
larger stored energy than
the pillbox
• Peak power is still high but
getting lower at smaller
beam hole
r [m]
f = 650 MHz, E = 20 MV/m, tan d = 0.4e-4, e = 9.6

## Slide 8: Constraint of HCC magnet
• M. Lopes made a field calculation code,
SolCalc written in Matlab (IPAC’14)
• He demonstrated the limit of IR at the
equal cooling decrements
IR: inner radius
DR: coil thickness
a: Helical radius = k l/2 p
a
IR
DR
• Left plot shows the correlation between the
HS coil geometry and the ratio of helical dipole
and field gradient
• Dispersion is determined from the strength of
helical dipole and the field gradient (see next slide)
• Therefore, the cooling decrements in the HCC
is determined by the coil geometry
• Maximum allowable current (conductance) is
another parameters to determine the coil
geometry
• Coil geometry becomes tighter (smaller IR)
if higher current is needed
Equal cooling decrements
High current
(Good conductance)
Low current (poor conductance)

## Slide 9: Propose new configuration of HCC magnet
Equal cooling decrements
High current
(Good conductance)
Low current (poor conductance)
New cooling lattice
• Relax the constraint of HCC magnet!
Larger IR & thinner DR
→ Helical dipole stronger
→ Field gradient smaller
• What happens cooling performance
in the new lattice configuration?

## Slide 10: Emittance evolution in cooling channel
; initial emittance
; equilibrium emittance
; cooling decrement
; beta function in HCC
(beta is constant)
; rms fraction due to stochastic process
; partition of cooling
In case of HCC,
• These formulae are still good approximation
• en has a strong coupling among
three orthogonal components
(horizontal, vertical & longitudinal)
• The coupling is given by the dispersion
In the HCC, dgL is given (D. Neuffer)
Generic emittance evolution formulae
Exact formulae for emittance evolution in
HCC are given in Slava & Rol’s PRSTAB
and IPAC’14
Equal cooling decrements
→ gL = gT
→ Need strong focusing (high field gradient)
In case of low field gradient…
→ gL > gT Longitudinal enhance cooling

## Slide 11: Equilibrium Emittance in various cooling decrements
Line: Prediction
+ Equal cooling
✕ Longitudinal enhance
Line: Prediction
+ Equal cooling
✕ Longitudinal enhance
Injection angle = 45 degrees (k = 1)
RF window thickness = 60 mm
Equal cooling decrements

## Slide 12: Recent cooling result
Matching
Transmission: 56 % → 72 %
6D HCC
• RF parameter
E = 20 MV/m
n = 325 & 650 MHz
• Gas pressure
160 atm at 300 K
43 atm at 80 K
• Magnetic fields
Bz = 4 – 12 Tesla
• Equilibrium emittance
eT = 0.6 mm (goal: 0.3 mm)
eL = 0.9 mm (goal: 1.5 mm)
• Transmission (no bunch merge)
~ 60 %
• Channel length
380 m → 280 m
Initial 6D cooling
325 MHz cooling
650 MHz
Matching
•
•
•
•
•
Simulation study for longitudinal enhance cooling
is just begun.
More result will be shown by next meeting.
Longitudinal enhance cooling
Bz = 10.4 Tesla
Equal cooling
decrements

## Slide 14: Power estimation
Section | Units | 1 | 2 | 3 | 4
, period | m | 1.0 | 0.8 | 0.5 | 0.4
bT/bL (equal) | m | 0.20/2.1 | 0.16/2.1 | 0.098/1.5 | 0.079/1.5
Length | m | 80 | 50 | 100 | 50
HS Coil Rin | mm | 275 | 217 | 105 | 100
HS Coil Rout | mm | 300 | 247 | 195 | 190
Coils/period |  | 10 | 10 | 10 | 10
Coil Length | mm | 100 | 80 | 50 | 40
J, curr density | A/mm2 | 258.2 | 271.4 | 149.1 | 188.8
Anti solenoid | T | -2.49 | -3.21 | -8.78 | -7.15
Stored B | MJ/m | 4.84* | 4.7 | 10.7 | 10.5
RF gradient | MV/m | 20 | 20 | 20 | 20
RF frequency | MHz | 325 | 325 | 650 | 650
Peak power | MJ/m | 11 (36)** | 11 (36) | 13 (50) | 13 (50)
*HS coil
+Anti Sol
**77 K
operation
(300 K)

## Slide 15: Summary
Progress on HCC machine design
  Re-evaluation & Re-optimization based on recent experimental results
Longitudinal enhance cooling is considerable option for later 6D cooling stage
  Significantly reduce the geometry constraint
  HCC does not have any limit due to longitudinal space charge
We should evaluate hydrogen safety if the gas filled channel is the solution