## Slide 1: Development of a 6TeV Muon Collider Design
Min-Huey Wang, Yuri Nosochkov, Yunhai Cai
MAP 2014 Winter Meeting (3-7 Dec., 2014), SLAC USA

## Slide 2: Outline
Introduction
Linear optics
Chromatic correction
Dynamic aperture optimization
Summary

## Slide 3: Introduction
CMS energy 6 TeV (future high energy collider)
High luminosity
Low b∗ at IP
Small circumference (6.3 km)
Sufficient momentum acceptance
Sufficient dynamic aperture for a beam with normalized emittance of ~25 mmrad
Absence of long straights to avoid hot spot of neutrino radiation

## Slide 4: IR linear optics for 6 TeV design
IP
-I
-I
DS
DS
b*x,y =1 cm
Field@poletip:
<15 T in quads
<20 T in bends
bxmax = 6.0 Km
bymax = 133.6 Km
L* =6 m

## Slide 5: Arc cell linear optics for 6 TeV design
Modification of the 1.5 TeV design (by Y. Alexahin et al)
Field increased with energy: < 15T in quads, < 20T in bends
mx/my = 0.875/0.875 2p, 8 cells per quarter ring

## Slide 6: 6 TeV complete ring linear optics
Two IPs, twofold symmetry
Circumference: 6.302km; nx/ny = 38.23/40.14

## Slide 7: Aperture of IR magnets
(m)
The half aperture calculation in IR is based on the definition: 5sx,y+ 15 mm

## Slide 8: IR Magnets
Magnet | Half-aperture | Pole tip field | Length
 | (mm) | (T) | (m)
QIR01A | 30 | 14.52 | 1.85
QIR01B | 35 | 14.52 | 1.85
QIR01C | 45 | 14.52 | 1.85
QIR02A | 65 | -14.94 | 2.2
QIR02B | 75 | -14.94 | 2.2
QIR02C | 75 | -14.94 | 2.2
QIR# | 60, 30, 25 | < 15 | 2 (1.7 QIR03,07)
Dipole | 50(66) | < 20 | 4/4.5/5.5

## Slide 9: Main parameters
Parameter | Unit | 1.5 TeV design | 3 TeV design | 6 TeV design
Beam energy | TeV | 0.75 | 1.5 | 3.0
Number of IPs |  | 2 | 2 | 2
Circumference | m | 2730 | 2767 | 6302
b* | cm | 1 | 1 | 1
Tune x/y |  | 18.56/16.58 | 20.13/22.22 (temporary) | 38.23/40.14 (temporary)
Momentum compaction |  | -1.30E-5 | -2.88E-4 | -1.22E-3
Normalized emittance | (p)mm·mrad | 25 | 25 | 25
Momentum spread | % | 0.1 | 0.1 | 0.1
Bunch length | cm | 1 | 1 | 1
Muons/bunch | 1012 | 2 | 2 | 2
Repetition rate | Hz | 15 | 15 | 15
Average luminosity | 1034 cm-2s-1 | 1.1 | 4.5 | 7.1
The average luminosity presented here does not take into account the BB or hourglass factor. The change of luminosity is due to beam energy and circumference.

## Slide 10: Chromatic correction
Local correction of chromatic beta beat and higher order chromatic tune shift created by the final focus quads
Two –I pairs of x and y correction sextupoles placed np in x or y phase from the final focus quads
    large x/y or y/x beta ratio at the IR sextupoles for orthogonal correction
    cancellation of IR sextupole geometric aberrations
    no other sextupoles within each IR sextupole pair to minimize octupole-like tune shift with amplitude
Phase advance of the arc cell (mx = 7/8 × 2p, my = 7/8 × 2p) provides cancellation of the 3rd order and 4th order resonance driving terms locally in each 8-cell quarter ring (except 2nx -2ny).

## Slide 11: Cancellation of IR chromatic W-function
The W function is locally corrected using the –I sextupole pairs
The linear chromaticity is corrected using arc sextupoles
-I
-I
SD
SF

## Slide 12: Beam dynamics properties before optimization
Amplitude tune
Tune footprint
Chromatic tune
Amplitude dependent tune
The vertical aperture is poor
No 0.5 % off- momentum particle survived
Large chromatic nx
Large ny tune shift

## Slide 13: Dynamic aperture optimization
Correction of vertical amplitude dependent tune shift
    Add one octupole at IR location with large beta-y and no dispersion
  Correction of the effect of finite sextupole length
    Add a pair of weak sextupoles near the main –I sextupoles, total two pairs are added.
Correction of horizontal chromatic tune shift
    Add a –I pair of ± sign octupoles at location of large beta-x and dispersion
Improve off momentum dynamic aperture to 0.5%

## Slide 14: Knobs for nonlinear corrections
IP
OCT2 pair
bxmax = 6.0 Km
bymax = 133.6 Km
OCT1
weak sextupoles

## Slide 15: Add octupole OCT1 near the defocusing final doublet quadrupole
Amplitude tune
Tune footprint
Frequency Map
Amplitude dependent tune
Tune footprint
Oct1 = 0.0074(lego) correction of on momentum only
Increase oct1 strength,
gain off -momentum
vertical
aperture
The vertical amplitude dependent tune changes sign

## Slide 16: Correction of the effect of finite sextupole length
Amplitude tune
Tune footprint
Frequency Map
Verify dynamic aperture using thin lense IR sextupoles
The length effect mainly comes from defocussing sextupoles where the beta y is huge
L is main sextupole length
K=0.5

## Slide 17: Correction of horizontal chromatic tune using octupole pair
Amplitude tune
Tune footprint
Frequency Map
Amplitude dependent tune
Add –I octupole pair with ± strengths on one side of the –I focusing sextupoles
Controlle the cubic term of the chromatic nx
Off-momentum dynamic aperture up to 0.5 %

## Slide 18: Optimized dynamic aperture
sx/sy @IP is 3 mm

## Slide 19: Summary
A preliminary design of 6.3 km 6TeV CM energy muon collider ring is presented
The IR chromatic correction scheme uses –I non-interleaved pairs of sextupoles
The arc chromatic correction scheme provides local cancelation of sextupole resonance driving terms in each quarter ring
Orthogonal knobs are implemented to optimize the vertical amplitude dependent tune shift and horizontal chromatic tune shift
The momentum dynamic aperture of bare lattice is up to 0.5%