## Slide 1: QXF 2D Magnetic Analysis & Coil Cross-Section
F. Borgnolutti
04/09/2012

## Slide 2: Outline
Cross-section presented at Frascati in Oct. 2012
Updated Yoke design
Updated cable dimensions (Cable 1042Z-13)
Re-optimized cross-section based on the new cable design
Field harmonics and transfer function
Tuning of the magnetic field to take into account coil deformation
Magnetic field sensitivity to components tolerances
Summary and plans

## Slide 3: Cross-section presented at Frascati
150 mm aperture diameter
140 T/m nominal gradient
Insulation:
  Total mid-plane Insulation thickness: Baseline 0.500 mm (2*250 µm)
  Inter-layer insulation thickness: 0.500 mm
Coil cross-section:
  The coil cross-section is optimized at room temperature/coil aligned on their OD
Conductor specifications:
  RRP
  Conductor specifications @4.2K 2650 A/mm2 @ 12T 1400 A/mm @ 15 T
  Jc curve available on the plone:
https://plone.uslarp.org/MagnetRD/DesignStudies/QX-CD/ShortSample/
Reference design as presented at the Frascati meeting

## Slide 4: Updated Yoke design
Updated yoke design:
Yoke design provided by M. Juchno
Holes for tie rods
New design:
Can still evolve, it is not the final design
Bladder location
Loading keys
Alignment key
Notch
Slot for bus bars
Former yoke design

## Slide 5: Updated Yoke design
“Frascati” coil cross-section in the new yoke:
 | With old yoke | With new yoke | With new yoke + more current
b6 | 0.26 | 0.11 | 0.03
b10 | 0.22 | 0.21 | 0.21
b14 | 0.33 | 0.33 | 0.33
b18 | -0.47 | -0.48 | -0.48
G (T/m) | 140.0 | 138.4 (-1.1 %) | 140
I (kA) | 17.32 | 17.32 | 17.55
The updated yoke cross-section has little impact on the harmonics
Need to increase the current to compensate for yoke material removal (+1.1 %)
Rref=2/3 of the aperture

## Slide 6: Updated cable dimension
Reacted Bare Cable (4.5 % and 2 % thickness and width growth assumed from un-reacted cable) |  |  | 
 |  | Frascati cable (v1) | New version (v2)
Width (mm) | mm | 18.638 | 18.300
Thickness in | mm | 1.462 | 1.454
Thickness out | mm | 1.673 | 1.660
Keystone angle | deg | 0.650 | 0.644
Insulation thickness | mm | 0.150 | 0.125
-0.388 mm
Insulated & Reacted Cable |  |  | 
 |  | Frascati cable (v1) | New version (v2)
Width (mm) | mm | 18.938 | 18.550
Thickness in | mm | 1.762 | 1.704
Thickness out | mm | 1.973 | 1.910
Dimensional changes
-0.338 mm
-0.008 mm
-0.013 mm
-0.006 mm
-0.058 mm
-0.063 mm
-0.025 mm
 The cross-sectional area of the new cable is ̴̴5% smaller than for the one used at Frascati
Cable 1042Z-13

## Slide 7: Updated cable dimension
1
2
3
4
  Block 1: 16 turns  0.5 cable
  Block 2: 6 turns  0.2 cable
  Block 3: 16 turns  0.5 cable
  Block 4: 12 turns  0.4 cable
1.6 cable in total (looking at the thickness)
The chosen coil design layout is “optimum”
How much turns could we add in each block if we want to match the dimension of the “Frascati” cross-section with the new cable?:
Reference design

## Slide 8: Re-optimized cross-section
“Frascati” coil layout with the new cable dimension
 | Changing the cable dimension only | Re-optimized cross-section (one turn added)
b6 | 21.2 | 0.07
b10 | 1.72 | 0.06
b14 | 0.26 | 0.02
b18 | -0.54 | -44
G (T/m) | 140 | 140
I (kA) | 17.32 | 17.00
Additional turn
Rref=2/3 of the aperture
Field quality is achieved
The current is smaller

## Slide 9: Re-optimized cross-section
16
6
16
12
17
6
16
12
“Frascati” cross-section: 50 turns
Updated coil cross-section with
new cable dimension: 51 turns
Additional turn
Easier to protect (quench)

## Slide 10: Re-optimized cross-section
 | Units | V1 | V2
Operational Temp. | K | 1.9 | 
Short sample gradient | T/m | 172 | 174
Short sample current | kA | 21.5 | 21.1
Peak field at Iss | T | 15.0 | 15.1
Nominal Gradient | T/m | 140 | 140
Nominal Current | kA | 17.55 | 17.00
Fraction of Iss | % | 81.6 | 80.6
Peak Field @ In | T | 12.19 | 12.15
Stored energy @ In | MJ/m | 1.33 | 1.310
Diff. inductance @ In | mH/m | 8.26 | 8.67
Nb turn/coil | - | 50 | 51
Chart: Peak field [T]
| 7 | 7.2 | 7.4 | 7.6 | 7.8 | 8 | 8.2000000000000011 | 8.4 | 8.6 | 8.8000000000000007 | 9 | 9.2000000000000011 | 9.4 | 9.6 | 9.8000000000000007 | 10 | 10.200000000000001 | 10.4 | 10.6 | 10.8 | 11 | 11.2 | 11.4 | 11.6 | 11.8 | 12 | 12.2 | 12.4 | 12.6 | 12.8 | 13 | 13.2 | 13.4 | 13.6 | 13.8 | 14 | 14.2 | 14.4 | 14.6 | 14.8 | 15 | 15.2 | 15.4 | 15.6 | 15.8 | 16
1.9 K | 88633.5365 | 85635.1214 | 82752.8021 | 79979.6735 | 77309.4332 | 74736.3139 | 72255.026 | 69860.7067 | 67548.8761 | 65315.3985 | 63156.4487 | 61068.4819 | 59048.2074 | 57092.565 | 55198.7047 | 53363.9674 | 51585.8691 | 49862.0856 | 48190.4392 | 46568.8871 | 44995.5102 | 43468.5038 | 41986.1682 | 40546.9013 | 39149.1911 | 37791.6092 | 36472.8044 | 35191.498 | 33946.478 | 32736.595 | 31560.7579 | 30417.9298 | 29307.1247 | 28227.4044 | 27177.8751 | 26157.6847 | 25166.0206 | 24202.1067 | 23265.2019 | 22354.5976 | 21469.6159 | 20609.6078 | 19773.9519 | 18962.0524 | 18173.338 | 17407.2605
 | 0 | 17000
 | 17000
 | 17000 | 21100
4.2 K | 74754.7068 | 72024.2122 | 69401.464 | 66880.1386 | 64454.4623 | 62119.15 | 59869.3522 | 57700.6093 | 55608.8112 | 53590.1624 | 51641.1508 | 49758.5206 | 47939.2484 | 46180.5215 | 44479.7193 | 42834.3961 | 41242.2659 | 39701.1895 | 38209.1615 | 36764.3 | 35364.8365 | 34009.1071 | 32695.5445 | 31422.6705 | 30189.0896 | 28993.4829 | 27834.6026 | 26711.2669 | 25622.3556 | 24566.8059 | 23543.6083 | 22551.8034 | 21590.4784 | 20658.7644 | 19755.8331 | 18880.8951 | 18033.1967 | 17212.0182 | 16416.6719 | 15646.5 | 14900.8729 | 14179.188 | 13480.8675 | 12805.3576 | 12152.127 | 11520.6657
 | 17550 | 21550
 | 0 | 17550
 | 17550
V1: “Frascati” x-section + new yoke
V2: Updated x-section with new cable and new yoke
V1
V2

## Slide 11: Magnetic field and transfer function
Chart: I/In
| 1.0000000000000009E-3 | 0.12590000000000001 | 0.25069999999999998 | 0.37560000000000027 | 0.5 | 0.6254000000000004 | 0.75020000000000042 | 0.87510000000000043 | 1
b6 | 2.8845 | 2.7808 | 3.0942 | 4.351 | 4.2257 | 3.1579 | 1.8982 | 0.88846 | 0.06986
b10 | 0.02356 | 0.01757 | 0.00661 | 0.02806 | 0.05047 | 0.05851 | 0.05803 | 0.05744 | 0.05703
b14 | 0.01913 | 0.01899 | 0.01806 | 0.01732 | 0.01733 | 0.01746 | 0.01752 | 0.01759 | 0.01766
b18 | -0.40168 | -0.40257 | -0.40882 | -0.41501 | -0.4207 | -0.42658 | -0.43218 | -0.43679 | -0.44065
Chart: I/In
| 1E-3 | 0.12590000000000001 | 0.25069999999999998 | 0.37559999999999999 | 0.5 | 0.62539999999999996 | 0.75019999999999998 | 0.87509999999999999 | 1
 | 1 | 0.99776 | 0.98268 | 0.96802 | 0.95579 | 0.94161 | 0.9291 | 0.91968 | 0.91027
9 % reduction on the TF at nominal current
Maximum of b6 of about 4.5 unit reached at I ≈ 0.4 In
Updated x-section with new cable

## Slide 12: Tuning of the magnetic field
Coil cross-sections are optimized at room temperature (does not take into account for coil deformation)
Estimated variation of the field components due to coil deformation
(see M. Juchno’s presentation)
  Most of the coil deformation is provided during cool-down
Harmonic | Value (unit)
b6 | +0.97
b10 | -0.03
b14 | +0.04
Need a cross-section that generate b6 ≈ -1 unit at room temperature
Impact of coil deformation on b10 and b14 is negligible

## Slide 13: Tuning of the magnetic field
A b6 of -1 unit can be easily generated without dramatically changing other harmonic components by moving the upper block of the outer layer by ~380 um
Harmonic order | Generated by coil deformation | Generated by the coil at room temperature
b6 | +0.97 | -1.05
b10 | -0.03 | 0.26
B14 | +0.04 | 0.019
B18 | - | -0.442
+380 um

## Slide 14: Magnetic field compensation
Chart: I/In
| 1.0000000000000013E-3 | 0.12590000000000001 | 0.25069999999999998 | 0.37560000000000032 | 0.5 | 0.62540000000000062 | 0.75020000000000064 | 0.87510000000000066 | 1
b6 | 2.8845 | 2.7808 | 3.0942 | 4.351 | 4.2257 | 3.1579 | 1.8982 | 0.88846 | 0.06986
 | 1.8845 | 1.7808 | 2.0942 | 3.351 | 3.2257 | 2.1579 | 0.89817 | -0.11154 | -0.93014
Maximum of b6 of reduced from 4.5 unit to 3.5 unit reached at I ≈ 0.4 In

## Slide 15: Field sensitivity to components tolerances
Method
Pole piece with defect
Cable insulation is thinner on the thin edge
Cable insulation is thicker on the thick edge
Realistic model
Matlab model is used (analytical equations)
The yoke is not considered
Example of method applied to a defect on the pole piece
Nominal pole dimension

## Slide 16: Field sensitivity to components tolerances
Chart: Skew multipole
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Defect on the pole piece | 0.1799 | 0.01644 | 0.083846 | 0.045829 | 0.028564 | 0.023836 | 0.0080298 | 0.0020335
Defect on wedge thickness | 0.11569 | 0.081536 | 0.062748 | 0.021215 | 0.031994 | 0.0097452 | 0.015836 | 0.010804
Defect on the wedge radial position | 0.039784 | 0.030125 | 0.024113 | 0.006901 | 0.012142 | 0.0031619 | 0.0055011 | 0.0039112
Defect on L1 inner radius | 0.41086 | 0.35795 | 0.17697 | 0.17551 | 0.056881 | 0.041663 | 0.013356 | 0.011929
Defect on L2 inner radius | 0.22928 | 0.1842 | 0.070118 | 0.04502 | 0.015014 | 0.0074412 | 0.0018258 | 0.00035608
Defect on the mid-plane | 0.24394 | 0.1976 | 0.13057 | 0.068291 | 0.050001 | 0.017093 | 0.01986 | 0.0041343
Chart: Skew multipole
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Defect on the pole piece | 0.1799 | 0.01644 | 0.083846 | 0.045829 | 0.028564 | 0.023836 | 0.0080298 | 0.0020335
Defect on wedge thickness | 0.11569 | 0.081536 | 0.062748 | 0.021215 | 0.031994 | 0.0097452 | 0.015836 | 0.010804
Defect on the wedge radial position | 0.039784 | 0.030125 | 0.024113 | 0.006901 | 0.012142 | 0.0031619 | 0.0055011 | 0.0039112
Defect on L1 inner radius | 0.41086 | 0.35795 | 0.17697 | 0.17551 | 0.056881 | 0.041663 | 0.013356 | 0.011929
Defect on L2 inner radius | 0.22928 | 0.1842 | 0.070118 | 0.04502 | 0.015014 | 0.0074412 | 0.0018258 | 0.00035608
Defect on the mid-plane | 0.24394 | 0.1976 | 0.13057 | 0.068291 | 0.050001 | 0.017093 | 0.01986 | 0.0041343
Chart: Normal multipole
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Defect on the pole piece | 0.16802 | 0.17285 | 0.078834 | 0.049998 | 0.031839 | 0.0026467 | 0.0087438 | 0.004698
Defect on wedge thickness | 0.10746 | 0.092133 | 0.063949 | 0.071893 | 0.032698 | 0.032129 | 0.015442 | 0.010485
Defect on the wedge radial position | 0.0396 | 0.033344 | 0.024423 | 0.024512 | 0.011956 | 0.011434 | 0.0054462 | 0.0036116
Defect on L1 inner radius | 0.42082 | 0.22056 | 0.1955 | 0.0094589 | 0.062536 | 0.010475 | 0.014397 | 0.0016007
Defect on L2 inner radius | 0.22805 | 0.081402 | 0.072969 | 0.0032117 | 0.015285 | 0.0043105 | 0.0018006 | 0.00029518
Defect on the mid-plane | 0.25419 | 0.16994 | 0.12932 | 0.09184 | 0.051034 | 0.044003 | 0.020042 | 0.016019
Defects with following Gaussian distribution with σ = 25 um , values >25 um are discarded
New tool to estimate field error due to parts/fabrication defects.

## Slide 17: Summary and Plans
Two cross-sections have been studied:
  “Big” cable with 150 um thick insulation
  “Small” cable with 125 um  one additional turn + less current
Compensation of b6 to take into account for coil deformation at cold:
  It easy to compensate one unit of b6
  Do we want to implement now a correction of b6 of 1 unit to compensate for cool down effect?
Magnetic shimming?