## Slide 1: DUNE (SP) and SBND TPC Field Cage Designs
Bo Yu (yu@bnl.gov)
Brookhaven National Lab

## Slide 2: The Field Cage Reference Designs of DUNE SP and SBND
58m
12m
14.5m
Are nearly identical
Both are made from copper strips on FR4 substrates
DUNE: 2000m2, 248 modules SBND: 72m2, interconnected panels
4m
4m
5m

## Slide 3: Previous PCB Based LArTPC Field Cage Constructions
ArgoNeut / LArIAT (0.5m drift)
Bo / Long Bo TPCs (0.5 / 2.0m drift)
Cellular Panel for FLARE
For high voltage/long drift, the electric field at the sharp copper strip edges is very high

## Slide 4: Field Cage of the 35ton TPC
Electric field along a line at the edges of the copper strips
Electric field [V/m]
lower strip upper strip
Red: left edges Green: right edges
In order to avoid exposing the high electric field at the edges of the copper strips, the solution for the 35ton TPC is to cover the edges of the copper strips with solder mask, a standard PCB fabrication technique. The catch is that we need a thicker layer than on typical PCBs.
The standard solder mask material for rigid FR4 boards are not very resilient in thick sections and may be damaged during assembly.
Maximum E field in liquid ~ 15kV/cm
External E field: 4.4kV/cm
Slot in the PCB

## Slide 5: Field Cage in DUNE FD and 35ton
The reference design is the light weight, PCB based field cage. The copper edges are covered by a thick layer of polymer with high dielectric strength (solder mask) to reduce the electric field exposed to the LAr. Surge suppressor will be installed in parallel with resistors along the divider.
A 2.3m x 3.6m field cage module for DUNE FD.
A corner of the 35ton TPC field cage during a trial assembly.

## Slide 6: 35 ton Field Cage PCB Features
¼” pins
Size 4 screws
Clearance holes for the resistor leads
Holes for the blind rivets
Total inter-strip capacitance from all four sides of the field cage ~ 3.5nF.
Nominal strip to ground capacitance ~ 10pF
Inside copper strip pattern
Outside copper strip pattern
The PCBs have copper strips on both sides. The strips outside the TPC are shifted by one strip pitch for most of their length, forming additional capacitance between strips.

## Slide 7: 35ton Field Cage Corner
Made of double sided 0.2mm thick FR4 substrate.
The vertical edge is mechanically and electrically connected to the larger side panel. Spring contacts on the top edge ensure electrical connection to the top panel.
Spring contact thermal relief
Eyelet holes to attach to the side panel
Notch for the CPA frame

## Slide 8: The Reservations about the PCB Construction
Cost
  Preferable to use large PCB panels to minimize assembly labor and reduce number of interconnect along strips
  Large PCB panels only available from limited specially shops and therefore are expensive
HV stability
  The solder mask at the copper strip edges are relatively fragile. It could get damaged in a mechanical impact (through rough handling) or a HV discharge. This is particularly important for large production
  Once the insulating layer is off, the exposed E field at the Cu strip edges will be high, even at normal operating conditions.

## Slide 9: Alternate DUNE Field Cage Design
A more robust field cage can be constructed with roll-formed metallic profiles. The example below shows the electric field on the highest biased field cage electrodes (180kV) can be controlled to under 12kV/cm using this profile even with only a 20cm ground clearance. If we can find a safe way of dealing with the ends of the profiles, this construction could allow a reduction in the top and bottom TPC clearance and make more efficient use of the LAr.

## Slide 10: Field at the Corner, Profile 1071
-180kV, 20cm to ground
Radius of curvature: 10cm
Max E field < 18kV/cm
Symmetry planes
+ the top and bottom faces
ground
Exploring manufacturing options:
- Bending roll-formed profile is difficult
- Machining solid profile possible

## Slide 11: Additional Views of the Design
Resistive divider and surge suppressor chain
Corner treatment (5mm thick UHMW PE caps, and optional PE angles) to minimize the exposed electric field

## Slide 12: FEA of the Field Cage Corner with PE Caps
20cm ground clearance, -180kV, UHMW PE cap thickness: 5mm
The exposed field in the LAr is ~ 25kV/cm
The field in the LAr is ~ 50% higher than the PE cap surface due to dielectric constant difference
Plot of the E field on the symmetry plane bisecting the metal profiles

## Slide 13: Roll-Formed Field Cage Test Setup
To validate the field cage concept in pure LAr
Designed to fit in the ICARUS 50 liter cryostat
Roll-formed metal profiles with UHMW PE caps
  Choice of metal (Al, SS) and surface finish
Pultruded fiberglass I-beams form 4 mini panels
All profiles are at same potential to simplify HV connection
Perforated ground planes 66mm away
Requires 1/3 of FD bias voltage to reach same E field
Ground planes can be connected to external amplifiers to monitor micro-discharges
PMT detects any light from discharges

## Slide 14: Pros and Cons of the Two Designs
 | PCB Design | Metal Profile
Unit cost [$/m2] | ~ 2000* | ~ 130**
Weight [kg/m2] | ~4 | ~ 10 (SS) ~ 3 (Al)
Robustness | Fair | Good
Compliance to TPC distortion | Poor | Good
Ease of assembly | Good | Fair
Built-in Inter-strip Capacitance | Yes | No
Reflectivity to visible light | Low | Hign
Max Field in LAr @ 180kV & 50cm ground clearance | ~15kV/cm | ~5kV/cm
*based on TriLabs quote for 35ton; **based on quote for SS profile. Mechanical support structure, divider boards excluded.

## Slide 15: Comments
Neither designs have been experimentally verified
  35ton will test the PCB construction (2.2m drift)
  Roll-formed field cage will be tested in ICARUS 50 liter cryostat (small scale, full field). Need to have full voltage test to be sure (HVC?).
  For the SBND PCB design, need to test a more robust solder mask (not on SBND schedule)
DUNE SP is moving forward to develop the roll-formed field cage for its low cost, small ground clearance, robust construction
SBND chose to stay with PCB construction without further R&D for budget reason (but may not be able to afford the cost of the PCBs)
If the roll-formed field cage is proven to hold the high voltage, it would benefit SBND for its lower cost, and perhaps the higher reflectivity to visible light.
QA on either designs in a production environment need to be addressed.

## Slide 16: Additional Slides

## Slide 17: Field Cage Divider Resistivity Range
Argon 39: 1bq/kg, average energy: 220keV
TPC drift cell: 2.3mx6mx3.6mx1.4=70t
  70kHz @ 220keV/23.6 = 6.5E8 e = 0.1nA
  Each CPA wall is connected to ~ 124 divider chains
  Upper limit: 1mA power supply to 124 divider chains: 8µA each divider
  If we want one supply to feed 2 CPA walls in an emergency, each CPA must draw <4µA
  180kV/60Gohm = 3µA

## Slide 18: Field Cage with Resistive Coating
Applying a resistive coating over the copper strips will completely remove the edge effect of the strips. The resistance between strips from the coating needs to be much higher than the resistive divider value to ensure a uniform drift field. The coating must maintain good bonding strength to the PCB substrate during repeated thermal cycles, and be resistant to impact and scratches during manufacturing and assembly steps. If a suitable coating can be found, this seems to be the most effective way of reducing edge field.
Resistive coating
Copper strip
Common development with the resistive cathode;

## Slide 19: Field Cage Transient Response in a Discharge
The resistors along the divider provide a linear DC voltage gradient.
However, at shorter time scale (<<1s), the electrical behavior of the divider is determined by the varies capacitances on and between each electrodes. This divider is no longer linear at this time scale.
A perfect capacitive divider requires the capacitance of each node to ground to be 0. In reality, there is always a finite capacitance from each node to ground. These capacitances “resist” change in the voltages on the nodes.
In the event of a HV breakdown between the cathode to ground (cryostat), the cathode voltage quickly collapses to ground, but the first field cage strip to ground capacitance keeps its voltage from changing instantaneously to follow the cathode voltage, results in a momentary larger voltage differential between the cathode and the first field cage strip.
This voltage differential can be a significant fraction of the cathode operating bias, large enough to cause HV breakdown between the two electrodes, or worse yet, destroy the resistors between the two electrodes.
The natural solution to this problem is to add additional capacitance between the nodes of this divider.
See MicroBooNE docdb 3307 for summary of the analyses

## Slide 20: Maximum Voltage Difference Tube-to-Tube for a discharge from the cathode or any of tubes
MicroBooNE: Added Capacitors: gaps 1-14: 10nF, gaps 15-21: 5nF, gap 22: 2.5nF
MicroBooNE:
Red: no added capacitors
Blue: add 22 capacitors
Discharge probability
35ton field cage w/ 3.5nF : <8kV
Analysis by S. Rescia

## Slide 21: Surge Suppressor Studies
An alternative to adding capacitance between divider nodes is to use surge protection
Extensive tests have been done by MicroBooNE (docdb 3242, arXiv:1406.5216v2) on the use of varistors and GDTs (gas discharge tubes) as a mean of limiting the over voltage condition in the event of a HV discharge in the TPC.
Both types will work for the purpose of restricting the voltage differential between field cage rings in LAr temperature.
  A GDT quickly shorts the terminals when the voltage differential exceeds a threshold
  A varistor changes its resistance to keep the voltage differential near the threshold voltage.
The smooth transition and well defined clamping voltage of the varistors are preferred to the abrupt switching of the GDTs.
The varistors would also function as redundant “resistors” in a divider chain.
Left: varistor
Right: GDT

## Slide 22: Field Cage with Profile # 1746
Ground plane 20cm above
-180kV
-177kV
-174kV
Pitch 6cm (3kV)
Max. E field ~15kV/cm
6cm

## Slide 23: Field Cage with 38mm tube (1.5”)
Ground plane 20cm above
Pitch 6cm (3kV)
Max. E field ~15kV/cm
6cm

## Slide 24: Field Cage + Ground Plane

## Slide 25: E Field at a GTT Knuckle
When faced with a 180kV conductive plane 20cm above the knuckle tip:
The maximum E field at the tip of the knuckle is 40kV/cm.
The field at the ridges of the corrugation is about 20kV/cm.
The facing HV plane has a maximum E field of 7.5kV/cm, average about 7.4kV/cm.
At 50cm clearance:
The tip field <15kV/cm
At the HV plane: E~3.3kV/cm
Based on these field values, the equivalent “flat” membrane distance is about 3cm above the real membrane flat: 180kV/7.4kV/cm ~24 cm, 180kV/3.3kV/cm~54cm.
40kV/cm in the liquid near the top of cryostat is high. But on the bottom of the cryostat where the pressure is 2atm higher and boiling point is 11K higher than the liquid temperature, the field may be acceptable.

## Slide 26: Comparison of Screw Heads
3kV/cm nominal field, screw length 0.25”.
6-32 screws, G10 plate