## Slide 1: Update of D1 Design and R&D Status
T. Nakamoto, Q. Xu, M. Iio, T. Ogitsu, K. Sasaki, N. Kimura, M. Sugano, M. Yoshida, A. Yamamoto, E. Todesco
Spring joint LARP/HiLumi-LHC Collaboration Meeting at Napa Valley CA.
8-10 April 2013

## Slide 2: Outline
Conceptual Design for D1 (MBXF) with Some Variants
2-m Long Model Magnet Development
Irradiation Tests: interim report
Summary

## Slide 3: Objective: New D1
Current D1 (MBXW) at IR1 & IR5
New D1 (MBXF)
For HL-LHC upgrade, needs for new Inner Triplet system at IR1 & IR5.
  Large aperture (150 mm) HF Quadrupoles, corrector package.
New beam separation dipole (D1) should be accommodated with large aperture IT Quads; which will have a even larger aperture than IT Quads and 50% increase in original integrated field (26 T m 35~40 T m).
Schematic layout of the IR
Schematic layout of the LHC

## Slide 4: Main Design Parameters: MBXF
20
14
9
4
Stress management
High saturation, stray field, flux return cryostat
Radiation resistance, cooling capability
47 turns
Option 1
Coil ID: 160 mm
Integrated field: 35 - 40 T m ( > 26 Tm for LHC)
  5.2 T at 11 kA. Lcoil=6.8 - 7.7 m (1 or 2 cold masses)
Top: 1.9 K
Op. point: 70 %
Coil layout: 1 layer of 15 mm cable
  Better cooling. Saving space for iron yoke.
Conductor: Nb-Ti LHC dipole cable (outer)
Structure: Collaring yoke structure
  RHIC dipole, MQXA, J-PARC SCFM
  Enhancing iron material for stray field issue
Field quality: < 10-4 at Rref = 50 mm
Cold mass OD: 550 +10 x 2 = 570 mm
Radiation, energy deposition:
< 40 MGy, several W/m, ~5 mW/cm3 ??

## Slide 5: Design Variants for D1
 | LHC outer cable & 50 mm HX hole | LHC inner cable & 50 mm HX hole | LHC inner cable with 80 mm HX hole | 20 mm cable (inner strand) & 50 mm HX hole
# of turns | 47 | 39 | 39 | 39
Nominal field (dipole) | 5.23 T | 5.47 T | 5.49 T | 5.90 T
Magnetic length | 7.65 m | 7.3 m | 7.3 m | 6.78 m
Operating current | 11 kA | 14 kA | 14.2 kA | 15.8 kA
Injection current | ~ 0.7 kA | ~ 0.9 kA | ~ 0.9 kA | ~ 1 kA
Peak field in the coil | 6.1 T | 6.5 T | 6.5 T | 6.9 T
Load line ratio | 70% @ 1.9 K ／91% @ 4.2 K |  |  | 
Inductance (low / nominal) | 6.58 / 5.91 mH/m | 4.6 / 3.1 mH/m | 4.5 / 4 mH/m | 4.5 / 3 mH/m
Stored energy | 331 kJ/m | 361 kJ/m | 367 kJ/m | 447 kJ/m
Lorenz force X/Y (1st quadrant) | 1.4/0.6 MN/m | 1.6/0.7 MN/m | 1.6/0.7 MN/m | 1.9/0.8 MN/m
Outer dia. of iron yoke | 550 mm |  |  | 
Inner dia. of iron yoke | 232 mm |  |  | 
Strand diameter | 0.825 mm | 1.065 mm |  | 
Cu/Non-Cu ratio | 1.95 | 1.65 |  | 
Cable dimension (bare) | 15.1* 1.48 mm2 | 15.1* 1.9 mm2 |  | 20* 1.9 mm2
No. of strands | 36 | 28 |  | 37
Keystone angle | 0.9 ° | 1.24 ° |  | 1.15 °
Total length of the cable | 752 m (Coil length ~8 m) | 600 m (Coil length ~7.7 m) |  | 554 m (Coil length ~7.1 m)
Option 1
Option 2
Option 3
Option 4

## Slide 6: Option 2: Inner Cable
¼ Cross section
including cryostat
¼ Coil layout
17
11
7
4
Load line ratio: 70% @ 1.9 K;
Nominal current: 14 kA;
Main field: 5.47 T @ Rref = 50 mm;
Magnetic length: 7.4 m;
Stray field outside of cryostat: 50 mT;
Cable parameters: 15.1 * 1.736 / 2.064 mm2, 28 (LHC dipole inner) strands.
Stray field at the outer surface of the cryostat

## Slide 7
¼ Cross section
including cryostat
¼ Coil layout
17
11
7
4
Load line ratio: 70% @ 1.9 K;
Nominal current: 15.8 kA; beyond P.S. limit at KEK
Main field: 5.90 T @ Rref = 50 mm;
Magnetic length: 6.8 m;
Stray field outside of cryostat: 78 mT;
Cable parameters: 20 * 1.7 / 2.1 mm2,
37 (LHC dipole inner) strands.
* New cable development necessary.
Stray field at the outer surface of the cryostat
Option 4: 20 mm wide cable

## Slide 8: Holes for HX or HeII Conduction Cooling
Improvement of heat transfer against energy deposition ( < 10 W/m ?):
Holes for internal HX, voids for longitudinal conduction cooling by HeII.
Baseline cross section: 2 x f 50 mm + 8 x f 30 mm + etc. = 174 cm2 >> Option 1, 2
New cross section: 2 x f 80 mm + 8 x f 30 mm + etc. = 235 cm2 >> Option 3
* Control of iron saturation
Option 1, 2
Option 3

## Slide 9: Variation of Multipole Coefficients: b3 (2D)
Chart: Current (kA)
| 0.49948 | 0.99947 | 1.4995 | 1.9995 | 2.4995 | 2.9995 | 3.4995 | 3.9995 | 4.4995 | 4.9995 | 5.4995 | 5.9995 | 6.4995 | 6.9995 | 7.4995 | 7.9995 | 8.4995 | 8.9995 | 9.4995 | 9.9995 | 10.499 | 9.9995 | 9.4995 | 8.9995 | 8.4995 | 7.9995 | 7.4995 | 6.9995 | 6.4995 | 5.9995 | 5.4995 | 4.9995 | 4.4995 | 3.9995 | 3.4995 | 2.9995 | 2.4995 | 1.9995 | 1.4995 | 0.99947 | 0.49948
LHC_Outer_cable_HX50_b3 | -22 | -8.73 | -5.44 | -4.07 | -3.35 | -2.91 | -2.64 | -2.47 | -2.31 | -2.16 | -2.6 | -2.82 | -2 | -1.19 | -0.458 | 0.885 | 1.46 | 1.57 | 1.39 | 0.882 | 0.0138 | 1.42 | 1.97 | 2.2 | 2.13 | 1.59 | 0.29 | -0.378 | -1.11 | -1.82 | -1.47 | -0.847 | -0.77 | -0.636 | -0.399 | -0.0908 | 0.355 | 1.08 | 2.41 | 5.44 | 16.4
LHC Inner cable_HX50_b3 | -10.994 | -3.2506 | -1.3262 | -0.52985 | -0.14218 | 0.18367 | -0.33739 | 0.54766 | 1.5988 | 3.2281 | 3.593 | 3.0375 | 1.6874 | -0.14834 | 2.3112 | 3.719 | 4.3489 | 4.0765 | 2.5542 | 1.6353 | 0.96133 | 1.8126 | 2.0045 | 2.4782 | 3.2951 | 5.1566 | 12.046
LHC_Inner_cable_HX80_b3 | -31.532 | -10.781 | -5.5137 | -3.3156 | -2.1543 | -1.4555 | -1.0005 | -0.70262 | -0.49603 | -0.32064 | -0.075836 | 0.098711 | -0.15484 | -0.087432 | 0.3753 | 1.0823 | 1.3901 | 1.7543 | 2.8137 | 3.7399 | 4.1666 | 3.1993 | 3.2516 | 3.381 | 2.7069 | 1.9383 | 1.0455 | 0.13512 | -0.83869 | 0.68489 | 1.6521 | 2.5558 | 3.3498 | 4.0497 | 3.9578 | 3.949 | 4.9546 | 4.5865 | 3.689 | 2.6812 | 2.3691 | 2.125 | 1.515 | 1.1816 | 1.2836 | 1.6317 | 1.7692 | 1.7675 | 1.9452 | 2.2055 | 2.5596 | 3.0227 | 3.7097 | 4.8274 | 6.8789 | 11.507 | 28.168
Option 1
Option 2
Option 3
Injection current
Nominal current

## Slide 10: Variation of Multipole Coefficients: b5 and higher (2D)
Chart: Current (kA)
| 0.499 | 0.999 | 1.5 | 2.0 | 2.5 | 3.0 | 3.5 | 4.0 | 4.5 | 5.0 | 5.5 | 6.0 | 6.5 | 7.0 | 7.5 | 8.0 | 8.5 | 9.0 | 9.5 | 10.0 | 10.5 | 11.0 | 11.5 | 12.0 | 12.5 | 13.0 | 13.5 | 14.0 | 14.5 | 14.0 | 13.5 | 13.0 | 12.5 | 12.0 | 11.5 | 11.0 | 10.5 | 10.0 | 9.5 | 9.0 | 8.5 | 8.0 | 7.5 | 7.0 | 6.5 | 6.0 | 5.5 | 5.0 | 4.5 | 4.0 | 3.5 | 3.0 | 2.5 | 2.0 | 1.5 | 0.999 | 0.499
b5 | -2.9383 | -2.4591 | -2.0998 | -1.9314 | -1.8391 | -1.7842 | -1.748 | -1.7248 | -1.7079 | -1.7034 | -1.7222 | -1.7922 | -2.0081 | -2.3335 | -2.7322 | -3.057 | -3.2911 | -3.3919 | -3.3192 | -3.1265 | -2.8256 | -2.5536 | -2.0785 | -1.6178 | -1.2179 | -0.84352 | -0.50756 | -0.18412 | 0.11125 | -0.087036 | -0.39147 | -0.72549 | -1.0975 | -1.4939 | -1.9483 | -2.4165 | -2.6851 | -2.9803 | -3.1762 | -3.2523 | -3.1575 | -2.9321 | -2.6088 | -2.2063 | -1.8742 | -1.6258 | -1.5648 | -1.5331 | -1.5142 | -1.4985 | -1.4771 | -1.4505 | -1.4117 | -1.3504 | -1.2426 | -1.0187 | -0.41127
b7 | 0.53432 | 1.093 | 1.3571 | 1.4818 | 1.5501 | 1.591 | 1.618 | 1.6367 | 1.6503 | 1.6589 | 1.6606 | 1.6475 | 1.606 | 1.5329 | 1.403 | 1.2095 | 0.96028 | 0.70242 | 0.46902 | 0.28435 | 0.15779 | 0.078029 | 0.036643 | -0.002126 | -0.020485 | -0.032491 | -0.041093 | -0.043304 | -0.044173 | -0.002765 | 0.0076982 | 0.018944 | 0.032645 | 0.053572 | 0.095847 | 0.14103 | 0.22355 | 0.35335 | 0.53926 | 0.77322 | 1.0314 | 1.2799 | 1.4758 | 1.6102 | 1.6914 | 1.746 | 1.7641 | 1.7765 | 1.7875 | 1.8003 | 1.8175 | 1.8414 | 1.8771 | 1.9345 | 2.0387 | 2.2715 | 3.082
b9 | -0.23383 | -0.52667 | -0.55462 | -0.55971 | -0.56119 | -0.56206 | -0.56259 | -0.56287 | -0.5629 | -0.56235 | -0.55994 | -0.55416 | -0.54259 | -0.52071 | -0.48638 | -0.44815 | -0.41837 | -0.40078 | -0.39454 | -0.39292 | -0.39219 | -0.38822 | -0.38555 | -0.3871 | -0.38419 | -0.38167 | -0.37921 | -0.37599 | -0.37263 | -0.37384 | -0.37455 | -0.37639 | -0.3789 | -0.38149 | -0.37936 | -0.38141 | -0.38512 | -0.38556 | -0.38747 | -0.3945 | -0.41316 | -0.44478 | -0.48415 | -0.5195 | -0.54255 | -0.55667 | -0.56154 | -0.56493 | -0.5664 | -0.56742 | -0.56858 | -0.5702 | -0.57275 | -0.57719 | -0.58613 | -0.60945 | -0.71322
b11 | -0.91869 | -0.73922 | -0.68518 | -0.65992 | -0.64599 | -0.6375 | -0.63189 | -0.62793 | -0.62505 | -0.62304 | -0.62205 | -0.62208 | -0.62388 | -0.62878 | -0.63626 | -0.64319 | -0.64865 | -0.65356 | -0.65925 | -0.66636 | -0.67484 | -0.68365 | -0.693 | -0.70299 | -0.71179 | -0.72042 | -0.72874 | -0.73659 | -0.74404 | -0.73161 | -0.72259 | -0.71371 | -0.70472 | -0.69544 | -0.68482 | -0.67478 | -0.66535 | -0.65616 | -0.6484 | -0.6421 | -0.63654 | -0.63058 | -0.62271 | -0.61402 | -0.6076 | -0.60357 | -0.60127 | -0.59905 | -0.59686 | -0.59416 | -0.59051 | -0.58533 | -0.57756 | -0.56492 | -0.54165 | -0.48873 | -0.29686
With LHC inner cable and HX80 iron yoke
Option 2
Option 3
Chart: Current (kA)
| 0.9993 | 1.9993 | 2.9993 | 3.9993 | 4.9993 | 5.9993 | 6.9993 | 7.9993 | 8.9993 | 9.9993 | 10.999 | 11.999 | 12.999 | 13.999 | 12.999 | 11.999 | 10.999 | 9.9993 | 8.9993 | 7.9993 | 6.9993 | 5.9993 | 4.9993 | 3.9993 | 2.9993 | 1.9993 | 0.9993
b5 | -0.686 | -0.052445 | 0.11835 | 0.18849 | 0.22047 | 0.15324 | -0.28235 | -1.0575 | -1.8196 | -1.8862 | -1.4446 | -0.92954 | -0.48725 | -0.088222 | -0.36524 | -0.79886 | -1.3032 | -1.7343 | -1.6682 | -0.91477 | -0.14055 | 0.31079 | 0.41408 | 0.44874 | 0.50309 | 0.62263 | 1.0225
b7 | 0.57898 | 1.0197 | 1.1416 | 1.1926 | 1.2192 | 1.2239 | 1.1667 | 0.97422 | 0.57833 | 0.24154 | 0.07513 | 0.0028707 | -0.027977 | -0.035599 | 0.026151 | 0.062785 | 0.14178 | 0.31561 | 0.65614 | 1.0538 | 1.2528 | 1.3256 | 1.3498 | 1.3744 | 1.4198 | 1.5235 | 1.899
b9 | 0.051223 | 0.020659 | 0.019423 | 0.018974 | 0.019254 | 0.023495 | 0.041631 | 0.096699 | 0.14509 | 0.15713 | 0.16515 | 0.17553 | 0.18498 | 0.19386 | 0.19097 | 0.18243 | 0.17303 | 0.16603 | 0.15315 | 0.1021 | 0.044168 | 0.023757 | 0.017782 | 0.01586 | 0.013328 | 0.0069555 | -0.023463
b11 | 0.35138 | 0.39101 | 0.40388 | 0.4094 | 0.4124 | 0.41356 | 0.41352 | 0.41005 | 0.41448 | 0.42255 | 0.42953 | 0.43489 | 0.43936 | 0.44334 | 0.44384 | 0.44014 | 0.43568 | 0.42978 | 0.42239 | 0.41828 | 0.42247 | 0.42413 | 0.42602 | 0.42849 | 0.43327 | 0.44432 | 0.48485
b13 | -0.39288 | -0.39813 | -0.39843 | -0.39852 | -0.39855 | -0.39853 | -0.39887 | -0.40032 | -0.40426 | -0.40975 | -0.41707 | -0.42509 | -0.43303 | -0.44061 | -0.43289 | -0.42482 | -0.41666 | -0.40915 | -0.40366 | -0.39994 | -0.39873 | -0.39862 | -0.39885 | -0.39904 | -0.39935 | -0.40015 | -0.4038
With LHC inner cable and HX50 iron yoke
Better behavior for HX50 case (Option 2)
Both still acceptable?

## Slide 11: Mechanical Analysis: After excitation (110 % Inom)
Peak local stress > 220MPa around slots.
>> nearly same, but still below Y.S. of JFE steel.
Option 3:
Inner Cable
HX80mm
Higher stress area increased around slots.
Maybe critical, or unfeasible?
Option 1:
Outer Cable
HX50mm
Stresses in both coils are acceptable.

## Slide 12: Coil End Design
Iron covers the whole coil ends currently. Peak field in coil ends is ~ 5% higher than straight section.
Cryostat
Iron yoke
Straight section
Return end
Lead end

## Slide 13: Coil End Design: Lead ends & transition turns
Jump turn
Transition turn
between blocks
Lead end
Straight section
Lead end

## Slide 14: Field Integral & Magnet Length: Option 1 (Tentative)
Chart: 
Chart: 
Chart: 
Return end
Lead end
S.S.
Field Integral | Return End (-2000 < z < -1400) | S.S. (-1400 < z < +1400 mm) | Lead End: (+1400 < z < +2000 mm) | Total
B1 | 1.39E+00 | 1.47E+01 | 1.49E+00 | 1.76E+01
B3 | -9.11E-03 | 1.48E-02 | -7.27E-03 | -1.58E-03
B5 | -3.42E-03 | 1.31E-03 | -2.28E-03 | -4.39E-03
B7 | -1.13E-03 | 2.52E-04 | -7.74E-04 | -1.65E-03
A1 | -- | 8.62E-04 | -5.43E-03 | -4.56E-03
A3 | -- | -1.27E-04 | 1.71E-03 | 1.59E-03
(T m)
*For Mechanical Coil Length: 3.51 m (-1757 < z < +1753)
Field integrals of higher order multipoles are designed to be less than 1 unit w.r.t. that of B1.
Peak field in coil ends is ~ 5% higher than straight section. (Iron yoke fully covers the ends.)
Coil length estimates
  - 35 Tm >> Mechanical coil length 6.82 m
  - 40 Tm >> Mechanical coil length 7.77 m

## Slide 15: Outline
Conceptual Design for D1 (MBXF) with Some Variants
2-m Long Model Magnet Development
Irradiation Tests: interim report
Summary

## Slide 16: Development of 2 m Model
  "Build and test a 2-m model magnet by 2015"
  Funding (model magnets and real machines) from JFY2014 will be proposed in 2013.
  Collaring yoke structure (RHIC, MQXA,J-PARC SCFM)
  Reuse of tooling, jigs, and facilities for SCFM
  Yoke OD < 550 mm (LHC MB)
  In-house development
  Schedule
  JFY 2013
  Engineering design.
  2 Practice coils to be used for mechanical short model.
JFY2014
  Coil winding 1st model, Magnet Assembly.
  Testing at cold.
JFY2015
  2nd model magnet assembly (possibly).
  TDR

## Slide 17: Cable Insulation
NbTi SC cable: LHC MB Inner or Outer layer
Insulation: 2 candidates
  MB-like: Apical tape, cured at 190-197 °C at > 15 MPa.
  improved MQXA-like: Upilex tape w/ prepreg (Cyanate Ester + Epoxy), cured at 150 °C.
P.P. Granieri, 2nd HiLumi Meeting, Frascati, 2012
MB insulation looks having better heat transfer capability.
Insulated inner and outer cables with Apical tapes were delivered from CERN.
10 stack measurements will be made soon.
Radiation resistance?

## Slide 18
Wedges, End Spacers
New radiation resistant GFRPs (w/ S-2 Glass or T-Glass) are baseline.
  Cyanate Ester & Epoxy
  BT (Bismaleimide Triazine)
  BMI (Bismaleimide)
Trial production has been made: prepreg sheets, laminated plates and pipes.
Backup plan (in case of higher dose) would be metallic parts with Polyimide coating by "Vapor Deposition Polymerization" technology.
Irradiation tests underway at RT, up to 100MGy.
  Gamma rays (Co60 ), 2 MeV electron at JAEA Takasaki
  30 MeV electron at KUR
  Irradiation at cold (LN2) ??
Polyimide coating
Alumina plasma spray
After 1.9K
(SUS plates)
CE
BMI
BT
Epoxy
(G10)
GFRP samples for irradiation tests
BT-GFRP pipe (L 1 m, I.D. 160 mm) for wedges and end spacers

## Slide 19
Collar, Yoke
Yoke dies for J-PARC SCFM
Collaring yoke structure (Originated at RHIC-dipole, followed by MQXA)
  Stainless collar as a spacer, vertically split iron yoke locked by keys
  Both collars and yokes should have small dimensional errors (20-30 mm at smallest). >> Fine-Blanking technology
Discussion with a fine-blanking company started in March.
  Some suggestions for the first design.
  Waiting for answers: cost estimates, technical feasibility, delivery time.
A set of fine-blanking die for iron yoke: very expensive, very long delivery time.
  Yoke cross section has to be finalized soon: single or double layer coil, size and location of holes, etc. >> determined by the heat load and the cooling scheme.
Business inquiry will be sent to vendors for stainless steel, iron yoke.
Control of packing factor is crucial to field quality due to high saturation.

## Slide 20: Outline
Conceptual Design for D1 (MBXF) with Some Variants
2-m Long Model Magnet Development
Irradiation Tests: interim report
Summary

## Slide 21
RT Gamma-ray Irradiation Tests: as of March 2013
All new GFRPs (CE&Epoxy, BT, and BMI) have shown better radiation resistance up to 10 MGy.
Samples were irradiated up to 50 MGy by April and evaluation tests will be carried out soon. Irradiation up to 100 MGy will be completed around July 2013.
Ordinary G10 already showed significant degradation at 10 MGy.
G10
CE
BT
BMI
After 13 MGy
Irradiation test results for J-PARC SCFM

## Slide 22: Neutron Irradiation at Cold for Copper (1/2)
Resistance increase due to the neutron irradiation at 12 K
Al-Y1
Cu
Al-Y2
1st cooling before 1st irradiation
2nd cooling before 2nd irradiation
3rd cooling after 2nd irradiation
Copper | 1st Test | 2nd Test
Before Irradiation | 2.61 mW at 13.2 K | 2.78 mW at 13 K
DR by irradiation | 1.07 mW | 1.18 mW
After T.C. | 2.78 mW at 13 K | 2.83 mW at 11 K
Recovery by anneal | 84 % | 96 % ?
Resistance at cool-down

## Slide 23: Neutron Irradiation at Cold for Copper (2/2)
Materials | Copper | Copper | Copper | 
 | Horak | Guinan | OFHC 2011 | OFHC 2012
RRR | 2280 | 172 | 306(10K) | 288(13K)
Tirr (K) | 4.5 | 4.2 | 12 | 15
Netutron Source | Reactor | 14 MeV | Reactor | 
Ftot (n/m2) (>0.1MeV) | 2 x 1022 | 1-2 x 1021 | 2.6 x 1020 | 2.63 x 1020
Drirr/ Ftot x10-31(Wm3) | 0.58 | 2.29 | 0.9 | 1.0
Recovery by thermal cycle | 90% | 80% | 84% | 96 % ?
Comparison: previous and present results.
  differences of degradation rates due to spectrum, fluence (saturation).
  recovery: 80 to 90 % ?
  Note: effects due to charged particle not included.
Deg. rate & fluence per cycle
Very rough estimates of RRR degradation
(Be careful to use this plot…)
Hypothesis
    Deg. rate of 0.95 or 2.3 E-31 (Wm3)
    Same deg. rate applied for charged particles (p, pi)
    Recovery: 85 %
  Reference: Fluence per cycle: < 2 E20 n/m2 (Mokhov, 2nd HiLumi Meeting, Frascati, 2012)

## Slide 24: Outline
Conceptual Design for D1 (MBXF) with Some Variants
2-m Long Model Magnet Development
Irradiation Tests: interim report
Summary

## Slide 25: Summary
Conceptual design study for new beam separation dipole (D1) for HL-LHC upgrade is underway.
  Features: f160mm, 5 T-NbTi at 1.9 K, iron saturation, high stress.
  Some design variants have been considered.
  Design choices should be made "soon" to start the model magnet development.
  To be addressed: quench protection studies.
2-m long practice coil with new insulation materials will be fabricated at KEK in JFY2013, followed by development of a 30-cm long mechanical short model.
  Engineering work has been started. Fabrication area for the model magnet development will be renovated shortly.
  Collaboration (support) with CERN: NbTi cable, QPH, etc.
Radiation resistant materials development and evaluation by irradiation test have been pursued.
  Neutron irradiation effects of copper at LT.
  Radiation resistant materials (CE, BT, BMI, PI): prepreg, GFRP, coating.
Funding proposal for model magnet R&D and real machine construction starting from JFY2014 to KEK and MEXT will be submitted in 2013.