## Slide 1: About MicroBooNE
Engineering Week

## Slide 2: MicroBooNE – liquid argon detector
~200 ton cryostat vessel, ~12m long, ~3.5m OD
TPC – Time Projection Chamber - inside
Vessel – single-walled, insulated.
~70 ton fiducial volume (inside TPC)
2.6m drift (500 V/m) = 1.6ms drift time
3 readout planes (+30-degrees induction, vertical collection)
9,000 channels
Cold pre-amplifiers (sit in gas)
~30 PMTs for trigger
Cryogenic system for purification and recirculation

## Slide 3: Why Lar-TPC?
Why do we want to like these detectors?
  Very fine-grained tracking - Like bubble-chamber pictures
  More – pulse height of hit is proportional to energy
  Tracking and calorimetry
  Might be able to determine if an “EM track” is a single electron or a gamma converting to electron
  Just what you need for neutrino physics
Why aren’t they everywhere?
  Terry’s talk tells you that there are operational difficulties
  More than just purity issues that can soak up your detector signals
  Very small signals from wires – need very low noise electronics

## Slide 4: TPC – how it works
Interactions inside the detector produce ionization particles that drift along electric field lines to readout planes
  Noble gas dielectric properties allows very high voltage applied
  High field pushes a good fraction of ionization along E field – doesn’t re-absorb
  The ionization can be drifted a long way -
  Get a train of pulses, with slight time offsets due to different drift lengths
  Knowledge of the drift velocity, and T0 of events, is used to reconstruct the interaction

## Slide 5: Wire Plane signals
U
V
Y
Induction
(small, bipolar)
Induction
(small, bipolar)
Collection
(large, unipolar)
u
v
y
Simulations using “Garfield” have given us a better understanding of the TPC signals
Under proper bias condition, the first two planes of wires see bipolar induction signals, but do not collect any net charge.
The 3rd wire plane collects 100% of the signal charge, enabling precise measurement of the ionization of a particle track

## Slide 6
Chart: Simulated Current Waveforms at Various Track Angle Collection Wires (Y), 0.6µs rms Diffusion (from left: 0, 10, 30, 60, 70, 80 degrees)
Signal on a single wire for
multi-track event

## Slide 7: Many challenges to making it work
Argon purity – parts per trillion – Terry’s talk
  High purity necessary for long drifts
Electronics
  Signals are small, so sources of electronic noise must be strictly controlled
  Wide range of pulse sizes and shapes
  High sampling rate + many wires = lots of raw data
Vacuum & cryogenics environments take special care
  Every penetration into the cryostat must be leak-tight
  Every penetration increases the heat load on the system
Safety issues
  ODH hazards
  Pressure vessel – (MicroBooNE is evacuable)

## Slide 8: Layout of device
High voltage feedthrough (-128kV)
Cathode plane
Cold electronics
Top ground plane
PMT frame
Wire planes
Field cage
Rails for TPC installation
Signal feedthrough
9% ullage (Argon Gas)

## Slide 9: Details
Top ground plane
Preamp motherboard
Top field cage support beam and bracket
Wire frame
3 wire planes
Shielding mesh

## Slide 10: Electronics – conceptual design
Pre-amp  feed-through  driver  Digitizer board
  2Mhz digitizing rate, 12-bit ADC
  10k channels  data compression, lossless
  16 Mb per event, hundreds Mb/s recorded

## Slide 11: Where
in the existing MiniBooNE enclosure
  Some modifications to the enclosure

## Slide 12: When?
Conceptual to preliminary design starting now
Design work into 2011
Start fabricating late 2011 and into 2012
Install late 2012
Read for beam 2013

## Slide 13: Who is working on this?
Cryostat and cryo systems - FNAL + BNL
  J. Kilmer, B. Sanders, G. Morgan and others
Wire chamber design – BNL + Yale
Photodetector - MIT
Main electronics conceptual design – BNL
Detector feed-throughs – various, needs help
Electronics Infrastructure - help
Integration - FNAL + collaboration – HELP
DAQ – HELP
Enclosure modifications - FESS
Installation activities – FNAL technicians