## Slide 1
ISIS Muon
Facilities
Sue Kilcoyne
University of Huddersfield
http://www.isis.stfc.ac.uk/groups/muons/

## Slide 2
Introduction to ISIS
Project X Muon Spin Rotation Forum
October 2012

## Slide 3
A World Centre for Condensed Matter Science with Neutrons and Muons
Project X Muon Spin Rotation Forum
October 2012

## Slide 4
ISIS
Broad academic base
25 Instruments (soon to be 33+)
700 Experiments per year
3000 Instrument-days per year
500 Publications per year
2000-strong user base

## Slide 5
Superconductivity
Magnetism
Engineering
Chemistry
Surfaces & Interfaces
Bio-molecular Science
Hydrogen Storage
Archeometry
Earth / Planetary Science
Environmental Science
Science at ISIS
Project X Muon Spin Rotation Forum
October 2012

## Slide 6
1985: Construction – EC, UK, Italy, France, Germany, Sweden
1987: First muons – single beamline (MuSR)
1991: Construction of beamline upgrade – EC-funded
1993: 3 beamlines operational (MuSR, EMU, DEVA)
1996 – 2008: €3.9M in EC Access funding
1998-2000: DEVA RF-spectrometer built (EPSRC)
2005-2009: HiFi constructed (£2.1M)
Project X Muon Spin Rotation Forum
October 2012
Muons at ISIS
A Brief History of ISIS Muons
2012: 25 years of muons at ISIS

## Slide 7
In a recent ISIS proposal rounds there were applications from
19 different countries (UK + 11 European + 7 outside Europe)
67 separate research groups
738 days applied for: 417 available (1.8 oversubscription)
~35% of applicants are regular neutron users
Usage of ISIS Muons
Project X Muon Spin Rotation Forum
October 2012

## Slide 8
Muons as passive probes in superconductivity, magnetism, molecular dynamics, charge transport.
Muons as active probes: proton analogues in semiconductors, proton conductors, light particle diffusion, etc.
Usage of ISIS Muons
Project X Muon Spin Rotation Forum
October 2012

## Slide 9
Average of 50 publications per year over the past 8 years
Hydrogen studies
Chemistry and molecular studies
Charge transport and diffusion
Organic magnetism and super-conductivity
Inorganic magnetism and super-conductivity
Usage of ISIS Muons
Project X Muon Spin Rotation Forum
October 2012

## Slide 10
Muons at ISIS
Project X Muon Spin Rotation Forum
October 2012
Two facilities – EC Muon Facility and RIKEN Muon Facility

## Slide 11
2 proton pulses, at 50 Hz
2.5x1013 protons per pulse ~200µA
800 MeV (0.84c)
Proton synchrotron
Project X Muon Spin Rotation Forum
October 2012

## Slide 12
Extracted beam pulses going to targets
~80ns wide pulses
Separated by ~300ns peak-to-peak
Last turns of beam in synchrotron
Synchrotron kicker fires
Proton pulse structure
Project X Muon Spin Rotation Forum
October 2012

## Slide 13
Muon production
Graphite target is 20m upstream of neutron target
10mm target at 900K and takes up to 5% of the protons
Pions decay to polarised muons
Project X Muon Spin Rotation Forum
October 2012
Result: a fully spin-polarised muon beam

## Slide 14
Project X Muon Spin Rotation Forum
October 2012
Ladder assembly of 3 graphite targets for muon production

## Slide 15
Project X Muon Spin Rotation Forum
October 2012

## Slide 16
Muons at ISIS
Project X Muon Spin Rotation Forum
October 2012

## Slide 17
HiFi
EC Muon Facility
Project X Muon Spin Rotation Forum
October 2012
Beamline tuned for muons of energy ~4 MeV ( ~29 MeV/c momentum):
‘surface’ muons

## Slide 18
Project X Muon Spin Rotation Forum
October 2012
First magnet excludes neutral particles and those of the wrong charge
Also acts as a momentum filter
Dipole magnets
Second magnet bends the beam

## Slide 19
Beamline tuned for muons of energy ~4 MeV ( ~29 MeV/c momentum):
‘surface’ muons
EC Muon Facility
Project X Muon Spin Rotation Forum
October 2012
HiFi

## Slide 20
Project X Muon Spin Rotation Forum
October 2012
Quadrupole magnets
Quadrupole magnets focus in one direction and defocus in the other.
Usually placed in the beamline in 2s or 3s to get best results
Also have quadrupole magnets at end of beamline to focus muon beam just before hitting sample

## Slide 21
HiFi
EC Muon Facility
Project X Muon Spin Rotation Forum
October 2012
Beamline tuned for muons of energy ~4 MeV ( ~29 MeV/c momentum):
‘surface’ muons

## Slide 22
Project X Muon Spin Rotation Forum
October 2012
The Separator

## Slide 23
HiFi
EC Muon Facility
Project X Muon Spin Rotation Forum
October 2012
Beamline tuned for muons of energy ~4 MeV ( ~29 MeV/c momentum):
‘surface’ muons

## Slide 24
received pulses
MuSR
EMU
kicker voltage
Each instruments receives a single, 80ns-wide pulse at 50Hz.
Central beamline (MuSR) has 2x muon flux of side beamlines
E=32.5kV
4 MeV µ+
The Muon kicker
Project X Muon Spin Rotation Forum
October 2012
The Kicker

## Slide 25
Project X Muon Spin Rotation Forum
October 2012
EMU
MuSR
HiFi
Bending magnets
Kicker
EC Muon facility beamline

## Slide 26
96-detectors
optimised for ZF and LF
0 - 0.45 T
50mK - 1500K
Spot 10 x 15mm
data rates ~25 MeV/hr
common vacuum
‘fly-past’ for small samples
SE kit prepared on-beam
EMU
Project X Muon Spin Rotation Forum
October 2012
Magnetism, superconductivity, molecular materials, semiconductors, metals, ionic and polymeric conductors, light particle diffusion, liquids and gases.

## Slide 27
64 detector elements
data rates ~50 MeV/hr
no common vacuum
no ‘fly-past’
SE kit prepared off-beam
30 mK – 1000 K
0 G – 2500 G LF
0 G – 600 G TF
MuSR
Project X Muon Spin Rotation Forum
October 2012
Mainly used to study magnetic and superconducting materials. Also used to study charge transport, proton diffusion, and the chemistry of muon radicals.

## Slide 28
64 detector elements
common vacuum
‘fly-past’
SE kit prepared off-beam
30 mK–1500 K (DR, CCR, furnace)
0 G – 5 T LF
0 G – 100 G TF
high field homogeneity
auxiliary sweep coils for ALC
HiFi
Project X Muon Spin Rotation Forum
October 2012
REVIEW OF SCIENTIFIC INSTRUMENTS 82, 073904 (2011)
Particularly suited to time-differential muon measurements at high fields, including
measurements which exploit level-crossing or radiofrequency resonance techniques. Liquids.

## Slide 29
Project X Muon Spin Rotation Forum
October 2012
Control of the Competition between a Magnetic Phase and a Superconducting Phase in Cobalt-Doped and Nickel-Doped NaFeAs Using Electron Count Phys Rev Lett 104 (2010) 057007
Ground State of the Easy-Axis Rare-Earth Kagome Langasite Pr3Ga5SiO14 Phys Rev Lett 104 (2010) 057202
Electric-Field-Enhanced Neutralization of Deep Centers in GaAs Phys Rev Lett 103 (2009) 216601
Tuning the Interlayer Spacing of High-Tc Bi-Based Superconductors by Intercalation: Measuring the Penetration Depth and the Two-Dimensional Superfluid Density Phys Rev Lett 102 (2009) 087002
Coexistence of static magnetism and superconductivity in SmFeAsO1-xFx as revealed by muon spin rotation Nature Materials (2009) 8 (2009) 310
Evidence for Time-Reversal Symmetry Breaking in the Noncentrosymmetric Superconductor LaNiC2 Phys Rev Lett 102 (2009) 117007

## Slide 30
Muons at ISIS
Project X Muon Spin Rotation Forum
October 2012

## Slide 31
1990: First agreement
1991: Construction began
1994: First muons
1995: Cond. matt. expts.
1996: mCF expts.
2000: Second agreement
2001: Port 4 added
RIKEN-RAL Muons
Project X Muon Spin Rotation Forum
October 2012

## Slide 32
PION
MUON
MUON
MUON
MUON
PROTON

## Slide 33
RIKEN-RAL Muons
Decay (positive and negative) muon beams + surface muon beam
Muon momentum range : 20 – 120 MeV/c
Muon beam intensity (200A proton beam and 10 mm thick production target)
Decay positive muon: 4 x 105 /sec （60 MeV/c）
Decay negative muon: 7 x 104 /sec （60 MeV/c）
Surface muon : 1.5 x 106 /sec （27 MeV/c）
Double pulsed muon beam is separated into two single muon pulses
(p < 65MeV/c, pulsed magnetic kicker + septum magnet)
Two muon experiments can be performed independently
Project X Muon Spin Rotation Forum
October 2012

## Slide 34
Port 1: µCF
d-t fusion catalyzed by negative muons
Project X Muon Spin Rotation Forum
October 2012

## Slide 35
Port 2: ARGUS
192 detector elements
~70 MeV/hr (double pulse)
no common vacuum
no ‘fly-past’
SE kit prepared off-beam
30 mK – 800 K
0 G – 4000 G LF
0 G – 150 G TF
Pressure experiments up to 0.7 GPa
Project X Muon Spin Rotation Forum
October 2012
magnetism, superconductivity, charge transport, molecular and polymeric materials and semiconductors.

## Slide 36
Port 3: Low-energy muon production
source: E. Morenzoni, PSI
Project X Muon Spin Rotation Forum
October 2012
laser ionisation of muonium
good beam spot size improved timing resolution (7.5ns pulse)
20 m/s at present good energy resolution

## Slide 37
Charge distribution of short-lived nuclei
Solid hydrogen film to stop both µ and A*
µH + Az*  µAz* + H
Port 4: Muonic atom spectroscopy
Project X Muon Spin Rotation Forum
October 2012

## Slide 38
Pros
Low intrinsic background – measurements to long times
Weak relaxations, slow precession
No fundamental data rate limit
Pulsed environments are a speciality:
reduce sample heating
allow dynamics
multi-pulse stimuli
light, laser, E-field, B- field, RF
Cons
Short time (<0.2 mS) structure lost
Not good at measurements > 10MHz or relaxations >0.1ms-1
Requires detector arrays with many elements
50 Hz is not time-efficient (we use 32ms every 20 ms)
Pulsed Muons – Pros and Cons
Muons arrive in 80ns-wide pulses: affects timing measurement but many muons
Project X Muon Spin Rotation Forum
October 2012

## Slide 39
LiVGe2O6
Blundell et al., Phys. Rev. B 67 (2003) 224411
Example - ISIS / PSI
ISIS
PSI
Project X Muon Spin Rotation Forum
October 2012

## Slide 40
Overcoming Pulsed Source Limitations
1. Pulse slicing
‘normal’ frequency response
‘reduced pulse’ frequency response
kicker chops within a pulse
Project X Muon Spin Rotation Forum
October 2012

## Slide 41
Overcoming Pulsed Source Limitations
2. Radio-frequency
muons accumulate during RF pulse
spins flipped through 90o
subsequent free muon precession
High frequency measurements at a pulsed muon source: beating the pulse width!
AD Hillier et al., Physica B 326 (2003) 275
type-II superconductor YNi2B2C
13.6 MHz precession (1034 G)
below Tc
above Tc
Project X Muon Spin Rotation Forum
October 2012

## Slide 42
Project X Muon Spin Rotation Forum
October 2012

## Slide 43
Project X Muon Spin Rotation Forum
October 2012
http://www.isis.stfc.ac.uk/groups/muons/
Muon beam profile on HiFi with increasing field: http://vimeo.com/47658674
http://www.isis.stfc.ac.uk/science/a-video-tour-of-the-isis-facility4469.html
http://www.isis.stfc.ac.uk/learning/video/backstage-science-muons12258.html
Links and Videos