## Slide 1: Jayakar Thangaraj Fermilab Accelerator Advisory Committee November 7-9, 2011
PROTOPLASMA: Proton-driven wakefield experiment at Fermilab

## Slide 2: Plasmas : a role in future accelerators ?
Linear colliders are in the TeV era.
Increasing cost of next generation accelerators
Conventional RF technology (~ 100 MV/m). Plasmas can support large electric fields (> GV/m).
Can we use plasmas to make accelerators compact?

## Slide 3
Physical mechanism
Space charge of the drive beam sets up a plasma wave
Drive beam could be (a) Laser beam (b) Electron beam

## Slide 4
Electron and Laser driven acceleration
Laser-driven and electron beam-driven
acceleration have shown great progress
(new facilities such as FACET, BELLA )
Nature v 445 (2007) I.Blumenfeld et al.,
(1 GeV in 3.3 cm)
(42 GeV in 85 cm)
Question: Can we use these schemes
for a multi-TeV collider?
Challenge: We will need many stages
Possible solution : Use a proton beam to drive plasma
A.Caldwell et. al Nature 2009, C. Joshi

## Slide 5
Plasma act as an energy transformer.
“Conventional” accelerators produce TeV proton beam. kJ’s of energy.
Key Idea
      Use an existing high energy proton beam to drive a plasma wake and accelerate an electron beam
Opportunity
      We could accelerate electrons to TeV in a single stage. This will be a new research frontier.
      Fermilab would be well-suited for such R&D. CERN has also proposed an experiment in their facility.
Why use a proton beam?

## Slide 6
Challenges on using a proton beam as a driver
Key challenge
    Proton bunches are the order of 10s of cm NOT sub-mm.
    Compressing high energy proton beam is expensive
Solution
    Use “self-modulation” of a long proton bunch in a plasma to generate short bunches
N.Kumar, A. Pukhov, K. Lotov PRL 2010

## Slide 7
People involved in Protoplasma
Fermilab:
    Tevatron: D. Still, J. Annala , A. Valishev
    Main Injector: I. Kourbanis, D. Morris, T. Johnson
    APC : V. Shiltsev, P. Spentzouris
    External Beamline: A. Soha, T. Kobilarcik, R. Coleman
  U
  W. Mori, C. Joshi, W. An

## Slide 8
Our goal and current status
Simulation status
      We are currently exploring various beam and plasma parameters to look for self modulation within 3 m.
      Current simulation effort is pursued by W. An under
      W. Mori at UCLA (Some discussions: Spentzouris talk)
Experimental design status
      We are considering the Tevatron option (120 GeV) or the external beam line option (120 GeV).
      A lower energy option (8 GeV) is being pursued as well.
Our goal : To demonstrate 1 GeV electron acceleration in 3 m

## Slide 9
Experimental schematic

## Slide 10
The Tevatron option
F0 to A49
CDF collision Hall
Portion of B section
      Inject 120 GeV protons at 1e11 protons per bunch from MI
      to Tevatron
      Beam is single pass from F11 to
      B17
      Beam will interact with plasma located in the CDF collision hall.
      There will be detector and beam dump at ~B17

## Slide 11
If Tevatron (120 GeV)…
Cryogenics
      Refrigerator work 40 weeks (~ $ 500 K)
      We have to run F, A, B sector cryogenically
      Half the current running cost of TeV: $ 4 million/yr
People 2 post-docs
Safety $30 K
Plasma cell $500K
Mechanical and Electrical
      48 weeks 10 hours a day 5-6 man crew
      < $500K (certify TeV)
Power supply (assuming no change the ring , HOPS)
      No significant cost M&S ($100 K)
      6 people (3 techs and 3 engineers) 2-4 weeks
Cost of moving CDF Detector
Possible sharing with kaon experiment (60 GeV)

## Slide 12
If External Beamline (120 GeV) …
Time to install ~ 6 months – 1 year long
Available space is about 200 m long
Magnets ~ $4 million
Power supply ~ $2 million
Cables, dipoles, engineering FTE ~ $400 K
Plasma cell ~ $500 K

## Slide 13
Plan
 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017
Approval |  |  |  |  |  |  | 
Experiment design Simulations Plasma cell R&D |  |  |  |  |  |  | 
Beamline restructuring |  |  |  |  |  |  | 
Measurements of proton beam modulation |  |  |  |  |  |  | 
Seeding |  |  |  |  |  |  | 
Electron injection |  |  |  |  |  |  | 
First demonstration of proton wakefield acceleration |  |  |  |  |  |  | 

## Slide 14
In summary for the protoplasma experiment:
Next steps, continue exploring the parameter space through simulation.
Continue search for experimental location: TeV or the external beamline or 8 GeV option
Our near term experimental goal is to demonstrate self-modulation of the proton bunch
Enable US leadership on proton-driven wakefield class of experiments
Fermilab (proton expertise) and UCLA ( plasma R&D leaders) have already started to work on optimal beam/plasma parameters design.