## Slide 1: Cisco 40GE/100GE Strategy and Direction
Chris Hocker
Consulting Systems Engineer
chocker@cisco.com

## Slide 2: Discussion Items
40GE/100GE Platform Investments
  Transport (DWDM and Routers)
  15454 MSTP Transponder/Muxponder
  CRS, ASR9K
  IP over DWDM
  Data Center - N2K, N3K, N5500, N6K, N7000/N7700
  Campus - Cat6K
CPAK Optics
Breakout Interfaces

## Slide 3: Cisco 100G Coherent DWDM Module
Cisco
100G Coherent
DWDM Module
ONS 15454
100G Transponder / Trunk
CRS-3
100G IP-over-DWDM PLIM
animated

## Slide 4: Optics – What Is CPAK?
New Cisco 100G transceiver form-factor using Silicon Photonics technology
IEEE standards compliant
High density
Low power consumption
Significantly smaller than current 100G CFPs
100G CPAKs available in 2013 timeframe:
Cisco 100G CPAK Transceiver
SR10 CPAK | LR4 CPAK
100m (OM3) or 150m (OM4) MMF ribbon cable MPO-24 connector Can also run as 10X10G SR or 2X40G SR4 | 10km SMF duplex cable SC connector

## Slide 5: Nexus 7700 F3 40G and 100G Modules
24-port 40G QSFP+ module / 12-port 100G CPAK module
Based on F3 ASIC technology
Wire-rate L2/L3 IPv4/IPv6
  960G / 1.2T per slot
  1.4 / 1.8 Bpps/slot
  ~6µsec latency cross-fabric
Buffering:
  6MB VOQ per 40G port
  12MB VOQ per 100G port
  User-configurable buffer sharing
Breakout cable support
Multi-protocol – Classic Ethernet, FabricPath, DCB/FCoE
MPLS, OTV, LISP, GRE, VXLAN
64K FIB TCAM/64K adjacency table
64K MAC address table
Nexus 2000 (FEX) support
2HCY13
F3 100G N77-F312CK-26
*Not all listed features committed for FCS of F3.

## Slide 6: Nexus 6004
Fixed ports
Expansion Modules
12 x 40 Gig
Per “module”
4 RU
N6K-C6004-M12Q
N6K-C6004-96Q
Notes: Q stands for QSFP
T stands for 10GbaseT
P stands for SFP+

## Slide 7: Multimode Fiber Cabling Options for 40GBASE-SR4
40G-SR4
40G-SR4
40G-SR4
10G-SR
10G-SR
10G-SR
10G-SR
MPO-12  MPO-12
MPO-12  LC Breakout
Could also be used with
Existing cabling infrastructure (*)